## Slide 1: Lecture 5
Topics
  Canonical or Standard Forms of Functions
    SOP (Sum of Products) form
    POS (Product of Sums) form
    Relationship Between MinTerms and MaxTerms
    Converting Between Compact Forms of Functions
  Minimizing (Reducing) Functions
    Karnaugh Maps (K-maps)
    Product term sharing

## Slide 2: Boolean Equations

## Slide 3: Obtaining a Boolean Equation
In Ecotopia it’s generally illegal to use a car pool lane during weekdays if the car doesn’t have at least two occupants. However, hybrid vehicles can use the lanes any time regardless of the number of occupants. SUVs (even with two or more occupants) are never allowed to use the car pool lanes (unless they are also hybrids).
Write a Boolean expression in SOP form for F(W, O, S, H) which is 1 if the car is permitted to use the car pool lane today. W is 1 if today is a weekday. O is 1 if there are two or more occupants, S is 1 if the vehicle is an SUV, H is 1 if the vehicle is a hybrid.
W O S H F
----------
0 0 0 0 1
0 0 0 1 1
0 0 1 0 0
0 0 1 1 1
0 1 0 0 1
0 1 0 1 1
0 1 1 0 0
0 1 1 1 1
1 0 0 0 0
1 0 0 1 1
1 0 1 0 0
1 0 1 1 1
1 1 0 0 1
1 1 0 1 1
1 1 1 0 0
1 1 1 1 1
ECOTOPIA EXAMPLE

## Slide 4: Deriving Boolean Equations
A truth table is a complete, unambiguous definition of a Boolean function…
But how do we get a Boolean expression from a truth table?
  SOP or POS
X Y Z F
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 0
1 1 0 1
1 1 1 0
F = X×Y×Z + X×Y×Z + X×Y×Z

## Slide 5: Obtaining SOP Forms of Functions
F(A,B) = F(0,0)×A×B + F(0,1)×A×B + F(1,0)×A×B + F(1,1)×A×B
= 0×A×B + 1×A×B + 1×A×B + 1×A×B
= 0 + A×B + A×B + A×B
= A×B + A×B + A×B
OR truth table
A B F(A,B)
0 0 0 = F(0,0)
0 1 1 = F(0,1)
1 0 1 = F(1,0)
1 1 1 = F(1,1)
Reduced Form
Canonical or Standard
SOP Form
Standard Product Term
(Minterm)
A + B
Notes: Comes from Claude Shannon’s MS work. Simplified way of looking at it: just list the “terms” of AB (and complements) which result in function value of 1.

## Slide 6: Minterms and Maxterms
Notes: Majority Function

## Slide 7: Minterms
Notes: Majority Function

## Slide 8: Compact Minterm Form
F(A,B) = F(0,0)×A×B + F(0,1)×A×B + F(1,0)×A×B + F(1,1)×A×B
= S3i=0 (Fi × mi)
= 0 × m0 + 1 × m1 + 1 × m2 + 1 × m3
= m1 + m2 + m3
= S m(1,2,3)
= S (1,2,3)
OR truth table
A B F(A,B)
0 0 0 = F(0,0)
0 1 1 = F(0,1)
1 0 1 = F(1,0)
1 1 1 = F(1,1)
Notes: Comes from Claude Shannon’s MS work. Simplified way of looking at it: just list the “terms” of AB (and complements) which result in function value of 1.

## Slide 9: Minterms
S (3,5,6,7)

## Slide 10: Generalized Compact Minterm Form
F(X1, X2,… Xn) = S (minterms for 1s of the function)
F(X1, X2,… Xn) = S (minterms for 0s of the function)

## Slide 11: Obtaining POS Forms of Functions
F(A,B) = (F(0,0) + A + B) × (F(0,1) + A + B) × (F(1,0) + A + B) × (F(1,1) + A + B)
= (0 + A + B) × (0 + A + B) × (0 + A + B) × (1 + A +B)
= (A+B) × (A+B) × (A+B) × (1)
= (A+B) × (A+B) × (A+B)
AND truth table
A B F(A,B)
0 0 0 = F(0,0)
0 1 0 = F(0,1)
1 0 0 = F(1,0)
1 1 1 = F(1,1)
Standard Sum Term
(Maxterm)
Canonical or Standard
POS Form
Reduced Form
A × B
Notes: Comes from Claude Shannon’s MS work. Simplified way of looking at it: just list the “terms” of AB (and complements) which result in function value of 1.

## Slide 12: Maxterms
Notes: Majority Function

## Slide 13: Compact Maxterm Form
F(A,B) = (F(0,0) + A + B) × (F(0,1) + A + B) × (F(1,0) + A + B) × (F(1,1) + A + B)
= P3i=0 (Fi + Mi)
= (0 + M0) × (0 + M1) × (0 + M2) × (1 + M3)
= M0 × M1 × M2
= P M(0,1,2)
= P (0,1,2)
AND truth table
A B F(A,B)
0 0 0 = F(0,0)
0 1 0 = F(0,1)
1 0 0 = F(1,0)
1 1 1 = F(1,1)
Notes: Comes from Claude Shannon’s MS work. Simplified way of looking at it: just list the “terms” of AB (and complements) which result in function value of 1.

## Slide 14: Maxterms
P (0,1,2,4)
Notes: Majority Function

## Slide 15: Generalized Compact Maxterm Form
F(X1, X2,… Xn) = P (maxterms for 0s of the function)
F(X1, X2,… Xn) = P (maxterms for 1s of the function)

## Slide 16: Relationship Between Minterms and Maxterms
mi = Mi, Mi = mi
S = P, P = S

## Slide 17
An example: Given the accompanying truth table, write the compact minterm form for F for its 1s and 0s. Write the standard SOP form for each.
X Y Z F
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 0
1 1 0 1
1 1 1 0
F = S(3,4,6)
Compact minterm form 1s:
Compact minterm form 0s:
Corresponding SOP form:
Corresponding SOP form:
F = X×Y×Z + X×Y×Z + X×Y×Z
F = S(0,1,2,5,7)
F = X×Y×Z + X×Y×Z + X×Y×Z + X×Y×Z + X×Y×Z
This is example problem 15, page 85. Solution on page 107.

## Slide 18
An example: Given the accompanying truth table, write the compact maxterm form for F for its 1s and 0s. Write the standard POS form for each.
X Y Z F
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 0
1 1 0 1
1 1 1 0
Compact maxterm form 1s:
Compact maxterm form 0s:
Corresponding POS form:
Corresponding POS form:
F = P(0,1,2,5,7)
F = P(3,4,6)
F = (X+Y+Z) × (X+Y+Z) × (X+Y+Z)
F = (X+Y+Z) × (X+Y+Z) × (X+Y+Z) × (X+Y+Z) × (X+Y+Z)
This uses the same truthtable as the preceding problem but asks for maxterms

## Slide 19: Function Minimization: Reduce Number of Literals and Terms
Simplify for Comprehension
Reduce Number of Components
Reduce Amount of Wiring/Routing
Smaller Circuit/Board Area
Lower Cost
Higher Reliability
Notes: Now we can derive an equation for a Boolean function from a truth table. How about minimizing it?

## Slide 20: Function Minimization: Reduce Number of Literals and Terms
Apply Boolean Algebra
Employ Computer Algorithm
  Quine-McCluskey tabular algorithm
  Boozer
  McBoole
  Espresso and Espresso/Exact (CAD packages)
Systematic Algebraic Reduction (SAR)
Karnaugh Maps (K-Maps)

## Slide 21: Karnaugh Maps

## Slide 22: Karnaugh (K) Maps
A graphical representation of Boolean function
Easy to perform functional reduction
Relies on adjacency (Gray code) of minterms
  Adjacent (horizontal/vertical & wrap around) cells differ in only one variable (complement)
Number form and Variable form

## Slide 23: K-Maps
2 Variable K-Map (Number Form)
Gray code!
Minterm numbers

## Slide 24: K-Maps
3 Variable K-Map (Number Form)
Gray code!
Minterm numbers

## Slide 25: K-Maps
4 Variable K-Map (Number Form)
Gray code!
Minterm numbers

## Slide 26: K-Maps
2 Variable K-Map (Variable Form)
May be more useful if plotting partially reduced functions
Careful! Preserve Gray code!

## Slide 27: K-Maps
3 Variable K-Map (Variable Form)

## Slide 28: K-Maps
4 Variable K-Map (Variable Form)

## Slide 29: My Preference…
W
W
X
Z
Y
Y

## Slide 30: Plotting Functions in K-Maps
Plot the function F1(X,Y,Z) = S(2,5,6,7)
X Y Z F1
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 0
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 1
Notes: May be given function in truth table, compact minterm/maxterm, or partially reduced (equation) form…
We’ll look at 1st two first

## Slide 31: Plotting Functions in K-Maps
Plot the function F2(A,B,C,D) = S(6,7,8,14,15)
Plot 0s!

## Slide 32: Don’t Care Outputs

## Slide 33: Don’t Care Outputs
Output of Function Doesn’t Matter
  Typically impossible input condition
  Use X instead of 0 or 1
BCD
A B C D Prime
0 0 0 0 0
0 0 0 1 1
0 0 1 0 1
0 0 1 1 1
0 1 0 0 0
0 1 0 1 1
0 1 1 0 0
0 1 1 1 1
1 0 0 0 0
1 0 0 1 0
1 0 1 0 X
1 0 1 1 X
1 1 0 0 X
1 1 0 1 X
1 1 1 0 X
1 1 1 1 X
0
1
2
3
4
5
6
7
8
9
.
.
.
.
.
.

## Slide 34: Don’t Care Outputs Compact Minterm and Maxterm Form
F3(A,B,C) = S(2,6) + Smd(3,5,7)
F3(A,B,C) = S(0,1,4) + Smd(3,5,7)
F3(A,B,C) = P(0,1,4) × PMd(3,5,7)
F3(A,B,C) = P(2,6) × PMd(3,5,7)
A B C F3
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 X
1 0 0 0
1 0 1 X
1 1 0 1
1 1 1 X

## Slide 35: Plotting K-Maps with Xs
A B C F3
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 X
1 0 0 0
1 0 1 X
1 1 0 1
1 1 1 X
F3(A,B,C) = S(2,6) + Smd(3,5,7)

## Slide 36: Plotting K-Maps from functions in partially reduced form
F4(A,B,C,D) = A×B×C×D + B×C×D + A×B + C
p1
p2
p3
p4
Notes: Need to explain. Think of missing variables as input don’t cares (X) and look for row/col where fits (e.g. C = XXCX and we care only about squares where C is 1 regardless of other variables). All variables present in term: single cell; one variable missing: 1x2, two variables missing: 2x4, etc…

## Slide 37: Plotting K-Maps from functions in partially reduced form
F4(A,B,C,D) = A×B×C×D + A×B×C×D + A×B×C
r1
r2
r3
Notes: Need to explain. Think of missing variables as input don’t cares (X) and look for row/col where fits (e.g. C = XXCX and we care only about squares where C is 1 regardless of other variables).

## Slide 38: K-Maps for functions of 5 variables
F(V,W,X,Y,Z)
m0 through m15
m16 through m31
Notes: Don’t usually go beyond 4 or 5 variables because there are good S/W packages to do this.
Split map into two (think of them as stacked). Still maintain Gray code.

## Slide 39: K-Maps for functions of 5 variables
F(V,W,X,Y,Z) = S(3,7,9,11,12,15,16,19,23,24,27,28,31) + Smd(4,18,20,26,30)
Notes: Don’t usually go beyond 4 or 5 variables because there are good S/W packages to do this.
Split map into two (think of them as stacked). Still maintain Gray code.

## Slide 40: Using K-Maps to Reduce Functions

## Slide 41: Using K-Maps to Reduce Functions
Assume you’ve plotted the K-map for F(X,Y,Z) as follows:

## Slide 42: Using K-Maps to Reduce Functions
You want to obtain a reduced expression for F(X,Y,Z) in SOP form
Notes: Smallest expressions  largest cube sizes

## Slide 43: Using K-Maps to Reduce Functions
Need to “cover” 1s
Fewest product terms
Simplest expressions
  (fewest variables)
You want to obtain a reduced expression for F(X,Y,Z) in SOP form
Notes: Smallest expressions  largest cube sizes

## Slide 44: Using K-Maps to Reduce Functions
Circle all isolated 0-cubes
Circle all 1-cubes not completely contained in a larger cube
Continue for 2, 3, 4-cubes
Write the product terms (prime implicants) and OR them together
Write the expression for each product term

## Slide 45: Using K-Maps to Reduce Functions
F(X,Y,Z) = p1 + p2 + p3 = X×Z + X×Z + Y
Notes: Smallest expressions  largest cube sizes

## Slide 46: Using K-Maps to Reduce Functions
F(X,Y,Z) = r1 + r2 = X×Y×Z + X×Y×Z
Notes: Smallest expressions  largest cube sizes

## Slide 47: K-Maps (Some Terminology)
Implicant: Product term of a function
Prime Implicant: Product term for a cube which is not completely contained in another cube
Essential Prime Implicant: Product term which provides the only covering for a given minterm and must always be used in the set of product term
Optional Prime Implicant: Product term which provides an alternative covering for a given minterm and may be used in the set of product terms
Redundant (Non-Essential) Prime Implicant: Product term for a cube which is completely contained in another cube (correct, but won’t lead to a minimum function)

## Slide 48: K-Map with only essential prime implicants

## Slide 49: K-Map with no essential prime implicants

## Slide 50: K-Map with no essential prime implicants

## Slide 51: K-Map with no essential prime implicants: alternative!

## Slide 52: Covering Order is Essential

## Slide 53: Using K-Maps to Reduce Functions
Given the following K-map, which minimum SOP form of the function
has the smallest literal count (the one for the 1s or the 0s)?
F(W,X,Y,Z) =
F(W,X,Y,Z) =
Notes: Smallest expressions  largest cube sizes

## Slide 54: Using K-Maps to Reduce Functions
F(W,X,Y,Z) = p1 + p2 + p3 = X×Z + W×Z + W×Y
lc = 6

## Slide 55: Using K-Maps to Reduce Functions
F(W,X,Y,Z) = r1 + r2 + r3 = W×X×Y + W×Z + Y×Z
lc = 7

## Slide 56: Using K-Maps to Reduce Functions
Given the following K-map, which minimum SOP form of the function
has the smallest literal count (the one for the 1s or the 0s)?
lc = 6
lc = 7
F(W,X,Y,Z) = r1 + r2 + r3 = W×X×Y + W×Z + Y×Z
F(W,X,Y,Z) = p1 + p2 + p3 = X×Z + W×Z + W×Y
Notes: Smallest expressions  largest cube sizes

## Slide 57: Using K-Maps to Reduce Functions
Given the following K-map, which minimum SOP form of the function
has the smallest literal count (the one for the 1s or the 0s)?
F(W,X,Y,Z) =
F(W,X,Y,Z) =
Only use don’t cares to allow larger cube sizes to be covered
Notes: Smallest expressions  largest cube sizes

## Slide 58: Using K-Maps to Reduce Functions
Only use don’t cares to allow larger cube sizes to be covered
F(W,X,Y,Z) = p1+p2+p3+p4 = X×Y×Z + W×X×Y + W×Z + Y×Z
lc = 10
Notes: Smallest expressions  largest cube sizes

## Slide 59: Using K-Maps to Reduce Functions
Only use don’t cares to allow larger cube sizes to be covered
F(W,X,Y,Z) = r1 + r2 + r3 = W×Y×Z+ X×Z + W×Y
lc = 7
Notes: Smallest expressions  largest cube sizes

## Slide 60: K-Maps for functions of 5 variables
F(V,W,X,Y,Z) = S(3,7,9,11,12,15,16,19,23,24,27,28,31) + Smd(4,18,20,26,30)
Notes: Don’t usually go beyond 4 or 5 variables because there are good S/W packages to do this.
Split map into two (think of them as stacked). Still maintain Gray code.

## Slide 61: Ecotopia Revisited

## Slide 62: Circuits with Multiple Outputs Product Term Sharing
x1
x2
x3
x4
f1
f2

## Slide 63: Product Term Sharing
May Result in K-Maps Different from Optimizing Separate Functions

## Slide 64: K-Maps: Caveats!
Empty K-Map must be constructed correctly
  Gray Code: Adjacent cells differ in only one variable
K-Map must be plotted correctly
  Minterms from truth table or compact form
  Minterms from partially reduced expressions
K-Map must be circled correctly
  Start with smallest cubes first!
  Remember that K-Maps “wrap” at edges
Use 1s for F, 0s for F

## Slide 65: Sources
Prof. Mark G. Faust
John Wakerly