## Slide 1: Lecture 7
Topics
  The Real World of IC Logic
    IC Packages
    IC Logic Families
    Key IC Parameters
    CMOS IC Datasheets
    Detailed Schematics using ICs

## Slide 2: Taxonomies of ICs

## Slide 3: Taxonomies of ICs
Density/Level of Integration
  SSI (Small Scale Integration) ~10 gates/IC
  MSI (Medium Scale Integration) 102 gates/IC
  LSI (Large Scale Integration) 103 gates/IC
  VLSI (Very Large Scale Integration) 107-108 gates/IC

## Slide 4: Taxonomies of ICs
Design Methodology
  Standard Components (SSI/MSI/LSI)
    Off-the-shelf Components
    Basic Universal Building Blocks (AND, OR, NAND, NOR…)
  Application-Specific Standard Parts (ASSP)
    Target Specific Application Area, but not Customer
    e.g. Printer Controller, USB Interface IC, HDD I/F
  Application-Specific IC (ASIC)
    Custom Design of IC Targeting Specific Market
    Full-custom, standard cell, gate-arrays
    e.g. ATI 3D Graphics Engine
  Programmable Logic Devices (PLD)
    Can be used to implement wide variety designs
    e.g. FPGA (Field-Programmable Gate Arrays)

## Slide 5: Taxonomies of ICs
Technology
  Bipolar
    TTL (Transistor-Transistor Logic)
    ECL (Emitter Coupled Logic)
    others
  CMOS
Advantages
  Inexpensive
  High level of integration
  High speed
  Very low quiescent (static) power consumption
  “Rail-to-Rail” outputs
Disadvantages
  Susceptible to electrostatic discharge (ESD) damage
  Susceptible to “latch-up”
Has become dominant logic technology

## Slide 6: Taxonomies of ICs
Families
  TTL
    STD TTL: Standard TTL
    LS TTL: Low Power Schottky TTL
    AS TTL: Advanced Schottky TTL
    ALS TTL: Advanced Low Power Schottky TTL
    F/FAST TTL: Fairchild Advanced Schottky TTL
  CMOS
    AC: Advanced CMOS
    ACT: Advanced CMOS (TTL Compatible)
    HC: High Speed CMOS
    HCT: High Speed CMOS (TTL Compatible)

## Slide 7: Integrated Circuit Costs
Die

## Slide 8: AMD Opteron

## Slide 9: Wafer Probing

## Slide 10: DIP (Dual In-Line Package) Details

## Slide 11: Additional IC Package Types
dual-in-line
flat
surface-mounting
Plastic leaded chip carrier
Pin grid array

## Slide 12: Surface Mount (SMT) PCB Assembly
Solder paste stencil
SMT placement system
Component feeder

## Slide 13
SMT components on reel
SMT components in inventory
Surface Mount (SMT) Components

## Slide 14
Reflow oven
Surface Mount (SMT) Assembly

## Slide 15: Key IC Parameters

## Slide 16: Key IC Parameters
Vcc (Power Supply Voltage)
Logic Levels
  VIH, VIL, VOH, VOL
  Noise Margin
Propagation Delay (tpd)
Rise/Fall Times (Tr, Tf)
Power Dissipation
Fan-Out

## Slide 17: Vcc – Power Supply Voltage
Common across a logic family (e.g. 5V for all HC parts)
Vcc and Gnd commonly called “power supply rails”
  Sometimes Vdd and Vss for CMOS devices
+5V

## Slide 18: Logic Levels

## Slide 19: Logic Levels
Common across a logic family (e.g. all HC parts)
VIH, VIL, VOH, VOL
  VIH Minimum input voltage guaranteed to be recognized as H
  VIL Maximum input voltage guaranteed to be recognized as L
  VOH Minimum output voltage guaranteed produced for H
  VOL Maximum output voltage guaranteed produced for L
+5V
Typical CMOS Values
  VOH Vcc – 0.1V
  VIH 70% of Vcc
  VIL 30% of Vcc
  VOL Gnd + 0.1V

## Slide 20: Logic Levels
Common across a logic family (e.g. all HC parts)
VIH, VIL, VOH, VOL
+5V
0.0V
Vcc = 5.0V
VIH = 3.5V
VIL = 1.5V
VOH = 4.44V
VOL = 0.5V
Low
Undefined
High

## Slide 21: Logic Levels
0V
5V
0V
5V
Input A
Output F
VIH = 3.5V
VIL = 1.5V
VOH = 4.44V
VOL = 0.5V

## Slide 22: Noise Margin
Ensures correct behavior despite typical conditions
0.0V
Vcc = 5.0V
VIH = 3.5V
VIL = 1.5V
VOH = 4.44V
VOL = 0.5V
Low
Undefined
High
Noise Marginhigh = VOH - VIH
Noise Marginlow = VIL - VOL
Aside from ensuring correct operation within a logic family, why else might we care about Vih, Vil, Voh, Vol?
Interfacing between logic families!

## Slide 23: Family Logic Level Comparison
Noise Margins for various families

## Slide 24: Propagation Delay

## Slide 25: Propagation Delay (Tpd, Tplh, Tphl)
Outputs don’t instantaneously reflect input changes
Propagation delay is a measure of this time
Delay from H to L can be different than from L to H
50%
50%

## Slide 26: Rise and Fall Time

## Slide 27: Rise and Fall Time (Tr, Tf)
Takes time for signal to reach its output voltage
Will be affected by capacitance, fan-out
Also known as slew rate
Typically measured from 10%/90% of VOL/VOH swing
VOL
VOH
90%
10%
tr
tf

## Slide 28: CMOS Voltage vs. Speed
How voltage affects speed?
Voltage grows and speed grows

## Slide 29: Fan-Out

## Slide 30: Current and Fan-Out
IIH, IIL, IOH, IOL
  IIH Maximum current that flows into the input in H state
  IIL Maximum current that flows into the input in L state
  IOH Maximum current that output can source in H state while maintaining output voltage of at least VOH
  IOL Maximum current that output can sink in L state while maintaining output voltage of no more than VOL

## Slide 31: Fan-Out
Sourcing current
IOH = S (IIH)
IOH Maximum current that output can source in H state while maintaining output voltage of at least VOH
IIH Maximum current that flows into the input in H state

## Slide 32: Fan-Out
Sinking current
IOL = S (IIL)
IIL Maximum current that flows into the input in L state
IOL Maximum current that output can sink in L state while maintaining output voltage of no more than VO

## Slide 33: Power Dissipation

## Slide 34: Power Dissipation
Power “dissipation” and “consumption”
Static (“quiescent”) power dissipation
  When device outputs not changing
  Very low for CMOS
Dynamic power dissipation

## Slide 35: CMOS Voltage Roadmap

## Slide 36: Product Life Cycle

## Slide 37: Sample Data Sheet (Part 1)
Description
Package options and pinouts
Main features/benefits of device (“features bullets”)
Brief device description
Part number: SN54/74<family><function>
SN54 – military; SN74 commercial
HC – high speed CMOS family
08 Quad 2-input positive (logic) AND gates

## Slide 38: Sample Data Sheet (Part 2)
Availability and corresponding orderable part number
Package style
Note different environmental conditions specified for 74/54

## Slide 39: Sample Data Sheet (Part 3)
Not Operating Conditions!

## Slide 40
Maximum
Nominal
Minimum
~70%

## Slide 41: Sample Data Sheet (Part 5)
Sometimes called “dc section”
Voh conditions:
Ioh = -20uA represents fairly normal conditions of sourcing current and results in a Voh of approximately Vcc-0.10
Ioh - -5.2mA represents high loading (TTL?) and we see a subsequent drop in the guaranteed Voh value
Similarly for Vol
Iol of 20uA results in max Vol of 0.1V (Gnd + 0.1)
Iol of 5.2mA results in max Vol of 0.33V
Notes: Voh conditions:
Ioh = -20uA represents fairly normal conditions of sourcing current and results in a Voh of approximately Vcc-0.10
Ioh - -5.2mA represents high loading (TTL?) and we see a subsequent drop in the guaranteed Voh value
Similarly for Vol
Iol of 20uA results in max Vol of 0.1V (Gnd + 0.1)
Iol of 5.2mA results in max Vol of 0.33V

## Slide 42
Sometimes called “ac section”
Include “From (Input) and To (Output)” because in more complex devices there will be multiple paths and multiple outputs.
In this device single Tpd (worst case of Tplh and Tphl)
Similary Tt instead of Tf and Tr

## Slide 43: Device Name and Package Designators

## Slide 44: Detailed Schematic Using ICs

## Slide 45: Sources
Prof. Mark G. Faust