## Slide 1: Chapter 11 Boolean Algebra
Rosen 6th ed., ch. 11

## Slide 2: What is Boolean Algebra?
A minor generalization of propositional logic.
  In general, an algebra is any mathematical structure satisfying certain standard algebraic axioms.
    Such as associative/commutative/transitive laws, etc.
  General theorems that are proved about an algebra then apply to any structure satisfying these axioms.
Boolean algebra just generalizes the rules of propositional logic to sets other than {T,F}.
  E.g., to the set {0,1} of base-2 digits, or the set {VL, VH} of low and high voltage levels in a circuit.
We will see that this algebraic perspective lends itself to the design of digital logic circuits.
Claude Shannon’s Master’s thesis!

## Slide 3: Boolean Algebra
Sections of chapter 11:
  §1 – Boolean Functions
  §2 – Representing Boolean Functions
  §3 – Logic Gates
  §4 – Minimization of Circuits

## Slide 4: §11.1 – Boolean Functions
Boolean complement, sum, product.
Boolean expressions and functions.
Boolean algebra identities.
Duality.
Abstract definition of a Boolean algebra.

## Slide 5: Complement, Sum, Product
Correspond to logical NOT, OR, and AND.
We will denote the two logic values as 0:≡F and 1:≡T, instead of False and True.
  Using numbers encourages algebraic thinking.
New, more algebraic-looking notation for the most common Boolean operators:
Precedence order→

## Slide 6: Boolean Functions
Let B = {0, 1}, the set of Boolean values.
For all nZ+, any function f:Bn→B is called a Boolean function of degree n.
There are 22ⁿ (wow!) distinct Boolean functions of degree n.
  B/c  2n rows in truth table, w. 0 or 1 in each.
Degree How many Degree How many
0 2 4 65,536 1 4 5 4,294,967,296 2 16 6 18,446,744,073,709,551,616.
3 256

## Slide 7: Boolean Expressions
Let x1, …, xn be n different Boolean variables.
  n may be as large as desired.
A Boolean expression (recursive definition) is a string of one of the following forms:
  Base cases: 0, 1, x1, …, or xn.
  Recursive cases: E1, (E1E2), or (E1+E2), where E1 and E2 are Boolean expressions.
A Boolean expression represents a Boolean function.
  Furthermore, every Boolean function (of a given degree) can be represented by a Boolean expression.

## Slide 8: Hypercube Representation
A Boolean function of degree n can be represented by an n-cube (hypercube) with the corresponding function value at each vertex.
(0,0,0)
(0,0,1)
(0,1,0)
(0,1,1)
(1,0,0)
(1,0,1)
(1,1,0)
(1,1,1)
0
1
0
1
0
1
0
1
(a, b, c)

## Slide 9: Boolean equivalents, operations on Boolean expressions
Two Boolean expressions e1 and e2 that represent the exact same function f are called equivalent. We write e1e2, or just e1=e2.
  Implicitly, the two expressions have the same value for all values of the free variables appearing in e1 and e2.
The operators ¯, +, and · can be extended from operating on expressions to operating on the functions that they represent, in the obvious way.

## Slide 10: Some popular Boolean identities
Double complement:
  x = x
Idempotent laws:
  x + x = x, x · x = x
Identity laws:
  x + 0 = x, x · 1 = x
Domination laws:
  x + 1 = 1, x · 0 = 0
Commutative laws:
  x + y = y + x, x · y = y · x
Associative laws:
  x + (y + z) = (x + y) + z
  x · (y · z) = (x · y) · z
Distributive laws:
  x + y·z = (x + y)·(x + z)
  x · (y + z) = x·y + x·z
De Morgan’s laws:
  (x · y) = x + y, (x + y) = x · y
Absorption laws:
  x + x·y = x, x · (x + y) = x
← Not true in ordinary algebras.
also, the Unit Property: x + x = 1 and Zero Property: x · x = 0

## Slide 11: Duality
The dual ed of a Boolean expression e representing function f is obtained by exchanging + with ·, and 0 with 1 in e.
  The function represented by ed is denoted fd.
Duality principle: If e1e2 then e1de2d.
  Example: The equivalence x(x+y) = x implies (and is implied by) x + xy = x.

## Slide 12: Boolean Algebra, in the abstract
A general Boolean algebra is any set B having elements 0, 1, two binary operators ,, and a unary operator  that satisfies the following laws:
  Identity laws: x  0 = x, x  1 = x
  Complement laws: x  x = 1, x  x = 0
  Associative laws:(xy)z = x(yz), (xy)z = x(yz)
  Commutative laws: x  y = y  x, x  y = y  x
  Distributive laws: x(yz) = (xy)(xz), x(yz)=(xy)(xz).
Note that B may generally have other elements besides 0, 1, and we have not fully defined any of the operators!

## Slide 13: §11.2 – Representing Boolean Functions
Sum-of-products Expansions
  A.k.a. Disjunctive Normal Form (DNF)
Product-of-sums Expansions
  A.k.a. Conjunctive Normal Form (CNF)
Functional Completeness
  Minimal functionally complete sets of operators.

## Slide 14: Sum-of-Products Expansions
Theorem: Any Boolean function can be represented as a sum of products of variables and their complements.
  Proof: By construction from the function’s truth table. For each row that is 1, include a term in the sum that is a product representing the condition that the variables have the values given for that row.
Show an example on the board.

## Slide 15: Literals, Minterms, DNF
A literal is a Boolean variable or its complement.
A minterm of Boolean variables x1,…,xn is a Boolean product of n literals y1…yn, where yi is either the literal xi or its complement xi.
  Note that at most one minterm can have the value 1.
The disjunctive normal form (DNF) of a degree-n Boolean function f is the unique sum of minterms of the variables x1,…,xn that represents f.
  A.k.a. the sum-of-products expansion of f.

## Slide 16: Conjunctive Normal Form
A maxterm is a sum of literals.
CNF is a product-of-maxterms representation.
To find the CNF representation for f,
take the DNF representation for complement f,
  f = ∑i∏j yi,j
and then complement both sides & apply DeMorgan’s laws to get:
  f = ∏i∑j yi,j
Can also get CNF more directly, using the 0 rows of the truth table.

## Slide 17: Functional Completeness
Since every Boolean function can be expressed in terms of ·,+,¯, we say that the set of operators {·,+,¯} is functionally complete.
There are smaller sets of operators that are also functionally complete.
  We can eliminate either · or + using DeMorgan’s law.
NAND | and NOR ↓ are also functionally complete, each by itself (as a singleton set).
  E.g., x = x|x, and xy = (x|y)|(x|y).

## Slide 18: §11.3 – Logic Gates
Inverter, Or, And gate symbols.
Multi-input gates.
Logic circuits and examples.
Adders, “half,” “full,” and n-bit.

## Slide 19: Logic Gate Symbols
Inverter (logical NOT, Boolean complement).
AND gate (Boolean product).
OR gate (Boolean sum).
XOR gate (exclusive-OR, sum mod 2).
x
x
y
x·y
x
y
x+y
y
x
x⊕y

## Slide 20: Multi-input AND, OR, XOR
Can extend these gates to arbitrarily many inputs.
Two commonly seen drawing styles:
  Note that the second style keeps the gate icon relatively small.
x1
x1x2x3
x2
x3
x1 ⋮
x5
x1…x5

## Slide 21: NAND, NOR, XNOR
Just like the earlier icons, but with a small circle on the gate’s output.
  Denotes that output is complemented.
The circles can also be placed on inputs.
  Means, input is complemented before being used.
x
y
x
y
y
x

## Slide 22: Buffer
What about an inverter symbol without a circle?
This is called a buffer. It is the identity function.
It serves no logical purpose, but…
It represents an explicit delay in the circuit.
  This is sometimes useful for timing purposes.
All gates, when physically implemented, incur a non-zero delay between when their inputs are seen and when their outputs are ready.
x
x

## Slide 23: Combinational Logic Circuits
Note: The correct word to use here is “combinational,” NOT “combinatorial!”
  Many sloppy authors get this wrong.
These are circuits composed of Boolean gates whose outputs depend only on their most recent inputs, not on earlier inputs.
  Thus these circuits have no useful memory.
    Their state persists while the inputs are constant, but is irreversibly lost when the input signals change.

## Slide 24: Combinational Circuit Examples
Draw a few examples on the board:
  Majority voting circuit.
  XOR using OR / AND / NOT.
  3-input XOR using OR / AND / NOT.
Also, show some binary adders:
  Half adder using OR/AND/NOT.
  Full adder from half-adders.
  Ripple-carry adders.

## Slide 25: §11.4 – Minimizing Circuits
Karnaugh Maps
Don’t care conditions
The Quine-McCluskey Method

## Slide 26: Goals of Circuit Minimization
(1) Minimize the number of primitive Boolean logic gates needed to implement the circuit.
  Ultimately, this also roughly minimizes the number of transistors, the chip area, and the cost.
    Also roughly minimizes the energy expenditure
      among traditional irreversible circuits.
  This will be our focus.
(2) It is also often useful to minimize the number of combinational stages or logical depth of the circuit.
  This roughly minimizes the delay or latency through the circuit, the time between input and output.

## Slide 27: Minimizing DNF Expressions
Using DNF (or CNF) guarantees there is always some circuit that implements any desired Boolean function.
  However, it may be far larger than needed!
We would like to find the smallest sum-of-products expression that yields a given function.
  This will yield a fairly small circuit.
  However, circuits of other forms (not CNF or DNF) might be even smaller for complex functions.