## Slide 1: Synthesis of Reversible Synchronous Counters Mozammel H A Khan Department of Computer Science and Engineering, East West University, 43 Mohakhali, Dhaka 1212, Bangladesh. mhakhan@ewubd.edu Marek A Perkowski Department of Electrical and Computer Engineering, Portland State University, 1900 SW 4th Avenue, Portland, OR 97201, USA. mperkows@cecs.pdx.edu
ISMVL, May 2011

## Slide 2: Large Toffoli Gates
Figure 2. Realizations of (a) 4×4 and (b) 5×5 Toffoli gates using 3×3 Toffoli gates, ancilla bits and garbage bits that is used in this paper.

## Slide 3: 4. Reversible Logic Synthesis Using Positive Polarity Reed-Muller Expression
An n-variable Boolean function
can be expanded on the variable
using the following positive Davio (pD) expansion:
where:

## Slide 4: 4. Reversible Logic Synthesis Using Positive Polarity Reed-Muller Expression
If we apply pD expansion on all variables of an n-variable Boolean function , then the resulting expression is called positive-polarity Reed-Muller (PPRM) expression.
An n-variable PPRM expression can be represented as
where the coefficients

## Slide 5: Calculation of PPRM coefficients
Figure 3. Computation of PPRM coefficients from output vector
For PPRM, very fast algorithms exist for conversion from truth table to PPRM, based on butterfly diagrams, illustrated here.

## Slide 6: PPRM expressions for quantum circuits
Figure 4. Realization of PPRM expression of (1) as cascade of Feynman and Toffoli gates.

## Slide 7: Synthesis of Synchronous Counters

## Slide 8
Input | Output | PPRM Coefficients
0000 | 000 | 000
0001 | 001 | 001
0010 | 010 | 010
0011 | 011 | 000
0100 | 100 | 100
0101 | 101 | 000
0110 | 110 | 000
0111 | 111 | 000
1000 | 001 | 001
1001 | 010 | 010
1010 | 011 | 000
1011 | 100 | 100
1100 | 101 | 000
1101 | 110 | 000
1110 | 111 | 000
1111 | 000 | 000
Table 2. Truth table and PPRM coefficients of the next state outputs for mod 8 up counter.
This realizes excitation functions as PPRMs. Similarly we can design methods for FPRM, GRM or a general ESOP

## Slide 9
Figure 6. Traditional circuit for mod 8 up counter

## Slide 10: Modulo 8 counter
Figure 5. Reversible circuit for mod 8 up counter.
Q2t+1 = Q1t Q0t C  Q2t
Q1t+1 = Q0t C  Q1t
Q0t+1 = C  Q0t
initialization
External or internal feedback wires

## Slide 11
Figure 7. Reversible circuit for mod 8 up counter after replacement of the T flip-flops and AND gates of Figure 6 by their reversible counter parts.
mod 8 up counter:

## Slide 12: Modulo 16 Counter
Figure 9. Traditional circuit for mod 16 up counter.

## Slide 13: mod 16 up counter:
Similarly, we can determine the PPRM expressions for the next state outputs of mod 16 up counter as follows:

## Slide 14
Figure 8. Reversible circuit for mod 16 up counter.
combinational
External quantum memory

## Slide 15
Figure 10. Reversible circuit for mod 16 up counter after replacement of the T flip-flops and AND gates of Figure 9 by their reversible counter parts.
Figure 8. Reversible circuit for mod 16 up counter.

## Slide 16: Table 3. Comparison of our direct design and replacement technique for mod 8 and mod 16 up counters.
 | Our direct technique |  | Replacement technique | 
Counter | Cost | Garbage | Cost | Garbage
mod 8 | 19 | 2 | 24 | 4
mod 16 | 35 | 4 | 40 | 6

## Slide 17: General pattern
for
for
,

## Slide 18: Conclusions
Reversible logic is very important for low power and quantum circuit design.
Most of the attempts on reversible logic design concentrate on reversible combinational logic design [9-22].
Only a few attempts were made on reversible sequential circuit design [23-28, 32-35].
The major works on reversible sequential circuit design [23-27] propose implementations of flip-flops and suggest that sequential circuit be constructed by replacing the flip-flops and gates of the traditional designs by their reversible counter parts.
This method leads to reversible sequential circuits with higher realization costs and garbage outputs. In this paper, we present a method of synchronous counter design directly from reversible gates.

## Slide 19: Conclusions (cont)
This method produces circuit with lesser realization cost and lesser garbage outputs than the circuit produced by replacement method. The proposed method also generates expressions for the next state outputs, which can be expressed in general terms for all up counters.
This generalization of the expressions for the next state outputs makes synchronous up counter design very easy and efficient.
Traditionally, state minimization and state assignment are parts of the entire synthesis procedure of finite state machines.
The role of these two processes in the realization of reversible sequential circuits [32,34] should be further investigated.
We showed a method that is specialized to certain type of counters. We can create similar methods for quantum circuits specialized to other types of counters, shifters or other sequential circuits.

## Slide 20
S. Bandyopadhyay, “Nanoelectric implementation of reversible and quantum logic,” Supperlattices and Microstructures, vol. 23, 1998, pp. 445-464.
H. Wood and D.J. Chen, “Fredkin gate circuits via recombination enzymes,” Proceedings of Congress on Evolutionary Computation (CEC), vol. 2, 2004, pp. 1896-1900.
S.K.S. Hari, S. Shroff, S.N. Mohammad, and V. Kamakoti, “Efficient building blocks for reversible sequential circuit design,” IEEE International Midwest Symposium on Circuits and Systems (MWSCAS), 2006.
H. Thapliyal and A.P. Vinod, “Design of reversible sequential elements with feasibility of transistor implementation,” International Symposium on Circuits and Systems (ISCAS 2007), 2007, pp. 625-628.

## Slide 21
M.-L. Chuang and C.-Y. Wang, “Synthesis of reversible sequential elements,” ACM journal of Engineering Technologies in Computing Systems (JETC), vol. 3, no. 4, 2008.
A. Banerjee and A. Pathak, “New designs of Reversible sequential devices,” arXiv:0908.1620v1 [quant-ph] 12 Aug 2009.
M. Kumar, S. Boshra-riad, Y. Nachimuthu and M. Perkowski, “Comparison of State Assignment methods for "Quantum Circuit" Model of permutative Quantum State Machines,” Proc. CEC 2010.
M. Lukac and M. Perkowski, Evolving Quantum Finite State Machines for Sequence Detection, Book chapter, New Achievements in Evolutionary Computation, Peter Korosec (Eds.), URL: http://sciyo.com/books/show/title/new-achievements-in-evolutionary-computation, ISBN: 978-953-307-053-7, 2010
M. Kumar, S. Boshra-riad, Y. Nachimuthu, and M. Perkowski, “Engineering Models and Circuit Realization of Quantum State Machines,” Proc. 18th International Workshop on Post-Binary ULSI Systems, May 20, 2009, Okinawa.
M. Lukac, M. Kameyama, and M. Perkowski, Quantum Finite State Machines - a Circuit Based Approach, Quantum Information Processing, accepted with revisions