## Slide 1: Triangular Sorter Using Memristive Architecture.
Under the Leadership and Guidance of Dr. Marek A Perkowski
ECE 590
By,
Sai Kiran Kadam
914459405

## Slide 2: Contents
Introduction
Triangular Sorter
Memristor
IMPLY Gate
Min_Max Cell
Parallel Sorting vs. Serial Sorting
Thermometer Code
Pipelined Data Flow
Applications

## Slide 3: Introduction
The memristive architecture is used and implemented to realize the parallel triangular sorter.
A memristor is a novel circuit produced by HP labs in the year 2008.
A parallel triangular sorting has been used rather than serial triangular sorting.
The Max_Min logic cells have been used to compare the minimum and maximum of the give input bits which is shown in the later stages.
This model can be used in computer engineering areas that deal with huge data.

## Slide 4: Triangular Sorter
A triangular sorter is a technique of sorting and comparing the given m, n bit inputs that gives out the minimum and maximum values through the implementation of Imply gate logic in its imply primitive logic cell.
The triangular sorter, here, begins with the two inputs at a time and proceeds with different inputs as the time progresses.
As the sorting progresses, the number of Max_Min cells that are required is minimized and at the last, only one Max_Min cell is required to get the maximum and minimum values

## Slide 5: Memristor
A memristor is a two terminal fundamental passive element with non-linear Characteristic
Smaller form factor.
Memristor provides the relation between Charge and Flux.
A resistor with a memory.

## Slide 6: V-I Chars of a Memristor
The ‘AB’ of the graph = ON (Less Resistance)
The ‘BC’ of the graph = Closed to Open.
The ‘CD’ of the graph = OFF (High resistance)
The ‘DA’ of the graph = Open to Close.

## Slide 7: IMPLY Gate
Imply gate is a digital logic gate used to implement a logical condition.
Imply gate is considered as a virtual gate for memristors.

## Slide 8: IMPLY Gate using Memristors
P is the input Memristor.
Q is the working Memristor.
Output available at Q
C – State of Memristor Q
RG – Ground Resistance.
P is varied.
Q is set to 0/1.

## Slide 9: IMPLY Logic using Memristors
Working of Imply Logic:
When P = 0
Memristor P =0, implies P is open
Memristor P has high resistance
The voltage across the grounding resistance is zero.
The voltage across memristor Q becomes Vset.
From V-I characteristics, Vset is greater than Vclose causing the Vset across memristor Q high that implies Vset = 1.
The state of Q becomes 1, irrespective of the input at Q.

## Slide 10: IMPLY Logic using Memristors

## Slide 11: IMPLY Logic using Memristors
When P = 1
Memristor P=1, implies P is closed.
Memristor P has less resistance. P can be treated as a wire.
The voltage across the grounding resistor is same as Vcond
The voltage across memristor Q becomes Vset-Vcond.
From Figure , Vset-Vcond < Vclose, not enough to switch the state of Q irrespective of its input.
The state of Q = Previous state of Q.

## Slide 12: 1 –bit Min_Max Cell – IMPLY Sequence

## Slide 13
4 –bit -Min_Max Cell - Imply Sequence

## Slide 14: Min_Max Cell Description
The above Min_Max cell can be described as follows:
0 represent working memristors which have value of ‘0’
P, Q are input memristors that can be ‘1’ or ‘0’
As shown above, the final output of Min and Max value is obtained after six pulses. i.e., (t0 – t5)
Max value = P+Q = P OR Q is obtained after t5. i.e., pulses after t0.
Min value = P.Q = P AND Q is obtained after t4 i.e., 5 pulses after t0.

## Slide 15: Min_Max Cell Basic
Inputs are in thermometer code
This makes comparison easy
Let X1=0011 X2=0111
0011 0011
&0111 +0111
0011=min 0111=max
Tradeoff is more bits/input

## Slide 16
Physical memristors are represented by Horizontal lines
The bottom side of this symbol is the negated input.
The left side is the non-negated input and the value of memristor before the pulse.
0 on the left side indicates an additional pulse required to reset the input state of the memristor to 0
The right side is the value of the memristor after the pulse

## Slide 17: Sorting
Sorting is an important operation in engineering applications.
Different types of sorting – Serial and Parallel.
  Serial Sorting:
The input bits are forwarded one after the other.
Less architecture is required.
Waiting time or delay is high.
  Parallel Sorting:
The input bits are forwarded all the same time.
Heavy architecture (more Min_Max cells) is required.
Very less waiting time as It implements a Pipeline model.

## Slide 18: Thermometer Code
Thermometer code is a type of encoding pattern in which the unsigned integer, n, is represented by n ones and the remaining zeros until the desired vector width.
The Thermometer code makes the comparison easy.
Let us take two numbers, say, 2 and 4
2 = 0011 and 4 = 1111 in Thermometer code

## Slide 19: Implemented Min_Max Cells & Buffers (Hardware)
1-bit Min_Max cell = 24
4- bit Min_Max cell = 6
4-bit 6 register - FIFO Buffers = 4
4- bit 12 register – FIFO Buffer = 2
4- bit registers = 8

## Slide 20: Pipelined Data Flow
The data flow of a parallel sorter requires more hardware when compared to a serial sorter.
The time required to get the output is less when compared to that of the Serial sorter.
The two 4-bit inputs are given at the first stage and it takes 6 pulses for the Max and Min values to appear at the output after comparison.
Meanwhile, the inputs at the second stage are already given and the second stage, now, requires a second input which is the Min value from the first stage of the pipeline.

## Slide 21
So, In order not to occur a false comparison, the inputs given at the second stage are given to a 6 stage-FIFO Buffer which enables the inputs to reach the 4-bit Min_Max cell when the Min value from the first stage is readily available.
Hence, the parallel sorting using memristive architecture progresses from here on in the similar fashion.
During the third stage, a, 12-bit FIFO Buffer is required to keep the inputs busy till the Min value from the second stage is available.
So, the parallel triangular sorter implements a Pipeline model and works in this fashion reducing the overall throughput time of the outputs

## Slide 22: Data Flow of a 4 four-bit Parallel Sorter

## Slide 23: Data Flow of a 4 four-bit Parallel Sorter.
Each Min_Max cell is labelled as (X,Y)
X – Row number;
Y- Column number.
To Maintain the delays, FIFO Buffers are placed where ever required to avoid faulty comparisons.

## Slide 24
Data Flow of a 4 four-bit Parallel Sorter.

## Slide 25: Color specification of Inputs
Here, the inputs 1,2,3,4 and outputs 1,2,3,4
are represented by registers colored in RED.
The Cells marked in ‘Yellow’ are the four input bits that are required to be sorted using this Parallel Triangular Sorter.
The Yellow colored inputs move as the pulse progresses and so on.

## Slide 26
Data Flow of a 4 four-bit Parallel Sorter.

## Slide 56
Hence , the o/p of parallel sorter is available 31st Pulse

## Slide 57: Pipelined Data Flow for multiple 4-bit inputs[4]
8 registers in RED are used to represent Inputs and Outputs (1,2,3,4)
4 FIFO Buffers are used to maintain synchronicity and Delays thereby avoiding faulty comparisons.
FIFO Buffers increase the Pipeline Throughput!
6 sets of 4-bit inputs of the following color are sorted
Yellow, Green, Blue, Orange, Purple and Gold

## Slide 58
Every output is available for 6 pulses as the input delay of Min_Max cell is 6 pulses.
Timing Constraints:
1. First input set given at ‘t0‘, the output
Input Set | Time at Input | Time atOutput
Set 1 | t0 | t30
Set 2 | t6 | t36
Set 3 | t12 | t42
Set 4 | t18 | t48
Set 5 | t24 | t54
Set 6 | t30 | t60

## Slide 91
At the end, only one 1 Min_Max cell is required, hence the name Triangular sorter.

## Slide 92
Advantages:
They are cost effective.
Array is modular i.e. adjustable to various performance goals.
Large number of processors work together.
Local communication in systolic array is advantageous for communication to be faster.
Exploit concurrency.

## Slide 93: Applications
Sorter circuits find application while working with a lot of large data sets.
A sorted array or data is much easier to understand
Sorted data is useful in extracting meaningful insights from unstructured or structured data.
Sorting detects the redundancy in a large circuit with m n-bit inputs.
Very significant role and is going to be useful in the near future in the areas of Data Science, Machine Learning, etc.

## Slide 94: References
http://web.cecs.pdx.edu/~mperkows/CLASS_VHDL_99/S2016/01.MEMRISTIVE_ARCHITECTURE/006.%20Anika%20davidson.pdf
http://web.cecs.pdx.edu/~mperkows/CLASS_VHDL_99/slides08.html
http://www.ijera.com/papers/Vol5_issue5/Part%20-%205/T50505105109.pdf
http://www.cs.kent.edu/~batcher/sort.pdf
http://www-bcf.usc.edu/~dkempe/CS104/10-31.pdf