Incremental Hough Transform

Derek Schmidlkofer

ECE 590:  VHDL

Prof. Marek Perkowski

June 15, 2006

Final Project

Introduction

The Hough transform was first introduced by Paul Hough in 1962 [1] with the aim of detecting alignments in T.V. lines.  It later became the basis of a great number of image analysis applications.  The Hough transform is mainly used to detect parametric shapes in images.  It was first used to detect straight lines and later extended to other parametric models such as circumferences or ellipses, being finally generalized to any parametric shape [2].  The key idea of the Hough transform is that spatially extended patterns are transformed into a parameter space where they can be represented in a spatially compact way.  Thus, a difficult global detection problem in the image space is reduced to an easier problem of peak detection in a parameter space.

A set of collinear image points (x, y) can be represented by the equation:

(1)

where m and b are two parameters, the slope and intercept, which characterize the line.  Equation (1) maps each value of the parameter combination (m, b) to a set of image points.  But Equation (1) can be “read” as a backprojection, i.e. it represents the set of straight lines, each defined by a point (m, b) in the parameter space, passing through an image point (x, y).  From this point of view, each image point (x, y) defines a straight line in the parameter space which represents all possible combinations of (m, b) defining lines passing through (x, y).  Points which are collinear in the image space all intersect at a common point in the parameter space and the coordinates of this parameter point characterize the straight line connecting the image points.  Thus, the problem of line detection in image space is transformed to the problem of finding intersection points (peaks) in the parameter space.

The Hough transform offers several advantages.  First, each image point is treated independently and therefore parallel processing is possible and the method is suitable for real-time applications.  Second, the method is robust to the presence of noise, since noisy image points are very unlikely to contribute to a peak in the parameter space.  Third, since each image point contributes independently to the parameter space points, the algorithm is able to work even if the shape is occluded.  A final advantage is that Hough transform is able to detect different instances of the desired shape at the same time, depending on the number of peaks which are considered in the parameter space.  The main drawbacks of the Hough transform are its large storage and computational requirements.

Standard Hough Transform

The Straight Line Hough transform (SLHT) was the first, and probably the most, used of the parameter-based transformations.  The SLHT idea has been introduced in the previous section starting from Equation (1).  However, a problem arises when lines have large slopes, i.e. .  Duda and Hart [3] solved the problem of an unbounded parameter space suggesting that straight lines might be more usefully parameterized by the use of polar coordinates, i.e. the length r and the orientation θ of the normal vector to the line from the image origin.  Thus, a straight line is represented by the following equation:

(2)

In the conventional implementation, The Hough transform essentially consists of three stages:

1. Characteristic point detection. Not all the image points are mapped to the parameter space. An information reduction is performed in the image such that it preserves the shapes which are wanted to be detected. Thus, some pixels of the image are selected according to certain local properties (e.g. gradient magnitude and gradient orientation). Usually this preprocessing step is a local edge detector.

2. Transform mapping. Each characteristic point of the image space is mapped to the parameter space. This parameter space is represented by a two-dimensional accumulator array (n-dimensional for detection of higher-order shapes). A voting rule usually underlies the transform mapping. This voting rule determines how the transform mapping affects the contents of the accumulator array. The simplest voting rule is to increment the parameter points (θ, r) mapped from an image point (x, y).

3. Peak detection. To extract the corresponding parameter values of the detected shape from the accumulator array. The simplest method consists in performing a global thresholding on the accumulator array. Since the presence of noise and distortion may result in true peaks split between several accumulator cells and, thus, not detected, different kinds of clustering procedures are also applied.

Each image point (x, y) is mapped using the Hough transform to the curve Equation (2) in the  plane.  Both r and θ axes have to be quantized and hence a two-dimensional accumulator array must be constructed in the  plane.  Equation (2) is applied to each point in the image and the contents of all the cells in the transform plane that the corresponding curve passes through are incremented.  This equation represents the line in the  plane that has a distance r to the origin and the normal to which makes an angle θ with the x-axis (Fig 1).  Therefore, all points in the  plane located on the line  are mapped to curves (1) in the  plane that all pass through the point.  The Hough transform method described above is known in literature as the Standard Hough Transform (SHT) [1].  Using of direct implementation of the SHT in PLD leads to slow and large multipliers and look-up table utilization.  To solve this problem, we utilize the incremental Hough Transform (IHT) [4], which eliminates necessity of trigonometric operations and is based on the following ideas.

Figure 1:  Relationship between (x, y) and (r, θ)

Incremental Hough Transform

The equation  can be written as:

(3)

whereand n and K are the index and the number of the divisions of the θ-axis of

the parameter space, respectively.  From (3) follows:

(4)

For small values of ε we can assume that  and .  Then:

(5)

If , we can write:

(6)

Note that

(7)

Thus, the IHT2 is defined by the equations:

for 	(8)

with and [4].

Modifications of the Incremental Hough Transform

As can be seen on Fig.2, IHT2 result contains an error increased with each transform step.  At  the beginning to the 2nd part is the difference eliminated, but in the next step is error increased as well.  We can assume the increasing of the initial points can decrease error comparing to SHT.

Figure 2:  SHT vs. IHT2 for point  with K = 20

Let’s assume, then

(9)

For calculation for (8) and (9) is for each n+1 step necessary to substitute results

from nth step.  Let’s divide the range of K:

(10)

By application of each sub-ranges  and  to (8) and  and  to (9) we obtain 4 ranges, where are independent to each other for each n+1 step.  Then a new

modification of the incremental Hough Transform (IHT4) [5]can be expressed:

for  	(11)

and the initial computing points are calculated:

(12)

Objective

Create a circuit that will perform the Hough transform on an image that has undergone edge detection information reduction.  The design should be able to read in an image of arbitrary size and output equations representing lines that are present in the image.

Specifications

The design should have a request bit, an input ready bit, a parallel vector input equal to the height of the image, an output bit representing that the task is complete, an output referencing which line coordinates are being output, an output for the r (distance coordinate, and an output for the θ (angle) coordinate.  All the edges in the image will be represented by ones in the image array all other elements of the array will be zero.  Each element of the image array will undergo Hough transformation and output to an accumulator array representing Hough Space.  The largest elements of the accumulator represent lines in the image.  The coordinates of these elements are sent to the output once all the input image points have undergone transformation.

Figure 3:  Hough Transformation Circuit

Implementation

The circuit will be divided into three sections.  The first section will obtain and store the image in an array.  This section is part of the control unit (CU) and can be seen in Fig. 4 CU0.  It first waits for a request form the user to start image acquisition.  It will then wait for each vector to be applied and then it will store them, sequentially, in an array of memory.  Once the entire image is obtained, a flag will be set to let the processing elements start the transform of the image.

The second section of the circuit contains the processing elements and will be explained in the next section (Fig. 6 Process Flow Chart).  The third and final step is to output the results of the transform.  The third step is actually the second part of the CU (CU1).  CU1 waits for the processing elements to finish; it then searches the accumulator for peek values which represent lines.  The design can be set to search for a certain number of lines, or lines of a certain length.  Once the indicated lines are located, the values for r and θ are output along with a corresponding line number and a flag for the user indicating that the circuit has finished (Fig. 4).

Figure 4: CU Flowchart

IHT4 Image Processing Element Implementation

Implementation of the IHT4 processor can be seen in the architecture of Fig. 5.  In the first transform step the initial values for each section of K are calculated from equations (12).  Then the actual values with help of the previous values are calculated in each transform step.  If the value of ε is carefully selected as 1/2m, multiplication from equations (11) can be realized using only shift registers.  This simplification leads to

effective and fast realization, which can be expressed as:

A more detailed view of the dynamics of the processing elements can be seen in the flow chart of Fig. 6.

Figure 5:  Architecture of IHT4 processor

Figure 6:  Processor Flowchart

VHDL Code for IHT4 Circuit

--Derek Schmidlkofer

--ECE 590

--Final Project:  Hough Transform

Library ieee;

use ieee.std_logic_1164.all;

use work.all;

--define entity

entity HT is

port (  Clk: in std_logic;

request: in std_logic;

image_vector_ready: in integer;

image_vector: in bit_vector(0 to 9);

hough_done: out bit;

line_number: out integer;

r_out: out integer;

n_out: out integer);

end entity HT;

architecture IHT4 of HT is

begin

--set constants

constant image_width: integer := (10-1);        --image width

constant image_height: integer := (10-1);       --image heigth

constant K: integer := 20;       	--resolution of theta in hough accumulator

constant number_of_lines: integer := 3;

--number of lines that are to be detected

constant length_of_line: integer := 5;

--minimum number of pixles required for a line

constant e: real := 0.15708;    	--e = pi/K

--internal signals

signal n0: integer :=0;                         --pointers for the accumulator

signal n1: integer :=0;                         --one for each processor

signal n2: integer :=0;

signal n3: integer :=0;

type accum_array is array (0 to K, 0 to K) of integer;  --row#, column#

signal accum: accum_array;

type image_array is array (0 to image_height, 0 to image_width) of integer;

signal image: image_array;

signal image_ready: bit := '0';

--lets image processors know that image is now in the image array

signal rn0: real;                	--intermediat values used in calculations

signal rn1: real;               	--one for each image processor

signal rn2: real;

signal rn3: real;

signal mux0: real;               	--intermediate values used in calculations

signal mux1: real;               	--again one for each processor

signal mux2: real;

signal mux3: real;

signal p0_done: bit := '0';                     --process0 is done

signal p1_done: bit := '0';                     --process1 is done

signal p2_done: bit := '0';                     --process2 is done

signal p3_done: bit := '0';                     --process3 is done

signal j: integer := 0;                         --local pointer for cu1

type r_out_array is array (0 to number_of_lines) of integer;

signal roa: r_out_array;                        --storage array for cu1

type n_out_array is array (0 to number_of_lines) of integer;

signal noa: n_out_array;                        --storage array for cu1

-------------------------------------------------------------------------------

--convert image_vector (bit) to image array (integer)

cu0: process

variable x: integer :=0;                               --local pointers x and y

variable y: integer :=0;

begin

wait until request = '1';       --wait for request form external source

x := 0;                                         --set starting column

while x <= image_width loop                     --image width = 10

wait until image_vector_ready = x;

--wait for new image vector to be input

y := 0;                                 --reset y pointer

while y <= image_height loop

if image_vector(y) = '1' then

--convert vector to 2D array

image(x,y) <= 1;

else

image(x,y) <= 0;

end if;

y := y + 1;                     --increment y pointer

end loop;

x := x + 1;                                     --increment x pointer

end loop;

image_ready <= '1';      --tell image processors that image is in array

end process cu0;

-------------------------------------------------------------------------------

--IHT4 process element

--<0,K/4>

process0: process

variable x0: integer :=0;                	--local pointers x and y

variable y0: integer :=0;

variable rn0i : integer;                	--used in converting real to integer

begin

wait until image_ready = '1';   	--image is in array

x0 := 0;                          	--set x pointer to inital position

while x0 <= image_width loop

y0 := 0;                         	--set y pointer to inital position

while y0 <= image_height loop

n0 <= 0;                  	--set n pointer to initial position

rn0 <= real(x0);

--set r to initial value/convert integer to real

mux0 <= rn0;

if image(y0,x0) = 1 then

--check to see if calculations are needed

rn0i := integer(rn0);

--converting real to integer

accum(rn0i,n0) <= accum(rn0i,n0) + 1;

--increment accumulator at initaial point

while n0 < (K/4) loop

--n goes from 0 to 4 because K = 20

n0 <= n0 + 1;     --increment n pointer

wait until n0 = n2;

--wait for r value from other processor

rn0 <= (mux0 + (e*rn2));

--calculate new r value

--later on, multiplication will be done using

--shift registers by selecting e to be 1/2m

mux0 <= rn0;         --update mux value

rn0i := integer(rn0);

--converting real to integer

accum(rn0i,n0) <= accum(rn0i,n0) + 1;

--increment accumulator

end loop;

else n0 <= 0;           --do nothing, reset n pointer

end if;

y0 := y0 + 1;                   --increment y pointer

end loop;

x0 := x0 + 1;                           --increment x pointer

end loop;

p0_done <= '1';                         --process is done

end process process0;

-------------------------------------------------------------------------------

--<K/4,K/2> --see process0 for code comments

process1: process

variable x1: integer :=0;

variable y1: integer :=0;

variable rn1i : integer;

begin

wait until image_ready = '1';

x1 := 0;

while x1 <= image_width loop

y1 := 0;

while y1 <= image_height loop

n1 <= 0;

rn1 <= (0.707* (real(y1 + x1)));

mux1 <= rn1;

if image(y1,x1) = 1 then

rn1i := integer(rn1);

accum(rn1i,(n1 + (K/4))) <= accum(rn1i,(n1 + (K/4))) + 1;

while n1 < (K/4) loop

n1 <= n1 + 1;

wait until n1 = n3;

rn1 <= (mux1 + (e*rn3));

mux1 <= rn1;

rn1i := integer(rn1);

accum(rn1i,(n1 + (K/4))) <= accum(rn1i,(n1 + (K/4))) + 1;

end loop;

else n1 <= 0;

end if;

y1 := y1 + 1;

end loop;

x1 := x1 + 1;

end loop;

p1_done <= '1';

end process process1;

-------------------------------------------------------------------------------

--<K/2,3K/4> --see process0 for code comments

process2: process

variable x2: integer :=0;

variable y2: integer :=0;

variable rn2i : integer;

begin

wait until image_ready = '1';

x2 := 0;

while x2 <= image_width loop

y2 := 0;

while y2 <= image_height loop

n1 <= 0;

rn2 <= real(y2);

mux2 <= rn2;

if image(y2,x2) = 1 then

rn2i := integer(rn2);

accum(rn2i,(n2 + (K/2))) <= accum(rn2i,(n2 + (K/2))) + 1;

while n2 < (K/4) loop

n2 <= n2 + 1;

wait until n2 = n0;

rn2 <= (mux2 - (e*rn0));

mux2 <= rn2;

rn2i := integer(rn2);

accum(rn2i,(n2 + (K/2))) <= accum(rn2i,(n2 + (K/2))) + 1;

end loop;

else n2 <= 0;

end if;

y2 := y2 + 1;

end loop;

x2 := x2 + 1;

end loop;

p2_done <= '1';

end process process2;

-------------------------------------------------------------------------------

--<3K/4,K> --see process0 for code comments

process3: process

variable x3: integer :=0;

variable y3: integer :=0;

variable rn3i : integer;

begin

wait until image_ready = '1';

x3 := 0;

while x3 <= image_width loop

y3 := 0;

while y3 <= image_height loop

n3 <= 0;

rn3 <= (0.707* (real(y3 - x3)));

mux3 <= rn3;

if image(y3,x3) = 1 then

rn3i := integer(rn3);

accum(rn3i,(n3 + ((3*K)/4))) <= accum(rn3i,(n3 + ((3*K)/4))) + 1;

while n3 < (K/4) loop

n3 <= n3 + 1;

wait until n3 = n1;

rn3 <= (mux3 - (e*rn1));

mux3 <= rn3;

rn3i := integer(rn3);

accum(rn3i,(n3 + ((3*K)/4))) <= accum(rn3i,(n3 + ((3*K)/4))) + 1;

end loop;

else n3 <= 0;

end if;

y3 := y3 + 1;

end loop;

x3 := x3 + 1;

end loop;

p3_done <= '1';

end process process3;

-------------------------------------------------------------------------------

--locate and output lines from accumulator

cu1: process

variable x4: integer :=0;               	--local pointers x and y

variable y4: integer :=0;

begin

wait until (p0_done and p1_done and p2_done and p3_done) = '1';

--wait for processing to finish

x4 := 0;                         	--set starting column

while x4 <= K loop

y4 := 0;                  	--reset y pointer

while y4 <= 9 loop

if accum(x4, y4) >= length_of_line then

roa(j) <= x4;

noa(j) <= y4;

j <= j + 1;

y4 := y4 + 1;

exit when j > number_of_lines;

--exit loop after lines are found

else

y4 := y4 + 1;   	--increment y pointer

end if;

end loop;

x4 := x4 + 1;            	--increment x pointer

exit when j > number_of_lines;

--exit loop after lines are found

end loop;

hough_done <= '1';              	--equations are ready to be output

j <= 0;                        	--set j pointer to initial value

while j <= number_of_lines loop

line_number <= j;        	--output current line number

r_out <= roa(j);        	--output current line r value

n_out <= noa(j);         	--output current line n value

wait for 10 ns;         --output new line elements every 10 ns

j <= j + 1;              	--increment j pointer

end loop;

end process cu1;

end architecture IHT4;

-------------------------------------------------------------------------------

Testbench for first part of CU (CU0)

library ieee;

use ieee.std_logic_1164.all;

use work.all;

use globals.all;

package globals is

constant image_width: integer := 10;

constant image_height: integer := 10;

end globals;

entity cu0 is

port (  Clk: in bit;

request: in bit;

image_vector_ready: in integer;

image_vector: in bit_vector(0 to 9));   --image height = 10

end entity cu0;

-------------------------------------------------------------------------------

architecture IHT4 of cu0 is

type image_array is array (0 to 9, 0 to 9) of integer;  --row,column

signal image: image_array;

signal image_ready: bit :='0';

begin

cu0: process

variable x: integer :=0;                               --local pointers x and y

variable y: integer :=0;

begin

wait until request = '1';       --wait for request form external source

x := 0;                                         --set starting column

while x <= 9 loop                               --image width = 10

wait until image_vector_ready = x;

--wait for new image vector to be input

y := 0;                                 --reset y pointer

while y <= 9 loop

if image_vector(y) = '1' then

--convert vector to 2D array

image(x,y) <= 1;

else

image(x,y) <= 0;

end if;

y := y + 1;                     --increment y pointer

end loop;

x := x + 1;                                     --increment x pointer

end loop;

image_ready <= '1';      --tell image processors that image is in array

end process cu0;

end IHT4;

-------------------------------------------------------------------------------

library ieee;

use ieee.std_logic_1164.all;

use work.all;

entity testcu0 is

end testcu0;

architecture stimulus of testcu0 is

component cu0

port (  Clk: in bit;

request: in bit;

image_vector_ready: in integer;

image_vector: in bit_vector(0 to 9));

end component;

signal Clk: bit;

signal request: bit;

signal image_vector_ready: integer;

signal image_vector: bit_vector(0 to 9);

type image_array is array (0 to 9, 0 to 9) of integer;

signal image: image_array;

signal image_ready: bit :='0';

begin

uut: cu0 port map(Clk, request, image_vector_ready, image_vector);

process

constant PERIOD: time := 40 ns;

begin

--test image

--0('1','1','0','0','0','0','0','0','0','0')

--1('0','1','0','0','0','0','0','0','0','0')

--2('0','1','1','0','0','0','0','0','0','0')

--3('0','1','0','1','0','0','0','0','0','0')

--4('0','1','0','0','1','0','0','0','0','0')

--5('0','1','0','0','0','1','0','0','0','0')

--6('0','1','0','0','0','0','1','0','0','0')

--7('1','1','1','1','1','1','1','1','1','1')

--8('0','1','0','0','0','0','0','0','1','0')

--9('0','1','0','0','0','0','0','0','0','1')

image_vector <= ('1','1','0','0','0','0','0','0','0','0');

image_vector_ready <= 0;

request <= '1';

wait for PERIOD;

image_vector <= ('0','1','0','0','0','0','0','0','0','0');

image_vector_ready <= 1;

wait for PERIOD;

image_vector <= ('0','1','1','0','0','0','0','0','0','0');

image_vector_ready <= 2;

wait for PERIOD;

image_vector <= ('0','1','0','1','0','0','0','0','0','0');

image_vector_ready <= 3;

wait for PERIOD;

image_vector <= ('0','1','0','0','1','0','0','0','0','0');

image_vector_ready <= 4;

wait for PERIOD;

image_vector <= ('0','1','0','0','0','1','0','0','0','0');

image_vector_ready <= 5;

request <= '1';

wait for PERIOD;

image_vector <= ('0','1','0','0','0','0','1','0','0','0');

image_vector_ready <= 6;

wait for PERIOD;

image_vector <= ('1','1','1','1','1','1','1','1','1','1');

image_vector_ready <= 7;

wait for PERIOD;

image_vector <= ('0','1','0','0','0','0','0','0','1','0');

image_vector_ready <= 8;

wait for PERIOD;

image_vector <= ('0','1','0','0','0','0','0','0','0','1');

image_vector_ready <= 9;

wait for PERIOD;

image_vector <= ('0','0','0','0','0','0','0','0','0','0');

image_vector_ready <= 10;

wait for PERIOD;

wait;

end process;

end stimulus;

Figure : Testbench results for CU0

Testbench for process0 (p0)

library ieee;

use ieee.std_logic_1164.all;

use work.all;

entity p0 is

--no ports, all signals

end entity p0;

-------------------------------------------------------------------------------

--IHT4 process element

--<0,K/4>

architecture IHT4 of p0 is

constant K: integer := 20;

constant e: real := 0.15708;                            --e = pi/K

signal n0: integer :=0;

signal n2: integer :=0;

signal rn0: real;

signal rn2: real;

signal mux0: real;

type accum_array is array (0 to K, 0 to K) of integer;  --row#, column#

signal accum: accum_array;

type image_array is array (0 to 4, 0 to 4) of integer;  --row,column

signal image: image_array;

signal image_ready: bit :='0';

signal p0_done: bit :='0';

begin

process0: process

variable x0: integer :=0;                  --local pointers x and y

variable y0: integer :=0;

variable rn0i : integer;                   --used in converting real to integer

begin

wait until image_ready = '1';       --image is in array

x0 := 0;                            --set x pointer to initial position

while x0 <= 4 loop

y0 := 0;                            --set y pointer to initial position

while y0 <= 4 loop

n0 <= 0;                    --set n pointer to initial position

rn0 <= real(x0);    --set r to initial value/convert

--integer to real

mux0 <= rn0;

if image(y0,x0) = 1 then  --check to see if

--calculations are needed

rn0i := integer(rn0); --converting real to int

accum(rn0i,n0) <= accum(rn0i,n0) + 1;

--increment accumulator at initial point

while n0 < (K/4) loop      --n goes from 0 to 4

--because K = 20

n0 <= n0 + 1;     --increment n pointer

wait until n0 = n2;

--wait for r value from other processor

rn0 <= (mux0 + (e*rn2));

--calculate new r value --later on,

--multiplication will be done using shift registers by selecting e to be 1/2m

mux0 <= rn0;         --update mux value

rn0i := integer(rn0);

--converting real to integer

accum(rn0i,n0) <= accum(rn0i,n0) + 1;

--increment accumulator

end loop;

else n0 <= 0;           --do nothing, reset n pointer

end if;

y0 := y0 + 1;                   --increment y pointer

end loop;

x0 := x0 + 1;                           --increment x pointer

end loop;

p0_done <= '1';                         --process is done

end process process0;

end IHT4;

-------------------------------------------------------------------------------

library ieee;

use ieee.std_logic_1164.all;

use work.all;

entity testp0 is

end testp0;

architecture stimulus of testp0 is

component pr0

port (  Clk: in bit;

image_ready: in bit;

n2: in integer;

rn2: in real;

p0_done: out bit);

end component;

signal Clk: bit;

signal n0: integer :=0;

signal n2: integer;

signal rn0: real;

signal rn2: real;

signal mux0: real;

type accum_array is array (0 to 4, 0 to 20) of integer; --row#, column#

signal accum: accum_array;

type image_array is array (0 to 4, 0 to 4) of integer;  --row,column

--signal image: image_array;

signal image_ready: bit :='0';

signal p0_done: bit :='0';

begin

uut: pr0 port map(Clk, image_ready, n2, rn2, p0_done);

process

constant PERIOD: time := 40 ns;

constant image: image_array := ((1,1,0,0,0),

(0,1,0,0,0),

(0,1,1,0,0),

(0,1,0,1,0),

(0,1,0,0,1));

begin

wait for PERIOD;

rn2 <= 0.0;

n2 <= 0;

wait for PERIOD;

image_ready <= '1';

wait for PERIOD;

rn2 <= 0.0;

n2 <= 1;

wait for PERIOD;

rn2 <= 0.0;

n2 <= 2;

wait for PERIOD;

rn2 <= 0.0;

n2 <= 3;

wait for PERIOD;

rn2 <= 0.0;

n2 <= 4;

wait for PERIOD;

rn2 <= 1.0;

n2 <= 0;

wait for PERIOD;

rn2 <= 1.0;

n2 <= 1;

wait for PERIOD;

rn2 <= 0.975;

n2 <= 2;

wait for PERIOD;

rn2 <= 0.926;

n2 <= 3;

wait for PERIOD;

rn2 <= 0.853;

n2 <= 4;

wait for PERIOD;

rn2 <= 2.0;

n2 <= 0;

wait for PERIOD;

rn2 <= 2.0;

n2 <= 1;

wait for PERIOD;

rn2 <= 1.951;

n2 <= 2;

wait for PERIOD;

rn2 <= 1.852;

n2 <= 3;

wait for PERIOD;

rn2 <= 1.705;

n2 <= 4;

wait for PERIOD;

wait;

end process;

end stimulus;

Figure : Testbench results for process0

|  | x=0 |  |  | x=1 |  |  | x=2 |  |  | x=3 |  |  | x=4 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| y=0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0.000 | 0.000 |  | 1.000 | 0.000 |  | 2.000 | 0.000 |  | 3.000 | 0.000 |  | 4.000 | 0.000 |
| n=1 | 0.000 | 0.000 |  | 1.000 | -0.157 |  | 2.000 | -0.314 |  | 3.000 | -0.471 |  | 4.000 | -0.628 |
| n=2 | 0.000 | 0.000 |  | 0.975 | -0.314 |  | 1.951 | -0.628 |  | 2.926 | -0.942 |  | 3.901 | -1.257 |
| n=3 | 0.000 | 0.000 |  | 0.926 | -0.467 |  | 1.852 | -0.935 |  | 2.778 | -1.402 |  | 3.704 | -1.869 |
| n=4 | 0.000 | 0.000 |  | 0.853 | -0.613 |  | 1.705 | -1.226 |  | 2.558 | -1.838 |  | 3.410 | -2.451 |
|  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |
| y=1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0.000 | 1.000 |  | 1.000 | 1.000 |  | 2.000 | 1.000 |  | 3.000 | 1.000 |  | 4.000 | 1.000 |
| n=1 | 0.157 | 1.000 |  | 1.157 | 0.843 |  | 2.157 | 0.686 |  | 3.157 | 0.529 |  | 4.157 | 0.372 |
| n=2 | 0.314 | 0.975 |  | 1.289 | 0.661 |  | 2.265 | 0.347 |  | 3.240 | 0.033 |  | 4.215 | -0.281 |
| n=3 | 0.467 | 0.926 |  | 1.393 | 0.459 |  | 2.319 | -0.009 |  | 3.245 | -0.476 |  | 4.171 | -0.943 |
| n=4 | 0.613 | 0.853 |  | 1.465 | 0.240 |  | 2.318 | -0.373 |  | 3.171 | -0.986 |  | 4.023 | -1.599 |
|  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |
| y=2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0.000 | 2.000 |  | 1.000 | 2.000 |  | 2.000 | 2.000 |  | 3.000 | 2.000 |  | 4.000 | 2.000 |
| n=1 | 0.314 | 2.000 |  | 1.314 | 1.843 |  | 2.314 | 1.686 |  | 3.314 | 1.529 |  | 4.314 | 1.372 |
| n=2 | 0.628 | 1.951 |  | 1.604 | 1.636 |  | 2.579 | 1.322 |  | 3.554 | 1.008 |  | 4.530 | 0.694 |
| n=3 | 0.935 | 1.852 |  | 1.861 | 1.385 |  | 2.787 | 0.917 |  | 3.713 | 0.450 |  | 4.639 | -0.017 |
| n=4 | 1.226 | 1.705 |  | 2.078 | 1.092 |  | 2.931 | 0.480 |  | 3.783 | -0.133 |  | 4.636 | -0.746 |
|  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |
| y=3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0.000 | 3.000 |  | 1.000 | 3.000 |  | 2.000 | 3.000 |  | 3.000 | 3.000 |  | 4.000 | 3.000 |
| n=1 | 0.471 | 3.000 |  | 1.471 | 2.843 |  | 2.471 | 2.686 |  | 3.471 | 2.529 |  | 4.471 | 2.372 |
| n=2 | 0.942 | 2.926 |  | 1.918 | 2.612 |  | 2.893 | 2.298 |  | 3.868 | 1.984 |  | 4.844 | 1.669 |
| n=3 | 1.402 | 2.778 |  | 2.328 | 2.311 |  | 3.254 | 1.843 |  | 4.180 | 1.376 |  | 5.106 | 0.908 |
| n=4 | 1.838 | 2.558 |  | 2.691 | 1.945 |  | 3.544 | 1.332 |  | 4.396 | 0.719 |  | 5.249 | 0.106 |
|  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |
| y=4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0.000 | 4.000 |  | 1.000 | 4.000 |  | 2.000 | 4.000 |  | 3.000 | 4.000 |  | 4.000 | 4.000 |
| n=1 | 0.628 | 4.000 |  | 1.628 | 3.843 |  | 2.628 | 3.686 |  | 3.628 | 3.529 |  | 4.628 | 3.372 |
| n=2 | 1.257 | 3.901 |  | 2.232 | 3.587 |  | 3.207 | 3.273 |  | 4.183 | 2.959 |  | 5.158 | 2.645 |
| n=3 | 1.869 | 3.704 |  | 2.795 | 3.237 |  | 3.721 | 2.769 |  | 4.647 | 2.302 |  | 5.573 | 1.834 |
| n=4 | 2.451 | 3.410 |  | 3.304 | 2.797 |  | 4.156 | 2.185 |  | 5.009 | 1.572 |  | 5.862 | 0.959 |

Table : real values for testbench p0

|  | x=0 |  |  | x=1 |  |  | x=2 |  |  | x=3 |  |  | x=4 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| y=0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0 | 0 |  | 1 | 0 |  | 2 | 0 |  | 3 | 0 |  | 4 | 0 |
| n=1 | 0 | 0 |  | 1 | 0 |  | 2 | 0 |  | 3 | 0 |  | 4 | -1 |
| n=2 | 0 | 0 |  | 1 | 0 |  | 2 | -1 |  | 3 | -1 |  | 4 | -1 |
| n=3 | 0 | 0 |  | 1 | 0 |  | 2 | -1 |  | 3 | -1 |  | 4 | -2 |
| n=4 | 0 | 0 |  | 1 | -1 |  | 2 | -1 |  | 3 | -2 |  | 3 | -2 |
|  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |
| y=1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0 | 1 |  | 1 | 1 |  | 2 | 1 |  | 3 | 1 |  | 4 | 1 |
| n=1 | 0 | 1 |  | 1 | 1 |  | 2 | 1 |  | 3 | 1 |  | 4 | 0 |
| n=2 | 0 | 1 |  | 1 | 1 |  | 2 | 0 |  | 3 | 0 |  | 4 | 0 |
| n=3 | 0 | 1 |  | 1 | 0 |  | 2 | 0 |  | 3 | 0 |  | 4 | -1 |
| n=4 | 1 | 1 |  | 1 | 0 |  | 2 | 0 |  | 3 | -1 |  | 4 | -2 |
|  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |
| y=2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0 | 2 |  | 1 | 2 |  | 2 | 2 |  | 3 | 2 |  | 4 | 2 |
| n=1 | 0 | 2 |  | 1 | 2 |  | 2 | 2 |  | 3 | 2 |  | 4 | 1 |
| n=2 | 1 | 2 |  | 2 | 2 |  | 3 | 1 |  | 4 | 1 |  | 5 | 1 |
| n=3 | 1 | 2 |  | 2 | 1 |  | 3 | 1 |  | 4 | 0 |  | 5 | 0 |
| n=4 | 1 | 2 |  | 2 | 1 |  | 3 | 0 |  | 4 | 0 |  | 5 | -1 |
|  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |
| y=3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0 | 3 |  | 1 | 3 |  | 2 | 3 |  | 3 | 3 |  | 4 | 3 |
| n=1 | 0 | 3 |  | 1 | 3 |  | 2 | 3 |  | 3 | 3 |  | 4 | 2 |
| n=2 | 1 | 3 |  | 2 | 3 |  | 3 | 2 |  | 4 | 2 |  | 5 | 2 |
| n=3 | 1 | 3 |  | 2 | 2 |  | 3 | 2 |  | 4 | 1 |  | 5 | 1 |
| n=4 | 2 | 3 |  | 3 | 2 |  | 4 | 1 |  | 4 | 1 |  | 5 | 0 |
|  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |  | rn0 | rn2 |
| y=4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n=0 | 0 | 4 |  | 1 | 4 |  | 2 | 4 |  | 3 | 4 |  | 4 | 4 |
| n=1 | 1 | 4 |  | 2 | 4 |  | 3 | 4 |  | 4 | 4 |  | 5 | 3 |
| n=2 | 1 | 4 |  | 2 | 4 |  | 3 | 3 |  | 4 | 3 |  | 5 | 3 |
| n=3 | 2 | 4 |  | 3 | 3 |  | 4 | 3 |  | 5 | 2 |  | 6 | 2 |
| n=4 | 2 | 3 |  | 3 | 3 |  | 4 | 2 |  | 5 | 2 |  | 6 | 1 |

Table : Integer values for testbench p0

Testbench for second part of CU (CU1)

library ieee;

use ieee.std_logic_1164.all;

use work.all;

entity cu1 is

port (  hough_done: out bit;

line_number: out integer;

r_out: out integer;

n_out: out integer);

end entity cu1;

-------------------------------------------------------------------------------

--locate and output lines from accumulator

architecture IHT4 of cu1 is

constant K: integer := 4;            --resolution of theta in hough accumulator

constant number_of_lines: integer := 3;

--number of lines that are to be detected

constant length_of_line: integer := 4;

--minimum number of pixles required for a line

signal p0_done: bit := '0';                     --process0 is done

signal p1_done: bit := '0';                     --process1 is done

signal p2_done: bit := '0';                     --process2 is done

signal p3_done: bit := '0';                     --process3 is done

signal j: integer := 0;                         --local pointer

type r_out_array is array (0 to number_of_lines) of integer;

signal roa: r_out_array;

type n_out_array is array (0 to number_of_lines) of integer;

signal noa: n_out_array;

type accum_array is array (0 to K, 0 to K) of integer;  --row#, column#

signal accum: accum_array;

begin

cu1: process

variable x4: integer :=0;                       --local pointers x and y

variable y4: integer :=0;

begin

wait until (p0_done and p1_done and p2_done and p3_done) = '1';

--wait for processing to finish

x4 := 0;                         	--set starting column

while x4 <= K loop

y4 := 0;                 	--reset y pointer

while y4 <= 9 loop

if accum(x4, y4) >= length_of_line then

roa(j) <= x4;

noa(j) <= y4;

j <= j + 1;

y4 := y4 + 1;

exit when j > number_of_lines;

--exit loop after lines are found

else

y4 := y4 + 1;   	--increment y pointer

end if;

end loop;

x4 := x4 + 1;           	--increment x pointer

exit when j > number_of_lines;

--exit loop after lines are found

end loop;

hough_done <= '1';                	--equations are ready to be output

j <= 0;                          	--set j pointer to initial value

while j <= number_of_lines loop

line_number <= j;         	--output current line number

r_out <= roa(j);          	--output current line r value

n_out <= noa(j);          	--output current line n value

wait for 10 ns;          --output new line elements every 10 ns

j <= j + 1;               	--increment j pointer

end loop;

end process cu1;

end architecture IHT4;

-------------------------------------------------------------------------------

library ieee;

use ieee.std_logic_1164.all;

use work.all;

entity testcu1 is

end testcu1;

architecture stimulus of testcu1 is

component cu1

port (  hough_done: out bit;

line_number: out integer;

r_out: out integer;

n_out: out integer);

end component;

constant K: integer := 4;

constant number_of_lines: integer := 3

constant length_of_line: integer := 4

signal hough_done: bit;

signal line_number: integer;

signal r_out: integer;

signal n_out: integer;

signal p0_done: bit := '0';                     --process0 is done

signal p1_done: bit := '0';                     --process1 is done

signal p2_done: bit := '0';                     --process2 is done

signal p3_done: bit := '0';                     --process3 is done

signal j: integer := 0;                         --local pointer

type r_out_array is array (0 to number_of_lines) of integer;

signal roa: r_out_array;

type n_out_array is array (0 to number_of_lines) of integer;

signal noa: n_out_array;

type accum_array is array (0 to K, 0 to K) of integer;  --row#, column#

begin

uut: cu1 port map(hough_done, line_number, r_out, n_out);

process

constant PERIOD: time := 40 ns;

constant image: accum_array := ((0,0,0,0,0),

(0,4,0,1,0),

(3,0,0,5,6),

(0,5,0,0,0),

(0,0,0,0,2));

begin

wait for PERIOD;

p0_done <= '1';

p1_done <= '1';

p2_done <= '1';

wait for PERIOD;

p3_done <= '1';

wait;

end process;

end stimulus;

Figure : Testbench results for CU1

Conclusion

We have created a circuit that will perform the Hough transform on an image that has undergone edge detection information reduction.  Our design is able to read in an image of arbitrary size and output equations representing the lines present in the image.  We have done so using a novel modification of incremental HT (IHT4), the key module of the invariant feature extractor. The main benefit of IHT4 is increasing of parallelism of computing by factor of 2 comparing to IHT and by factor of 4 comparing to SHT. Another benefit of IHT4 is decreasing of inaccuracy of IHT by 50% in comparison to SHT.

Improvements

The most difficult aspect of coding was dealing with different data types and converting them from one form to another.  I would prefer to stay away from the real data type but is just not possible to do so in this situation.  IHT processor (IHT2 and IHT4) are parametrisable, i.e. it is possible to modify a format of representation of the float-point number, width of a mantissa or an exponent of a processed numbers as well as an image dimension.   By shrinking the width of the floating-point numbers, it’s possible to increase calculation speed and decrease the number of resources needed by the calculations without increasing error by a large margin.  I indicated in the processing elements to use shifting to perform the multiplication this would remove the need for large/slow multipliers.  The shifting elements will be left for future coding.  One final improvement would be to start processing the image as soon as the first vector is applied to the image array.

Contact Info

E-mail:  dereks@covad.net

Web:  http://www.geocities.com/dschmidlkofer/ECE590.html

References

[1]  P.V.C. Hough.  Method and means for recognizing complex patterns.  Technical

report, 1962.  U.S. Patent No. 3069654

[2]  D.H. Ballard.  Generalizing the Hough transform to detect arbitrary shapes.  Pattern

Recognition, 13(2):111-122, 1981.

[3]  R.O. Duda and P.E. Hart. Use of the Hough transform to detect lines and curves in

pictures.  Communications of the Association for Computer Machinery, 15:11-15,

1972.

[4]  S. Tagzout, K. Achour, and K. Dejekoune.  Hough transform algorithm for FPGA

implementation.  Signal Processing, 84, 2001, 1295-1301.

[5]  J. Turan and M. Benca.  PLD Implementation of Novel Algorithm of Incremental

Hough Transform.  3,  2003

# Text boxes

Clock

Input Image Vector

Hough Transform

Input Vector Ready

Line Number

Image Height

r Value Out

Transform Request

Hough Done

Transform Request

Wait For Input Vector Ready

Vector Ready

Place Image Vector into Image array

Increment to next column of image array

Whole Image Obtained

Wait for Hough Transform to complete

Transform Done

Request Line Equations

Wait for Line Equations

Equations Ready

Output Equations and Hough Done Bit

No

No

No

No

No

Yes

Yes

Yes

Yes

Yes

Set Initial MUX Value

Increment Accumulator

Increment n

Wait for other MUX

MUX in other process done

Calculate new r value

New r value goes to MUX

Increment Accumulator

n > K

Wait for image ready

Image ready

Set y = 0

Increment y

y > image width

Increment x

x > image height

Output done to CU

Yes

Yes

Yes

Yes

Yes

No

No

No

No

No

CU0

CU1

θ Value Out

Image element an edge

Yes

No