## Slide 1: ECE 171 Digital Circuits
Prof. Marek Perkowski
Maseeh College of Engineering
and Computer Science

## Slide 2
Marek Perkowski obtained his M.S. degree in Electronics and Ph.D. Degree in automatic control from Institute of Automatic Control, Department of Electronics, Technical University of Warsaw, Warsaw, Poland. He studied also pure mathematics at University of Warsaw. In years 1981-1983 he was a Visiting Assistant Professor at University of Minnesota in Minneapolis.
Since 1983 Dr. Perkowski works for Department of Electrical and Computer Engineering at Portland State University where he is a full professor and director of Intelligent Robotics Laboratory.
He worked for Cypress Semiconductor (co-author of WARP, the first FPGA compiler of VHDL), Intel Supercomputer, Sharp Microelectronics, GTE and other companies in areas of computer architecture, CAD tools for logic synthesis and image processing.
Dr. Perkowski invented Kronecker Decision Diagrams and lattices and contributed to logic synthesis software that is used in US industry. In 1994 he worked for Machine Learning group in Wright Laboratories of U.S. Air Force applying logic decomposition as a machine learning approach to pattern recognition and continued this work on several grants.
He is an author of more than 340 papers in CAD, logic synthesis, multiple-valued logic, machine learning, robotics and quantum computing and his research is highly cited. His h-index is 41 and there are more than 6300 citations to his work on Google Scholar. His “ErdÖs Number” is 4 and his ”Publication Distance” to Einstein and many famous researchers is also 4 or 3. He had visiting professor and visiting scientist positions in the Netherlands, France, Japan and Korea. In years 2002-2004 he was professor in KAIST – Korean Advanced Institute of Science and Technology where he participated in research on humanoid robotics and quantum computing.
He chaired the IEEE Technical Committee on Multiple-Valued Logic in years 2003-2005 and was a chair of IEEE Computational Intelligence Society Task Force on Quantum Computing 2006 - 2007. His main current interests are in quantum circuits and algorithms, humanoid bipeds, emotional quantum robots, robotics for teenagers, Grover algorithm, memristor logic and system design and logic synthesis for other nano-technologies such as QCA and STO. He collaborates with many groups worldwide.
Dr. Perkowski works with very talented middle-school and high-school students on projects related to quantum computing, intelligent robotics and image processing. Since 2001, the students that he supervised obtained more than 40 awards in US national and international science fairs and competitions.
His main research area is quantum computing – how to build a new generations of computers based on principles of quantum mechanics. These computers will be significantly more powerful than all contemporary standard computers.
Who is this old guy?

## Slide 3: I teach this class since 1970
1996
1981-1983
1983-2017
1970-1981
1996
2010
2002-2005
2002
And it has been exciting

## Slide 4: Year 1967
Polish Computer UMC-1
Me in your age
Flip-flops and logic gates

## Slide 5: Why Study Digital Systems
Because you’ll probably
  Design them
  Use them
  Interface with them
  Program them
They’re ubiquitous
  Obvious: PCs, Consumer Electronics
    Audio, Video, Cameras, Phones, Cable Set-top Boxes, Games
  Also: Appliances, Automobiles, Medical Devices

## Slide 6: The old days…
Only electronics – car radio (analog)

## Slide 7: Now…
Hybrid vehicle
  >150 motors, solenoids to control
  >15 microcontrollers (MCUs)
  >100 sensors to be checked
  Airbags and belt pretensioners to be fired/pre-fired
  60kW of electrical power to control

## Slide 8: Features
Digital satellite radio
GPS guidance systems
ABS brakes
Fuel injection
Anti-collision systems
Video camera
Cell phone
Entertainment systems (DVD, CD, MP3)
Anti-theft system

## Slide 9: To the “pedestrian”

## Slide 10: Our Robots

## Slide 11: Digital Systems
Two Valued (Binary) System
  On/Off
  High/Low Voltage
  Open/Closed Switch (vs. “Dimmer” Switch)
  Magnetized/Unmagnetized
  1/0

## Slide 12: Digital vs. Analog Systems
Analog systems
  continuous change
Digital systems
  discrete change

## Slide 13: Digital vs. Analog
Continuous
Discrete
(Analog audio)
(Digital audio: CD, MP3)

## Slide 14: Lecture 1
Topics
  Radix number representations
    Decimal, Binary, Octal, Hexadecimal
    Conversions
      Decimal to Binary, Octal, Hexadecimal
      Binary, Octal, Hexadecimal to Decimal
      Group of 3 for Octal
      Group of 4 for Hexadecimal

## Slide 15: Decimal and Binary Numbers

## Slide 16: Decimal
623410
100 10 1
103 102 101 100
6 2 3 4
dndn-1…d1d0 = dn x 10n + dn-1 x 10n-1 + … d1 x 101 + d0 x 100
where: 0 £ d £ 9
623410 = 6 x 103 + 2 x 102 + 3 x 101 + 4 x 100
MSD
LSD
Radix or Base 10 (Why?)
Zero referencing
MSD = most significant digit
LSD = least significant digit

## Slide 17
01
02
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
…
00
01
02
10
11
12
20
21
22
decimal
ternary
000
001
010
011
100
101
110
111
1
2
4
8
16
32
64
128
256
512
1024
2048
binary
Powers of two
Useful tables to remember

## Slide 18: Decimal
Question: How many unique (non-negative) n digit decimal numbers are there?
  10n
  1 digit: 0-9, 10 (101)
  2 digits: 00-99, 100 (102)
  3 digits: 000-999, 1000 (103)
Question: What’s the largest n digit decimal number?
  10n-1
For n=2 it is 102-1 = 99

## Slide 19: Binary
11012
8 4 2 1
23 22 21 20
1 1 0 1
dndn-1…d1d0 = dn x 2n + dn-1 x 2n-1 + … d1 x 21 + d0 x 20
where: 0 £ d £ 1
11012 = 1 x 23 + 1 x 22 + 0 x 21 + 1 x 20
MSB
LSB
Zero referencing
Radix or Base 2 (Why?)
bit
(binary digit)
word size
MSB = most significant bit
LSB = least significant bit

## Slide 20: Binary
1101101110010001
MSB
LSB
4 bit “nibble”
8 bit “byte”
This example: 16 bit word

## Slide 21: Binary
Question: How many different (non-negative) n bit binary numbers are there?
  2n
  1 bit: {0,1} 2 (21)
  2 bits: {00, 01, 10, 11}, 4 (22)
  3 bits: {000, 001, 010, 011, 100, 101, 110, 111}, 8 (23)
Question: What’s the largest n bit binary number (what’s the largest number you can represent in an n bit word)?
  2n-1

## Slide 22: Binary
Question: How many bits (what word size) do you need to represent a number n in binary?
  Let’s first ask: How many bits do you need to represent n different binary numbers?
    élog2 nù
    1 bit: n = (21) numbers
    2 bits: n = (22) numbers
    3 bits: n = (23) numbers
    m bits: n = 2m numbers
    Ceiling function because we need an integer number of bits
  Now, to represent number n, how many different numbers? n+1, so
  élog2 (n+1)ù
0 and 1
00, 01, 10 and 11
n=4, then élog (4+1)ù = 3
100

## Slide 23: Example: Disk Drives
Early ATA specification for hard disk drives
  Identified sectors of 512 (29) bytes each
    Cylinder (16 bits), numbered [0..216-1]
    Head (4 bits), numbered [0..24-1]
    Sector (8 bits), numbered [1..28-1]
  Limited hard disk capacity
    216 x 24 x (28-1) x 29 bytes
    = 127.5 x 230 = 127.5 GB
    = 136902082560 ≈ 137 x 109 bytes (137 GB)
Notes: Because disk drives capacity is touted by marketing, they use decimal to make them seem larger! Note: not same as formatted/unformatted capacity, etc.

## Slide 24: Decimal Fractions

## Slide 25: Decimal Fractions
6234.12510
100 10 1 1/10 1/100 1/1000
103 102 101 100 10-1 10-2 10-3
6 2 3 4 . 1 2 5
dndn-1…d1d0 .d-1…d-m = dn x 10n + dn-1 x 10n-1 + … d1 x 101
+ d0 x 100 + d-1 x 10-1 + … d-m x 10-m
where: 0 £ d £ 9
6234.12510 = 6 x 103 + 2 x 102 + 3 x 101 + 4 x 100
+ 1 x 10-1 + 2 x 10-2 + 5 x 10-3

## Slide 26: Binary Fractions (“Fixed Point”)
1101.1012
8 4 2 1 1/2 1/4 1/8
23 22 21 20 2-1 2-2 2-3
1 1 0 1 . 1 0 1
dndn-1…d1d0 .d-1…d-m = dn x 2n + dn-1 x 2n-1 + … d1 x 21
+ d0 x 20 + d-1 x 2-1 + … d-m x 2-m
where: 0 £ d £ 1
1101.1012 = 1 x 23 + 1 x 22 + 0 x 21 + 1 x 20
+ 1 x 2-1 + 0 x 2-2 + 1 x 2-3

## Slide 27: Octal Numbers

## Slide 28: Octal
27368
512 64 8 1
83 82 81 80
2 7 3 6
dndn-1…d1d0 = dn x 8n + dn-1 x 8n-1 + … d1 x 81 + d0 x 80
where: 0 £ d £ 7
27368 = 2 x 83 + 7 x 82 + 3 x 81 + 6 x 80
Radix or Base 8 (Why?)
Why: binary quickly becomes cumbersome for larger numbers, octal has advantage of requiring fewer digits but easily convertible to binary

## Slide 29: Octal
Radix or Base 8 (Why?)
Groups of 3 bits (8 = 23)
27368 = 010 111 011 1102
2
7
3
6
27368 = 010 111 011 1102
4 2 1
4 2 1
4 2 1
4 2 1
Why: binary quickly becomes cumbersome for larger numbers, octal has advantage of requiring fewer digits but easily convertible to binary

## Slide 30: Converting from Binary to Octal
Example: Convert 10111.11 to Octal
10111.11
… 010111.110 …
2
7
6
27.68
Group by 3s
Extend leading, trailing 0s if needed
Convert each grouping to octal
4 2 1
4 2 1
4 2 1

## Slide 31: Hexadecimal Numbers

## Slide 32: Hexadecimal
273616
4096 256 16 1
163 162 161 160
2 7 3 6
dndn-1…d1d0 = dn x 16n + dn-1 x 16n-1 + … d1 x 161 + do x 160
where: 0 £ d £ 15 !!
273616 = 2 x 163 + 7 x 162 + 3 x 161 + 6 x 160
Radix or Base 16 (Why?)
10 = A
11 = B
12 = C
13 = D
14 = E
15 = F
Why: Great if you’re a mutant (16 fingers!). Same reason as octal – better than binary for larger numbers, more popular than octal

## Slide 33: Hexadecimal
2A3F16
4096 256 16 1
163 162 161 160
2 A 3 F
2A3F16 = 2 x 163 + A x 162 + 3 x 161 + F x 160
10 = A
11 = B
12 = C
13 = D
14 = E
15 = F
2A3F16 = 2 x 163 + (10) x 162 + 3 x 161 + (15) x 160
2A3F16 = 1081510

## Slide 34: Hexadecimal
Radix or Base 16 (Why?)
Groups of 4 bits (16 = 24)
2
A
3
F
2A3F16 = 0010 1010 0011 11112
10 = A
11 = B
12 = C
13 = D
14 = E
15 = F
2A3F16 = 0010 1010 0011 11112
8 4 2 1
8 4 2 1
8 4 2 1
8 4 2 1

## Slide 35: Converting from Binary to Hex
Example: Convert 10111.11 to Hex
10111.11
… 00010111.1100 …
17.C16
Group by 4s
Extend leading, trailing 0s if needed
Convert each grouping to hex
1
7
C
8 4 2 1
8 4 2 1
8 4 2 1

## Slide 36
00
01
02
03
04
05
06
07
08
09
0A
0B
0C
0D
0E
0F
10
11
10 = A
11 = B
12 = C
13 = D
14 = E
15 = F
00
01
02
03
04
05
06
07
10
11
12
13
14
15
16
17
20
21
22
23
24
25
26
27
30
hex
octal
Useful tables to remember

## Slide 37: Decimal Conversions

## Slide 38: Decimal Conversions
Conversions from Decimal
  “Subtract the Weights” Method
  Repeated Radix Division (RRD)/Multiplication (RRM) Method
Conversions to Decimal
  Polynomial Function Method

## Slide 39: Subtract the Weights Method to convert from decimal to binary
Example: Convert 7610 to binary
28 = 256
27 = 128
26 = 64
25 = 32
24 = 16
23 = 8
22 = 4
21 = 2
20 = 1
76
64 12
12
- 8 4
4
- 4 0
1
0
0
1
1
0
0
7610 = 10011002
Works for other bases, too
MSB
LSB
Generates MSB first
What’s the largest power of 2 that will divide into the quantity?

## Slide 40: Repeated Radix Division (RRD) Method to convert to binary
Example: Convert 7610 to binary
7610 = 10011002
Works for other bases, too
2 | 76 0
| 38 0
| 19 1
| 9 1
| 4 0
| 2 0
| 1 1
Remainder from division by 2
MSB
LSB
Generates LSB first
Result of division by2
MSB

## Slide 41: Repeated Radix Multiplication (RRM) Method to convert to binary
Example: Convert 0.12510 to binary
0.125
x 2
0.250
0.250
x 2
0.500
0.500
x 2
1.000
Continue multiplying fractional part until 0
Record whole bits generated
0.0012
Works for other bases, too
MSB
LSB
Generates MSB first

## Slide 42: Polynomial Function Method
Example: Convert 4B.C216 to decimal
4B.C216 = 4 x 161 + B x 160 + C x 16-1 + 2 x 16-2
= 4 x 16 + (11) x 1 + 12 x 1/16 + 2 x 1/162
= 4 x 16 + (11) x 1 + 12 x 1/16 + 2 x 1/162
= 64 + 11 + 12 x 0.0625 + 2 x 0.00390625
= 75 + 0.75 + 0.0078125
= 75.7578125
Fancy name, but just the definition of a radix number

## Slide 43: Conversion Summary
From Decimal
  RRD Method for Integers (generates LSB first)
  RRM Method for Fractions (generates MSB first)
To Decimal
  Polynomial Function Method
Between Binary and Hex/Octal
  Use Groups of 4 (Hex) or 3 (Octal)
    Remember to extend leading/trailing 0s where necessary!
For Conversions Between Decimal/Binary
  Consider Using Hex or Octal to Reduce Work
  Then Convert Between Binary and Hex/Octal

## Slide 44
Decimal | Binary | Octal | Hex
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 45: Questions, Problems and Exam Problems
What is the difference between analog and digital signals?
Give examples of digital circuits applications in real life?
Explain general radix notation for arbitrary radix.
Draw table of powers of two.
Draw counting in binary and ternary system with about 30 numbers each.
Explain how to convert from binary to decimal and decimal to binary.
How to convert a ternary number to a binary number?
How to convert a binary number to octal number?
How to convert a binary number to radix 5 number?
How to convert from a hex number to a binary number?
How to convert from a octal number to a hex number?
How to convert between a base 5 number to a base 7 number?

## Slide 46: Sources
Mark G. Faust
John Wakerly
Notes: I talk fast. Ask me to slow down. Let me know if there are words you don’t understand. Let me know if there are concepts you don’t understand.
Poll students: Where in program are you? prior EE/ECE classes? Programming? Work experience?