## Slide 1: Lecture 2
Topics
  Binary Arithmetic (Unsigned binary operands)
  Signed number representations
    Signed Magnitude
    Diminished Radix Complement (Ones Complement)
    Radix Complement (Twos Complement)
  Binary Arithmetic Revisited and Overflow
  Sign Extension

## Slide 2: Binary Arithmetic
Rules for “carry” same as in decimal
0
0
0
+
0
1
1
+
1
0
1
+
1
1
10
+
1
carry
Here are the rules for adding of each bit
carry

## Slide 3: Unsigned Binary (UB) Addition
Examples (4-bit word)
1011
0110
+
1
1
1
10001
0010
0110
+
1
1
1000
Overflow
2 + 6
2
+ 6
8
11
+ 6
17
11 + 6
17 > 24-1

## Slide 4: Overflow (Underflow)
10101101
01101100
Definition:
Result of an arithmetic operation is too large (or small) to be represented in number of bits available
Detection:
Varies with the representation. For unsigned binary, it’s determined by a carry out of the MSB
+
1
1
1
1
1
100011001
8 bit operands

## Slide 5: Signed Numbers
Have been assuming non-negative numbers
  Unsigned Binary (UB)
Several representations for signed numbers
  Sign Magnitude (SM)
  Diminished Radix Complement (DRC)
    1s Complement
  Radix Complement (RC)
    2s Complement

## Slide 6: Sign Magnitude
MSB functions as sign bit
0 = positive
1 = negative
Range of numbers:
-(2n-1 – 1) to +(2n-1 – 1)
n = 6
Two representations for 0
Negative formed by complementing sign bit
1510 = 001111SM
-1510 = 101111SM
010100SM = 2010
110100SM = -2010

## Slide 7: Diminished Radix Complement (DRC)
Called “Ones Complement”
MSB indicates sign
0 = positive
1 = negative
(but not a sign bit!)
Range of numbers:
-(2n-1 – 1) to +(2n-1 – 1)
Two representations for 0
Negative formed by complementing entire word
(called “taking the ones complement”)
  1510 = 001111DRC
  -1510 = 110000DRC
  010100DRC = 2010
  101011DRC = -2010

## Slide 8: Radix Complement (RC)
Called “Twos Complement”
MSB indicates sign
0 = positive
1 = negative
(but not a sign bit)
Range of numbers:
-(2n-1) to +(2n-1 – 1)
Only one representation for 0
Negative formed by complementing entire word
and adding 1 (called “taking the twos complement”)
  1510 = 001111RC
  -1510 = 110001RC
  010100RC = 2010
  101100RC = -2010

## Slide 9: Radix Complement (RC)
Called “Twos Complement”
MSB indicates sign
0 = positive
1 = negative
(but not a sign bit)
Range of numbers:
-(2n-1) to +(2n-1 – 1)
Only one representation for 0
Negative formed by complementing entire word
and adding 1 (called “taking the twos complement”)
  1510 = 001111RC
  -1510 = 110001RC
  010100RC = 2010
  101100RC = -2010
1 1 1 1 0 1
-3
000011 =3
111100 = neg
111101=-3

## Slide 10: Twos Complement – Special Cases
Notes: Note: Discard carry out of sign bit position!

## Slide 11: Twos Complement – Special Cases
Example: Take Twos Complement (RC)
of 0000 (010)
0000
1111
+ 1
0000
Complement
Add One
1
1
1
Ignore carry out of MSB
Note: Discard carry out of sign bit position!
Only one representation for 0

## Slide 12: Twos Complement – Special Cases
Example: Take Twos Complement (RC)
of 1000 (-810) (most negative)
1000
0111
+ 1
1000
Complement
Add One
1
1
1
Can’t represent
Complement of the most negative number
1000 (-810) is the most negative number
-810
+810 is not represented
Notes: Note: Discard carry out of sign bit position!

## Slide 13: Why do we use RC (Twos Complement)?
BCD (which we’ll see shortly) was used in very early 4-bit microprocessors, but 2s complement is universally used now
Only one representation for zero
Simplified Addition in Twos Complement!
  Sign Magnitude Addition has complicated algorithm below:
    Must consider two operands without sign bits
    If sign bits same: perform add, check overflow
    If sign bits different: subtract (two cases)
      +A and – B  A – B
      – A and + B B – A
    Generate correct sign bit for sum
  Radix Complement (Twos Complement) Addition
    Just add!
Simple Subtraction
  Done via addition
    A + B
    A – B = A + (-B)
    Caution: Can’t take negative of most negative number

## Slide 14: Conversions of Signed Representations

## Slide 15: Conversions of Signed Representations From Decimal
Conversion from decimal
  Represent the absolute value of the number in unsigned binary (UB)
  Use the correct number of bits (add leading 0s)
  If the decimal number is negative, use the appropriate rule to negate the representation
    Sing/Magnitude (S/M) – complement the sign bit
    DRC (ones complement) – complement every bit
    RC (twos complement) – complement every bit, add 1

## Slide 16: Conversions of Signed Representations to Decimal
Conversion to decimal if number is +
  convert from unsigned binary to decimal (done!)
Conversion to decimal if number is -
  use appropriate rule to negate it (obtain its absolute value)
    Sign/Magnitude – complement the sign bit
    Ones complement – complement every bit
    Twos complement – complement every bit, add 1
  Convert this (positive) number as though unsigned binary to decimal
  Add a negative sign

## Slide 17: Binary Arithmetic
Unsigned Binary (UB)
Signed Binary (SB)
Diminished Radix Complement (DRC)
  1s complement
Radix Complement (RC)
  2s complement
Rarely used

## Slide 18: Radix Complement (RC) or Twos Complement Addition – Subtraction and Negative Numbers
Examples (4-bit word)
0101
1001
+
1
1110
Ignore carry out of MSB
7 + (-2)
5 + (-7)
7
+ (-2)
5
5
+ (-7)
(-2)
0111
1110
+
1
1
10101
1
No overflow

## Slide 19: Radix Complement (RC) or Twos Complement Addition
Examples (4-bit word)
Ignore carry out of MSB
-7 + (-2)
-7
+ (-2)
-9
1001
1110
+
10111
1
-9 < - (23)
We added two negative numbers and got a positive result!
Overflow!!

## Slide 20: Carry and Overflow

## Slide 21: Carry and Overflow
Is this an overflow condition?
If this is an unsigned binary (UB) number – Yes!
10101101
01101100
+
1
1
1
1
1
100011001
0
0
0
Overflow in UB

## Slide 22: Carry and Overflow
Is this an overflow condition?
If this is a radix complement (RC) number – No!
10101101
01101100
+
1
1
1
1
1
100011001
0
0
0
A negative number plus a positive number cannot produce an overflow
No overflow in Twos Complement

## Slide 23: Carry and Overflow Radix Complement (2s Complement)
Consider:
  Positive + Negative  Never overflow
  Negative + Negative  Overflow possible
  Positive + Positive  Overflow possible
Detecting Overflow:
  If signs of addends are same and sign of sum is different
  Equivalent to CSBP ¹ CSBP+1
C – Carry
SBP – Sign Bit Position

## Slide 24: Carry and Overflow in Twos Complement
10101101
01101100
+
1
1
1
1
1
100011001
CSBP+1
CSBP
C – Carry
SBP – Sign Bit Position
0
0
0
CSBP = CSBP+1
A negative number plus a positive number cannot produce an overflow
No overflow in Twos Complement

## Slide 25: Addition in Twos Complement
Examples (4-bit word)
1001
1110
+
10111
-7 + (-2)
-7
+ (-2)
-9
1
-9 < - (23)
We added two negative numbers and got a positive result!
0
0
0
CSBP+1
CSBP
CSBP+1 ¹ CSBP
Overflow!
Conclusion on Overflow in 2s Complement:
  There is an overflow if signs of addends are same and sign of sum is different
  Equivalent to CSBP ¹ CSBP+1
In this case there is an overflow
Notes: Returning to our previous example…

## Slide 26: Sign Extension
What happens when you move a number from a smaller word size to a larger one?
00000011
0000000000000011
(3)
(3)
11111101
0000000011111101
(253)
(253)
UB
00000011
0000000000000011
(3)
(3)
11111101
1000000001111101
(-125)
(-125)
S/M
00000011
0000000000000011
(3)
(3)
11111101
0000000011111101
(-3)
(+253!)
RC (2s complement)
11111101
1111111111111101
(-3)
(-3)
“extend” the sign bit left through the new MSB
Unsigned Binary is no problem, fill with zeros
Sign Magnitude is no problem, sign goes to MSB
26
bad
good

## Slide 27: Subtraction in Two’s -Complement

## Slide 28: Addition versus Subtraction
Use same technique as decimal
Except that the addition and subtraction tables are different
Already seen addition table
  Truth table for Sum and Cout function

## Slide 29: Subtraction table
bin | x | y | bout | d
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
difference

## Slide 30
borrow
borrow out
difference
Another method of doing subtraction

## Slide 31
Examples of decimal and corresponding binary subtractions

## Slide 32
A modular counting representation of 4-bit two’s-complement numbers
There is no plus 8

## Slide 33
A modular counting representation of 4-bit unsigned numbers

## Slide 34
Summary of addition and subtraction rules for binary numbers

## Slide 35: Questions, Problems and EXAM Problems
Meaning of carry bit.
Addition of unsigned numbers
Addition in two’s-complement system
Addition in ones-complement system.
Subtraction of unsigned numbers
Subtraction in two’s-complement system
Subtraction in ones-complement system.
Advantages of sign-magnitude system.
Advantages of two’s-complement system
Advantages of ones-complement system

## Slide 36: Questions and problems
11. Discuss examples to add binary numbers in Two’s-complement code (representation) and when it leads to overflow?
12. What are the advantages of Two’s-complement code?
13. Discuss overflow in Two’s-complement code.
14. Discuss subtraction overflow in Two’s-complement code.
15. Discuss advantages and disadvantages of number systems.
16. Discuss sign extension and show examples.
Questions, Problems and EXAM Problems

## Slide 37: Sources
Prof. Mark G. Faust
John Wakerly