## Slide 1: Lecture 5
Topics
  Canonical or Standard Forms of Functions
    SOP (Sum of Products) form
    POS (Product of Sums) form
    Relationship Between MinTerms and MaxTerms
    Converting Between Compact Forms of Functions
  Minimizing (Reducing) Functions
    Karnaugh Maps (K-maps)
    Product term sharing

## Slide 2: Boolean Equations

## Slide 3: Obtaining a Boolean Equation
In Ecotopia it’s generally illegal to use a car pool lane during weekdays if the car doesn’t have at least two occupants.
However, hybrid vehicles can use the lanes any time regardless of the number of occupants.
SUVs (even with two or more occupants) are never allowed to use the car pool lanes (unless they are also hybrids).
Write a Boolean expression in SOP form for F(W, O, S, H) which is 1 if the car is permitted to use the car pool lane today.
W is 1 if today is a weekday.
O is 1 if there are two or more occupants, S is 1 if the vehicle is an SUV, H is 1 if the vehicle is a hybrid.
W O S H F
----------
0 0 0 0 1
0 0 0 1 1
0 0 1 0 0
0 0 1 1 1
0 1 0 0 1
0 1 0 1 1
0 1 1 0 0
0 1 1 1 1
1 0 0 0 0
1 0 0 1 1
1 0 1 0 0
1 0 1 1 1
1 1 0 0 1
1 1 0 1 1
1 1 1 0 0
1 1 1 1 1
ECOTOPIA EXAMPLE

## Slide 4: Another Example: Deriving Boolean Equations
A truth table is a complete, unambiguous definition of a Boolean function…
But how do we get a Boolean expression from a truth table?
  SOP or POS
X Y Z F
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 0
1 1 0 1
1 1 1 0
F = X×Y×Z + X×Y×Z + X×Y×Z

## Slide 5: Another Example: Obtaining SOP Forms of Functions
F(A,B) = F(0,0)×A×B + F(0,1)×A×B + F(1,0)×A×B + F(1,1)×A×B
= 0×A×B + 1×A×B + 1×A×B + 1×A×B
= 0 + A×B + A×B + A×B
= A×B + A×B + A×B
OR truth table
A B F(A,B)
0 0 0 = F(0,0)
0 1 1 = F(0,1)
1 0 1 = F(1,0)
1 1 1 = F(1,1)
Reduced Form
Canonical or Standard
SOP Form
Standard Product Term
(Minterm)
A + B
Notes: Comes from Claude Shannon’s MS work. Simplified way of looking at it: just list the “terms” of AB (and complements) which result in function value of 1.

## Slide 6: Minterms and Maxterms
Notes: Majority Function

## Slide 7: Minterms
Notes: Majority Function

## Slide 8: Compact Minterm Form
F(A,B) = F(0,0)×A×B + F(0,1)×A×B + F(1,0)×A×B + F(1,1)×A×B
= S3i=0 (Fi × mi)
= 0 × m0 + 1 × m1 + 1 × m2 + 1 × m3
= m1 + m2 + m3
= S m(1,2,3)
= S (1,2,3)
OR truth table
A B F(A,B)
0 0 0 = F(0,0)
0 1 1 = F(0,1)
1 0 1 = F(1,0)
1 1 1 = F(1,1)
Notes: Comes from Claude Shannon’s MS work. Simplified way of looking at it: just list the “terms” of AB (and complements) which result in function value of 1.

## Slide 9: Minterms
S (3,5,6,7)

## Slide 10: Generalized Compact Minterm Form
F(X1, X2,… Xn) = S (minterms for 1s of the function)
F(X1, X2,… Xn) = S (minterms for 0s of the function)
Pay attention, this is negation of function F

## Slide 11: Obtaining POS Forms of Functions
F(A,B) = (F(0,0) + A + B) × (F(0,1) + A + B) × (F(1,0) + A + B) × (F(1,1) + A + B)
= (0 + A + B) × (0 + A + B) × (0 + A + B) × (1 + A +B)
= (A+B) × (A+B) × (A+B) × (1)
= (A+B) × (A+B) × (A+B)
AND truth table
A B F(A,B)
0 0 0 = F(0,0)
0 1 0 = F(0,1)
1 0 0 = F(1,0)
1 1 1 = F(1,1)
Standard Sum Term
(Maxterm)
Canonical or Standard
POS Form
Reduced Form
A × B
Notes: Comes from Claude Shannon’s MS work. Simplified way of looking at it: just list the “terms” of AB (and complements) which result in function value of 1.

## Slide 12: Maxterms
Notes: Majority Function

## Slide 13: Compact Maxterm Form
F(A,B) = (F(0,0) + A + B) × (F(0,1) + A + B) × (F(1,0) + A + B) × (F(1,1) + A + B)
= P3i=0 (Fi + Mi)
= (0 + M0) × (0 + M1) × (0 + M2) × (1 + M3)
= M0 × M1 × M2
= P M(0,1,2)
= P (0,1,2)
AND truth table
A B F(A,B)
0 0 0 = F(0,0)
0 1 0 = F(0,1)
1 0 0 = F(1,0)
1 1 1 = F(1,1)
Notes: Comes from Claude Shannon’s MS work. Simplified way of looking at it: just list the “terms” of AB (and complements) which result in function value of 1.

## Slide 14: Maxterms
P (0,1,2,4)
Notes: Majority Function

## Slide 15: Generalized Compact Maxterm Form
F(X1, X2,… Xn) = P (maxterms for 0s of the function)
F(X1, X2,… Xn) = P (maxterms for 1s of the function)
Canonical SOP
Canonical POS
negation

## Slide 16: Relationship Between Minterms and Maxterms
mi = Mi, Mi = mi
S = P, P = S

## Slide 17: Canonical SOP and POS forms using minterms and maxterms

## Slide 18
An example: Given the accompanying truth table, write the compact minterm form for F for its 1s and 0s. Write the standard SOP form for each.
X Y Z F
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 0
1 1 0 1
1 1 1 0
F = S(3,4,6)
Compact minterm form 1s:
Compact minterm form 0s:
Corresponding SOP form:
Corresponding SOP form:
F = X×Y×Z + X×Y×Z + X×Y×Z
F = S(0,1,2,5,7)
F = X×Y×Z + X×Y×Z + X×Y×Z + X×Y×Z + X×Y×Z
This is example problem 15, page 85. Solution on page 107.

## Slide 19
An example: Given the accompanying truth table, write the compact maxterm form for F for its 1s and 0s. Write the standard POS form for each.
X Y Z F
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 0
1 1 0 1
1 1 1 0
Compact maxterm form 1s:
Compact maxterm form 0s:
Corresponding POS form:
Corresponding POS form:
F = P(0,1,2,5,7)
F = P(3,4,6)
F = (X+Y+Z) × (X+Y+Z) × (X+Y+Z)
F = (X+Y+Z) × (X+Y+Z) × (X+Y+Z) × (X+Y+Z) × (X+Y+Z)
This uses the same truthtable as the preceding problem but asks for maxterms

## Slide 20: Function Minimization: Reduce Number of Literals and Terms
Simplify for Comprehension
Reduce Number of Components
Reduce Amount of Wiring/Routing
Smaller Circuit/Board Area
Lower Cost
Higher Reliability
Notes: Now we can derive an equation for a Boolean function from a truth table. How about minimizing it?

## Slide 21: Function Minimization: Reduce Number of Literals and Terms
Apply Boolean Algebra
Employ Computer Algorithm
  Quine-McCluskey tabular algorithm
  Boozer
  McBoole
  Espresso and Espresso/Exact (CAD packages)
Systematic Algebraic Reduction (SAR)
Karnaugh Maps (K-Maps)

## Slide 22: Karnaugh Maps

## Slide 23: Karnaugh (K) Maps
A graphical representation of Boolean function
Easy to perform functional reduction
Relies on adjacency (Gray code) of minterms
  Adjacent (horizontal/vertical & wrap around) cells differ in only one variable (complement)
Number form and Variable form

## Slide 24: K-Maps
2 Variable K-Map (Number Form)
Gray code!
Minterm numbers

## Slide 25: K-Maps
3 Variable K-Map (Number Form)
Gray code!
Minterm numbers

## Slide 26: K-Maps
4 Variable K-Map (Number Form)
Gray code!
Minterm numbers

## Slide 27: K-Maps
2 Variable K-Map (Variable Form)
May be more useful if plotting partially reduced functions
Careful! Preserve Gray code!

## Slide 28: K-Maps
3 Variable K-Map (Variable Form)

## Slide 29: K-Maps
4 Variable K-Map (Variable Form)

## Slide 30: My Preference…
W
W
X
Z
Y
Y

## Slide 31: Plotting Functions in K-Maps
Plot the function F1(X,Y,Z) = S(2,5,6,7)
X Y Z F1
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 0
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 1
Notes: May be given function in truth table, compact minterm/maxterm, or partially reduced (equation) form…
We’ll look at 1st two first

## Slide 32: Plotting Functions in K-Maps
Plot the function F2(A,B,C,D) = S(6,7,8,14,15)
Plot 0s!

## Slide 33: Don’t Care Outputs

## Slide 34: Don’t Care Outputs
Output of Function Doesn’t Matter
  Typically impossible input condition
  Use X instead of 0 or 1
BCD
A B C D Prime
0 0 0 0 0
0 0 0 1 1
0 0 1 0 1
0 0 1 1 1
0 1 0 0 0
0 1 0 1 1
0 1 1 0 0
0 1 1 1 1
1 0 0 0 0
1 0 0 1 0
1 0 1 0 X
1 0 1 1 X
1 1 0 0 X
1 1 0 1 X
1 1 1 0 X
1 1 1 1 X
0
1
2
3
4
5
6
7
8
9
.
.
.
.
.
.

## Slide 35: Don’t Care Outputs Compact Minterm and Maxterm Form
F3(A,B,C) = S(2,6) + Smd(3,5,7)
F3(A,B,C) = S(0,1,4) + Smd(3,5,7)
F3(A,B,C) = P(0,1,4) × PMd(3,5,7)
F3(A,B,C) = P(2,6) × PMd(3,5,7)
A B C F3
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 X
1 0 0 0
1 0 1 X
1 1 0 1
1 1 1 X

## Slide 36: Plotting K-Maps with Xs
A B C F3
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 X
1 0 0 0
1 0 1 X
1 1 0 1
1 1 1 X
F3(A,B,C) = S(2,6) + Smd(3,5,7)

## Slide 37: Plotting K-Maps from functions in partially reduced form
F4(A,B,C,D) = A×B×C×D + B×C×D + A×B + C
p1
p2
p3
p4
This is Sum of Products of literals, called SOP
Notes: Need to explain. Think of missing variables as input don’t cares (X) and look for row/col where fits (e.g. C = XXCX and we care only about squares where C is 1 regardless of other variables). All variables present in term: single cell; one variable missing: 1x2, two variables missing: 2x4, etc…

## Slide 38: Plotting K-Maps from functions in partially reduced form
F4(A,B,C,D) = A×B×C×D + A×B×C×D + A×B×C
r1
r2
r3
Notes: Need to explain. Think of missing variables as input don’t cares (X) and look for row/col where fits (e.g. C = XXCX and we care only about squares where C is 1 regardless of other variables).

## Slide 39: K-Maps for functions of 5 variables
F(V,W,X,Y,Z)
m0 through m15
m16 through m31
Notes: Don’t usually go beyond 4 or 5 variables because there are good S/W packages to do this.
Split map into two (think of them as stacked). Still maintain Gray code.

## Slide 40: K-Maps for functions of 5 variables
F(V,W,X,Y,Z) = S(3,7,9,11,12,15,16,19,23,24,27,28,31) + Smd(4,18,20,26,30)
Notes: Don’t usually go beyond 4 or 5 variables because there are good S/W packages to do this.
Split map into two (think of them as stacked). Still maintain Gray code.

## Slide 41: Another type of K-Maps for functions of 5 variables
 | 000 | 001 | 011 | 010 | 110 | 111 | 101 | 100
00 |  |  |  |  |  |  |  | 
01 |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  | 
a,b
c,d,e
Axis of symmetry (of mirror for d and e)

## Slide 42: Another type of K-Maps for functions of 6 variables
 | 000 | 001 | 011 | 010 | 110 | 111 | 101 | 100
000 |  |  |  |  |  |  |  | 
001 |  |  |  |  |  |  |  | 
011 |  |  |  |  |  |  |  | 
010 |  |  |  |  |  |  |  | 
a,b,c
d,e,f
110 |  |  |  |  |  |  |  | 
111 |  |  |  |  |  |  |  | 
101 |  |  |  |  |  |  |  | 
100 |  |  |  |  |  |  |  | 

## Slide 43: Using K-Maps to Reduce Functions

## Slide 44: Using K-Maps to Reduce Functions
Assume you’ve plotted the K-map for F(X,Y,Z) as follows:

## Slide 45: Using K-Maps to Reduce Functions
You want to obtain a reduced expression for F(X,Y,Z) in SOP form
Notes: Smallest expressions  largest cube sizes

## Slide 46: Using K-Maps to Reduce Functions
Need to “cover” 1s
Fewest product terms
Simplest expressions
  (fewest variables)
You want to obtain a reduced expression for F(X,Y,Z) in SOP form
Notes: Smallest expressions  largest cube sizes

## Slide 47: Using K-Maps to Reduce Functions
Circle all isolated 0-cubes
Circle all 1-cubes not completely contained in a larger cube
Continue for 2, 3, 4-cubes
Write the product terms (prime implicants) and OR them together
Write the expression for each product term

## Slide 48: Using K-Maps to Reduce Function F in SOP form
F(X,Y,Z) = p1 + p2 + p3 = X×Z + X×Z + Y
Notes: Smallest expressions  largest cube sizes

## Slide 49: Using K-Maps to Reduce Functions
F(X,Y,Z) = r1 + r2 = X×Y×Z + X×Y×Z
Notes: Smallest expressions  largest cube sizes

## Slide 50: K-Maps (Some Terminology)
Implicant: Product term of a function
Prime Implicant: Product term for a cube which is not completely contained in another cube
Essential Prime Implicant: Product term which provides the only covering for a given minterm and must always be used in the set of product term
Optional Prime Implicant: Product term which provides an alternative covering for a given minterm and may be used in the set of product terms
Redundant (Non-Essential) Prime Implicant: Product term for a cube which is completely contained in another cube (correct, but won’t lead to a minimum function)

## Slide 51: K-Map with only essential prime implicants

## Slide 52: K-Map with no essential prime implicants

## Slide 53: K-Map with no essential prime implicants

## Slide 54: K-Map with no essential prime implicants: alternative!

## Slide 55: Covering Order is Essential

## Slide 56: Using K-Maps to Reduce Functions
Given the following K-map, which minimum SOP form of the function
has the smallest literal count (the one for the 1s or the 0s)?
F(W,X,Y,Z) =
F(W,X,Y,Z) =
Notes: Smallest expressions  largest cube sizes

## Slide 57: Using K-Maps to Reduce Functions
F(W,X,Y,Z) = p1 + p2 + p3 = X×Z + W×Z + W×Y
lc = 6

## Slide 58: Using K-Maps to Reduce Functions
F(W,X,Y,Z) = r1 + r2 + r3 = W×X×Y + W×Z + Y×Z
lc = 7
This is POS form

## Slide 59: Using K-Maps to Reduce Functions
Given the following K-map, which minimum SOP form of the function
has the smallest literal count (the one for the 1s or the 0s)?
lc = 6
lc = 7
F(W,X,Y,Z) = r1 + r2 + r3 = W×X×Y + W×Z + Y×Z
F(W,X,Y,Z) = p1 + p2 + p3 = X×Z + W×Z + W×Y
Notes: Smallest expressions  largest cube sizes

## Slide 60: Using K-Maps to Reduce Functions
Given the following K-map, which minimum SOP form of the function
has the smallest literal count (the one for the 1s or the 0s)?
F(W,X,Y,Z) =
F(W,X,Y,Z) =
Only use don’t cares to allow larger cube sizes to be covered
Notes: Smallest expressions  largest cube sizes

## Slide 61: Using K-Maps to Reduce Functions
Only use don’t cares to allow larger cube sizes to be covered
F(W,X,Y,Z) = p1+p2+p3+p4 = X×Y×Z + W×X×Y + W×Z + Y×Z
lc = 10
Notes: Smallest expressions  largest cube sizes

## Slide 62: Using K-Maps to Reduce Functions
Only use don’t cares to allow larger cube sizes to be covered
F(W,X,Y,Z) = r1 + r2 + r3 = W×Y×Z+ X×Z + W×Y
lc = 7
Notes: Smallest expressions  largest cube sizes

## Slide 63: K-Maps for functions of 5 variables
F(V,W,X,Y,Z) = S(3,7,9,11,12,15,16,19,23,24,27,28,31) + Smd(4,18,20,26,30)
Notes: Don’t usually go beyond 4 or 5 variables because there are good S/W packages to do this.
Split map into two (think of them as stacked). Still maintain Gray code.

## Slide 64: Parallel Adder Design

## Slide 65: Let us remind the Unsigned Binary (UB) Addition
Examples (4-bit word)
1011
0110
+
1
1
1
10001
0010
0110
+
1
1
1000
Overflow
2 + 6
2
+ 6
8
11
+ 6
17
11 + 6
17 > 24-1

## Slide 66: The parallel Ripple Carry Adder is built from Full Adders
Consider a circuit to add two 4-bit numbers:
A3 A2 A1 A0
+ B3 B2 B1 B0
CO4 S3 S2 S1 S0
Truth table would have 8 inputs (28 = 256 rows) and 5 outputs,
requiring 5 minimized functions (5 8-variable K-maps).
But operation at each bit position (after A0/B0) is identical:
COi
Ai
+ Bi
COi+1 Si
“bit slice”
We iterate the Full Adder several times

## Slide 67: Full Adder Truth Table
CI A B CO S
0 0 0 0 0
0 0 1 0 1
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 1

## Slide 68: Parallel Adder Design (Iterative Circuit)
S0
S1
S2
S3
A0
A1
B0
C0
A3
B3
C3
A2
B2
C2
B1
C1
C4
The same full adder repeated 4 times in an iterative circuit.
This one is called Ripple Carry Adder
Least significant bits are here
Most significant bits are here

## Slide 69: Ripple Carry Adder
A1 A0
+ B1 B0
CO2 S1 S0
Least significant bits are here
Most significant bits are here
This is Ripple Carry Adder for two bits. Adds numbers with two bits each.
The Ripple Carry Adder below is for four bits. Adds numbers A and B with four bits each.

## Slide 70: Subtractor Design
Based on your knowledge of negative numbers in two-complement, design a parallel subtractor similar to the parallel adder from last slides.
Combine the design of the above subtractor and the parallel adder to a single circuit with control signal X that controls subtraction or addition of two numbers, A and B. If X=0 the circuit should add A and B. If X=1 the circuit should do the subtraction A-B.
Repeat the above problems for sign-magnitude systems.
Repeat the above problems for one’s-complement system.

## Slide 71: ECOTOPIA REVISITED
In Ecotopia it’s generally illegal to use a car pool lane during weekdays if the car doesn’t have at least two occupants.
However, hybrid vehicles can use the lanes any time regardless of the number of occupants.
SUVs (even with two or more occupants) are never allowed to use the car pool lanes (unless they are also hybrids).
Write a Boolean expression in SOP form for F(W, O, S, H) which is 1 if the car is permitted to use the car pool lane today.
W is 1 if today is a weekday.
O is 1 if there are two or more occupants, S is 1 if the vehicle is an SUV, H is 1 if the vehicle is a hybrid.
W O S H F
----------
0 0 0 0 1
0 0 0 1 1
0 0 1 0 0
0 0 1 1 1
0 1 0 0 1
0 1 0 1 1
0 1 1 0 0
0 1 1 1 1
1 0 0 0 0
1 0 0 1 1
1 0 1 0 0
1 0 1 1 1
1 1 0 0 1
1 1 0 1 1
1 1 1 0 0
1 1 1 1 1
“1” if car is permitted to use pool today
W is 1 if today is a weekday.
O is 1 if there are two or more occupants
S is 1 if the vehicle is an SUV,
H is 1 if the vehicle is a hybrid

## Slide 72
ECOTOPIA REVISITED
“1” if car is permitted to use pool today
W is 1 if today is a weekday.
O is 1 if there are two or more occupants
S is 1 if the vehicle is an SUV,
H is 1 if the vehicle is a hybrid
Car is permitted to use pool if it is a hybrid or it is not a hybrid and it is not a weekday or it is not a hybrid and there are more than two occupants

## Slide 73: Circuits with Multiple Outputs Product Term Sharing

## Slide 74: Circuits with Multiple Outputs Product Term Sharing
x1
x2
x3
x4
f1
f2
This is SOP

## Slide 75: Product Term Sharing
May Result in K-Maps Different from Optimizing Separate Functions

## Slide 76: Look for Shared Terms
AB
01
0
0
0
0
00
CD
00
0
0
0
0
01
11
10
1
0
1
0
1
1
1
0
11
10
F1 = m(11,12,13,14,15) = AB + ACD
AB
01
0
0
0
0
00
00
1
1
0
0
01
11
10
1
0
1
0
1
1
0
0
11
10
F2= m(3,7,11,12,13,15) = A’CD + ABC’ + ACD
AB
01
0
0
0
0
00
CD
00
1
1
0
0
01
11
10
1
0
1
0
1
0
1
0
11
10
F3= m(3,7,12,13,14,15) = A’CD+AB
Minimize separately

## Slide 77: Implementation with Shared Terms
A
B
A
C
D
A
B
C’
A’
C
D
F1 = AB + ACD
F2= A’CD + ABC’ + ACD
F3= A’CD+AB

## Slide 78: Design example: two-bit comparator
we'll need a 4-variable Karnaugh map for each of the 3 output functions
block diagram
LT EQ GT
A B < C D A B = C D A B > C D
A
B
C
D
N1
N2
A B C D LT EQ GT
0 0 0 0 0 1 0
0 1 1 0 0
1 0 1 0 0
1 1 1 0 0
0 1 0 0 0 0 1
0 1 0 1 0
1 0 1 0 0
1 1 1 0 0
1 0 0 0 0 0 1
0 1 0 0 1
1 0 0 1 0
1 1 1 0 0
1 1 0 0 0 0 1
0 1 0 0 1
1 0 0 0 1
1 1 0 1 0
and
truth table

## Slide 79: Design example: two-bit comparator (cont’d)
A' B' D + A' C + B' C D
B C' D' + A C' + A B D'
LT =
EQ =
GT =
K-map for EQ
K-map for LT
K-map for GT
0 0
1 0
0 0
0 0
D
A
1 1
1 1
0 1
0 0
B
C
1 0
0 1
0 0
0 0
D
A
0 0
0 0
1 0
0 1
B
C
0 1
0 0
1 1
1 1
D
A
0 0
0 0
0 0
1 0
B
C
= (A xnor C) • (B xnor D)
LT and GT are similar (flip A/C and B/D)
A' B' C' D' + A' B C' D + A B C D + A B' C D’
EQ =
Another variant that can be extended to any size comparator

## Slide 80: Design example: two-bit comparator (cont’d)
two alternative
implementations of EQ
with and without XOR
XNOR is implemented with at least 3 simple gates
A B C D
EQ
EQ

## Slide 81: Another solution to this problem
A' B' D + A' C + B' C D
B C' D' + A C' + A B D'
LT =
EQ =
GT =
K-map for EQ
K-map for LT
K-map for GT
0 0
1 0
0 0
0 0
D
A
1 1
1 1
0 1
0 0
B
C
0 1
1 0
1 1
1 1
D
A
1 1
1 1
0 1
1 0
B
C
0 1
0 0
1 1
1 1
D
A
0 0
0 0
0 0
1 0
B
C
= (A xnor C) • (B xnor D)
LT and GT are similar (flip A/C and B/D)
A' B' C' D' + A' B C' D + A B C D + A B' C D’
EQ =
Another variant that can be extended to any size comparator
Free groups from here
Free groups from here

## Slide 82: Another solution to this problem
A' B' D + A' C + B' C D
B C' D' + A C' + A B D'
LT =
EQ =
GT =
K-map for EQ
K-map for LT
K-map for GT
0 0
1 0
0 0
0 0
D
A
1 1
1 1
0 1
0 0
B
C
0 1
1 0
1 1
1 1
D
A
1 1
1 1
0 1
1 0
B
C
0 1
0 0
1 1
1 1
D
A
0 0
0 0
0 0
1 0
B
C
A' B' C' D' + A' B C' D + A B C D + A B' C D’
Free groups from here
Free groups from here
LT
A B C D
LT
GT
A B C D
GT
EQ
Better than previous solutions
From Kmap
From Kmap

## Slide 83: Design example: 2x2-bit multiplier
block diagram
and
truth table
4-variable K-map
for each of the 4
output functions
A2 A1 B2 B1 P8 P4 P2 P1
0 0 0 0 0 0 0 0
0 1 0 0 0 0
1 0 0 0 0 0
1 1 0 0 0 0
0 1 0 0 0 0 0 0
0 1 0 0 0 1
1 0 0 0 1 0
1 1 0 0 1 1
1 0 0 0 0 0 0 0
0 1 0 0 1 0
1 0 0 1 0 0
1 1 0 1 1 0
1 1 0 0 0 0 0 0
0 1 0 0 1 1 1 0 0 1 1 0
1 1 1 0 0 1
P1
P2 P4
P8
A1
A2 B1
B2

## Slide 84: Design example: 2x2-bit multiplier (cont’d)
K-map for P8
K-map for P4
K-map for P2
K-map for P1
0 0
0 0
0 0
0 0
B1
A2
0 0
0 0
0 1
1 1
A1
B2
0 0
0 1
0 0
1 0
B1
A2
0 1
0 0
1 0
0 0
A1
B2
0 0
0 0
0 0
1 1
B1
A2
0 1
0 1
0 1
1 0
A1
B2
0 0
0 0
0 0
0 0
B1
A2
0 0
0 0
1 0
0 0
A1
B2
P8 = A2A1B2B1
P4 = A2B2B1' + A2A1'B2
P2 = A2'A1B2 + A1B2B1' + A2B2'B1 + A2A1'B1
P1 = A1B1

## Slide 85: Design example: BCD increment by 1
I8 I4 I2 I1 O8 O4 O2 O1 0 0 0 0 0 0 0 1
0 0 0 1 0 0 1 0
0 0 1 0 0 0 1 1
0 0 1 1 0 1 0 0
0 1 0 0 0 1 0 1
0 1 0 1 0 1 1 0
0 1 1 0 0 1 1 1
0 1 1 1 1 0 0 0
1 0 0 0 1 0 0 1
1 0 0 1 0 0 0 0
1 0 1 0 X X X X
1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
block diagram
and
truth table
4-variable K-map for each of the 4 output functions
O1
O2 O4
O8
I1
I2 I4
I8

## Slide 86: Design example: BCD increment by 1 (cont’d)
O8 = I4 I2 I1 + I8 I1'
O4 = I4 I2' + I4 I1' + I4’ I2 I1 O2 = I8’ I2’ I1 + I2 I1'
O1 = I1'
O8
O4
O2
O1
0 0
0 0
X 1
X 0
I1
I8
0 1
0 0
X X
X X
I4
I2
0 0
1 1
X 0
X 0
I1
I8
0 0
1 1
X X
X X
I4
I2
0 1
0 1
X 0
X 0
I1
I8
1 0
0 1
X X
X X
I4
I2
1 1
0 0
X 1
X 0
I1
I8
0 0
1 1
X X
X X
I4
I2

## Slide 87: K-Maps: Caveats!
Empty K-Map must be constructed correctly
  Gray Code: Adjacent cells differ in only one variable
K-Map must be plotted correctly
  Minterms from truth table or compact form
  Minterms from partially reduced expressions
K-Map must be circled correctly
  Start with smallest cubes first!
  Remember that K-Maps “wrap” at edges
Use 1s for F, 0s for F

## Slide 88: Short List of Rules for Exor Logic
A  A = 0
A  A’ = 1
A  1=A’
A’  1=A
A  0=A
A  B= B  A
A B = B A
A(B  C) = AB  AC
A+B = A  B  AB
A+B = A  B when AB = 0
A  (B  C) = (A  B)  C
(A B) C = A (B C)
A+B = A  B  AB =
A B(1  A) = A  BA’
These rules are sufficient to minimize Exclusive Sum of Product expression for small number of variables
We will use these rules in the class for all kinds of reversible, quantum, optical, etc. logic. Try to remember them or put them to your “creepsheet”.

## Slide 89: Chess Patterns
W
Y
1 1
1 1
1 1
1 1
0 0
0 0
WY
WX  Y  Z
1 0 1 0
1 0 1 0
1 0 1 0
0 1 0 1
0 1 0 1

## Slide 90: Chess Patterns
Y Z
1 1 1 1
1 0 1 0
0 1
0 0 0 0
0 1
WX
WX  Y  Z
1 0 1 0
1 0 1 0
1 0 1 0
0 1 0 1
0 1 0 1
WX  Y  Z  1
1 0 1 0
0 1 0 1
0 1 0 1
0 1 0 1
0 1 0 1
0 1 0 1
1 1 1 1
0 0 0 0

## Slide 91: Chess Patterns for functions of 5 variables
01
00
DE
00
01
11
10
11
10
AB
11
00
DE
10
01
11
10
01
00
AB
mirror
001
1
0
1
0
00
CDE
000
1
0
1
0
01
11
10
1
0
1
0
1
0
1
0
011
010
AB
111
0
1
0
1
110
0
1
0
1
0
1
0
1
0
1
0
1
101
100
E
D
D  E

## Slide 92: EXOR Patterns
0 1 0 0
WX Y
1 1 1 1
1 1 0 1
0 0
0 0 0 0
1 0
WX
0 1 0 0
1 0 1 1
0 1 0 0
0 1 0 0
WX  YZ
0 0 1 0
0 0 1 0
0 0 1 1
0 0 1 1
1 1 0 0
0 0 1 1
1 1 1 1
0 0 0 0
W X  Y Z

## Slide 93: Example of Application in Quantum Computing

## Slide 94
Use of Toffoli Gate
x1x2w
x1x2w  x1x2
(x1x2w)x3 y
(x1x2w)x3 y  wx3

## Slide 95: Example of Application in Robotics

## Slide 96: Another Example: Braitenberg Vehicles and Quantum BV

## Slide 97: Braitenberg Vehicles

## Slide 98: Braitenberg Vehicles
Instead of only analog components we can have binary components such as logic gates and circuits.
We can use analog-to-digital converters for sensors and digital-to-analog converters for motors and lights.

## Slide 99
Essence of logic synthesis approach to learning

## Slide 100: Example of Logical Synthesis in Machine Learning
John
Dave
Mark
Jim
Alan
Nick
Mate
Robert

## Slide 101
A - size of hair
C - size of beard
D - color of eyes
B - size of nose
Dave
Jim
John
Mark
Good guys
Alan
Nick
Mate
Robert
Bad guys

## Slide 102
Good guys
John
Mark
Dave
Jim
C - size of beard
D - color of eyes
A - size of hair
B - size of nose
A’ BCD
A’ BCD’
A’ B’CD
A’ B’CD
00
01
11
10
00
-
1
-
01
–
1
1
11
-
–
-
-
10
-
-
-
-
AB
CD
-
-

## Slide 103
C - size of beard
D - color of eyes
A - size of hair
B - size of nose
A’ BC’D’
AB’C’D
ABCD
A’ B’C’D
00
01
11
10
00
-
1
-
01
0
1
1
11
-
–
0
-
10
-
0
-
-
AB
CD
-
0
Alan
Nick
Mate
Robert
Bad guys
A’C

## Slide 104
C - size of beard
D - color of eyes
A - size of hair
B - size of nose
00
01
11
10
00
-
1
-
01
0
1
1
11
-
–
0
-
10
-
0
-
-
AB
CD
-
0
A’C
Generalization 1:
Bald guys with beards are good
Generalization 2:
All other guys are no good

## Slide 105: Example of Application in Machine Learning: Decision Trees

## Slide 106
a=0
a=1
c=1
c=0
1
0
Using Kmaps to illustrate cofactoring or splitting
a*c
c=1
c=0
1
a*c
b=1
b=0
0
a*c
d
*b*d
THIS METHOD ASSUMES NO PRUNNING
The same as
a*c
a*c
+
SOLUTION
a*c
*b*d
+

## Slide 107
a=0
a=1
c=1
c=0
1
0
Using Kmaps to illustrate cofactoring or splitting
a*c
c=1
c=0
1
a*c
0
a*c
*b*d
THIS METHOD ASSUMES PRUNNING when there is more ones than zeros in a cofactor group or more zeros than ones
The same as
In this cofactor a*c we have more zeros than ones so we prune to constant 0
+
SOLUTION

## Slide 108: Conclusion on Prunning
a*c
a*c
+
SOLUTION without PRUNNING
a*c
*b*d
+
a*c
a*c
+
SOLUTION with PRUNNING
These are two different functions.
PRUNNING OR NO PRUNNING CAN LEAD TO OVERFITTING

## Slide 109: PROJECT EXAMPLE Full Adder in VERILOG
YOU WILL HAVE A PROJECT

## Slide 110: Various specifications of combinational circuits
Schematic of a circuit
Truth Table
Karnaugh Map
Natural Language Specification
Verilog Code
Hypercube
Logic Equations

## Slide 111: Verilog Dataflow Example: Full Adder
CI A B CO S
0 0 0 0 0
0 0 1 0 1
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 1

## Slide 112: Verilog Structural Example: Full Adder

## Slide 113: Verilog Structural Example: Full Adder

## Slide 114: COLLECTION OF PROBLEMS FOR MIDTERM (with partial solutions)

## Slide 115: Problem 1: Minimize Function F as SOP
Given is function from Fig. 3.17.
Synthesize minimum SOP and draw the circuit.

## Slide 116
f’ = z’ + wy’ Complement of f
f = z(w’ + y) Product of Sums
f = w’z + yz Sum of Products
Problem 2: Minimize Function F as POS
Given is function from Figure above.
Synthesize minimum POS and draw the circuit.
f = w’x’ + yz
Another sum of products
In this example there are two solutions for SOP with the same cost of literals. Cost of inputs to gates is different.

## Slide 117: NAND Implementations of AND, OR, and NOT Gates
NOT Gate
AND Gate
OR Gate
x
x
x
y
y
f
f
f
f = x’
f = ((xy)’)’ = xy
f = (x’y’)’ = x + y
Problem 3: Realize NOT , AND and OR functions using only NAND gates.
Draw schematics of circuits realizing NOT, AND and OR Gates using only NAND gates.
Repeat this problem using only logic operators that realize function f=x’a + xb

## Slide 118: NOR Implementations of AND, OR, and NOT Gates
x
x
y
x
y
f
f
f
NOT Gate
AND Gate
OR Gate
f = x’
f = (x’ + y’)’ = xy
f = ((x + y)’)’ = x + y
Problem 4: Realize NOT, OR and AND functions using NOR gates only
Draw schematics of circuits realizing NOT, AND and OR Gates using only NOR gates.
Repeat this problem using only logic operators that realize function f = (x’+a) * (x+b)

## Slide 119
XOR gates have the following interesting properties:
x  0 = x
x  1 = x’
x  x = 0
x  x’ = 1
x  y’ = x’  y = (x  y)’
x  y = y  x
x  y  z = (x  y)  z = x  (y  z)
Problem 5: Write basic logic formulas related to EXOR gate
Write formulas for exor of x and 0, x and 1 and other similar formulas for EXOR gate.
Prove that they are true using truth tables.

## Slide 120: Two-Input XOR Implementation Using AND, OR, and NOT Gates
x
y
x  y
Problem 6: Draw schematics of EXOR gate from AND, OR and NOT gates
Draw logic diagram for EXOR gate using AND, OR and NOT gates. There are several solutions not shown above.

## Slide 121: Two-Input XOR Implementation Using NAND Gates
x
y
x  y
Problem 7: Realize EXOR gate using only four NAND gates and no other gates.
Draw logic diagram for EXOR gate using only four NAND gates.
How many NOR gates you need to realize EXOR? Try to minimize this circuit.

## Slide 122
Problem 8: Minimize Parity functions of 4 variables
Using the truth tables of parity functions from the left, realize both of them in a circuit with minimum number of arbitrary gates AND, OR, EXOR and NOT

## Slide 123: Karnaugh Maps for Four-Input XOR and XNOR Gates
Realize these maps with the minimum number of EXOR gates and no other gates.
You may use constants.

## Slide 124: Example of XOR Extraction
Given a Boolean function f, is it possible to simplify this complex sum of products function using XOR and XNOR gates?
Consider the following Karnaugh Map:
NOTE:
This Boolean function uses six terms in sum of products form.
Problem 9: Minimize Function using only two EXOR, one NOT and one AND gates
Realize these maps with the minimum number of EXOR, AND and NOT gates and no other gates. You may use constants.
Draw the schematic.

## Slide 125: Example of XOR Extraction
XNOR
XOR

## Slide 126: Example of XNOR Extraction
Simplifying…
Arguably, this simplified expression using two XOR gates will require fewer total gates to implement the function

## Slide 127: Example of Reuse of Intermediate Nodes
Consider the following functions f1 and f2:
f1 = x + y
f2 = xz + yz = (x + y)z
A more advanced solution is the following:
x
y
z
f2
f1
Problem 10: Realize functions f1 and f2 from equations below using minimum number of gates AND and OR
Realize functions f1 and f2 using only AND and OR gates.
Repeat this problem using only NAND gates.
Repeat this these problem using only NOR gates.
Draw the schemata.

## Slide 128: Example of Analyzing a Combinational Circuit
NOTE:
Step 1 adds labels T1, T2, T4, T5, and T6 to to the diagram.
Step 2 is repeated to label F2, F’2, T3, and F1 in order.
Step 4 is performed to find the Boolean functions in terms of inputs.
T4
T5
T6
Problem 11: Analyze the function from the circuit given below

## Slide 129: Determining the Boolean Functions
The combinational circuit on the previous slide contains two outputs that need to be expressed as Boolean functions of the three inputs
To express these functions, Boolean functions for each intermediate node (T1, T2, T3, T4, T5, T6, and F’2) must be determined

## Slide 130: Determining the Boolean Functions for Each Logic Gate
F1 = T2T3
F2 = T4 + T5 + T6
T1 = A + B + C
T2 = ABC
T3 = T1F’2
T4 = AB
T5 = AC
T6 = BC
F’2 = (F2)’

## Slide 131: Determining the Boolean Function for F1
F1 = T2 + T3
= ABC + T1F’2
= ABC + (A + B + C)(F2)’
= ABC + (A + B + C)(T4 + T5 + T6)’
= ABC + (A + B + C)(AB + AC + BC)’
= ABC + (A + B + C)(A’ + B’)(A’ + C’)(B’ + C’)
= ABC + (A’B + A’C + AB’ + B’C)(A’B’ + B’C’ + A’C’)
= ABC + A’B’C + A’BC’ + AB’C’

## Slide 132: Determining the Boolean Function for F2
F2 =T4 + T5 + T6
= AB + AC + BC
Question:
What combinational circuit is shown in this example?
Answer:
The combinational circuit implements a 1-bit full adder:
  A and B are single-bit inputs and C is the carry-in
  F1 is the sum and F2 is the carry-out

## Slide 133: Full Adder Truth Table
A full adder circuit performs 1-bit addition
The truth table shown to the right describes a 1-bit addition circuit
The inputs to the circuit are A, B, and C (carry-in)
The outputs of the circuit are F1 (sum) and F2 (carry-out)
A | B | C | F1 | F2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Problem 11: Draw truth table of a full adder
Draw the truth table.
Using the truth table, draw a Kmap.
Using Kmap, find the realization using the minimum number of EXOR gates and other gates such as NOT, AND and OR.
Draw the schemata.
Repeat this problem using only NAND gates.
Repeat this these problem using only NOR gates.
Draw the schemata.

## Slide 134: Textbook Example
Design a combinational circuit to convert from BCD code to Excess-3 code
Step 1: Determine the inputs and outputs of the circuit
  Four inputs labelled A, B, C, and D
  Four outputs labelled w, x, y, and z
  The label names were chosen arbitrarily in this case
Problem 12: Convert from BCD code to Excess-3 code

## Slide 135: Step 2: Truth Table
Input BCD Code |  |  |  | Output Excess-3 Code |  |  | 
A | B | C | D | w | x | y | z
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0

## Slide 136: Step 3: Boolean Simplification

## Slide 137: Step 4: Logic Diagram

## Slide 138: Problem 13. Design of The Half Adder and Full Adder
A | B | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Half Adder
(HA)
B
A
C
S
NOTE:
From the truth table, it can be seen that S = A  B and C = AB
Design full adder from half adders and in other variant directly.

## Slide 139: Implementations of the Half Adder
Implementation 1
S = AB’ + A’B
C = AB
Implementation 2
S = A  B
C = AB
A
A’
A
B’
B
B
B
S
C
S
C
A
B
A
B

## Slide 140: The Full Adder
Ai | Bi | Ci | Ci+1 | Si
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
(FA)
Bi
Ai
Ci
Ci+1
Si

## Slide 141: The Full Adder
Recall that a full adder can be built as follows:
NOTE:
Ai = A
Bi = B
Ci = C
Si = F1
Ci+1 = F2

## Slide 142: The Full Adder
Ai | Bi | Ci | Ci+1 | Si
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Half Adder
(HA)
Bi
Ai
Ci+1
Si
Half Adder
(HA)
Ci
However, the full adder can also be built as follows:

## Slide 143: Questions and EXAM Problems (1)
Explain how to derive Boolean Equations from a Truth Table.
Explain how to derive Boolean Equations from a circuit schematic.
What are minterms.
How to obtain an equation based on minterms from a Truth Table?
How to obtain a circuit based on minterms?
What is SOP form?
What is POS form?
Write an equation for a function that is not in POS and not in SOP form. Show circuit.
What are maxterms? How they are used in logic synthesis?
Generalized Compact Minterm Form, give examples.
Generalized Compact Maxterm Form, give examples.
Draw Kmap for a function of two variables in two different ways.
Draw Kmap for a function of three variables in two different ways.
Draw Kmap for a function of four variables in two different ways.
Draw Kmap for a function of five variables in two different ways.

## Slide 144: Questions and EXAM Problems (2)
16. What is an Implicant? How to find it on Kmap?
17. What is a Prime Implicant. How to find it on Kmap?
18. What is an Essential Prime Implicant. How to find it on Kmap?
19. What is Optional Prime Implicant. How to find it on Kmap?
20. What is Redundant (Non-Essential) Prime Implicant. How to find it on Kmap?
21. Give example of a function that is composed only from essential prime implicants.
22. Give example of a function in which the largest prime implicant will be not included in the minimal solution.
23. What is a don’t care? What is an incompletely specified function?
24. Give example of POS circuit with term sharing.

## Slide 145: Questions and EXAM Problems (3)
25. What are chess patterns?
26. Show chess pattern ab on Kmap of three variables and next on Kmap of 4 variables.
27. Show chess pattern ab on Kmap of 5 variables.
28. Show chess pattern ab  c on Kmap of 5 variables.
29. What are exor patterns?
30. Show exor pattern aebc  d on Kmap of 5 variables.
31. Show exor pattern a  eb  c  ad on Kmap of 5 variables.

## Slide 146: EXOR Patterns
0 0
0 0 0 0
1 0
1 0 1 0
1 0 1 0
1 0 1 0
0 1 1 1
0 1 0 1
0 0 1 0
0 1 0 0
1 0 0 1
0 0 1 0
0 0 0 1
1 0 1 0
1 1 0 0
0 0 1 1
Questions and EXAM Problems (4)
Minimize functions above using only EXOR and AND gates and literals.
0 0 0 0
1 0 1 1

## Slide 147: Challenge Problems for ambitious students
Problem 1. Express function AB+CD+A’C using only EXORs and AND gates
Problem 2. Prove that
(A+B)’ = A  B  AB 1
Problem 3 . Prove that A+B = A  B when AB = 0 without using Kmaps or truth tables.
Problem 4. Given are three functions of three inputs:
A = NOT(a), B = NOT(b), C = NOT(c).
You have only two inverters. You can have an arbitrary large set of two-input AND and OR gates.
Realize these three functions with the gates that you have at your disposal. You cannot use other gates. You can use only two inverters. Draw the schematic of the solution

## Slide 148: Sources
Prof. Mark G. Faust
John Wakerly
Caetano Boriello
Morris Mano