## Slide 1: Lecture 6
Topics
  Combinational Logic Circuits
    Graphic Symbols (IEEE and IEC)
    Switching Circuits
    Analyzing IC Logic Circuits
    Designing IC Logic Circuits
    Detailed Schematic Diagrams
    Using Equivalent Symbols

## Slide 2: Combinational Logic Circuits
Combinational Logic
  Outputs depend only upon the current inputs (not previous “state”)
Positive Logic
  High voltage (H) represents logic 1 (“True”)
  “Signal BusGrant is asserted High”
Negative Logic
  Low voltage (L) represents logic 1 (“True”)
  “Signal BusRequest# is asserted Low”

## Slide 3: Graphic Symbols

## Slide 4
IEEE: Institute of Electrical
and Electronics Engineers
IEC: International Electro-
technical Commission

## Slide 7: Pass Logic versus Regenerative Logic

## Slide 8
n.o. = normally open
n.c. = normally closed
These regenerative logic switching circuits that we’ll be seeing are actually very close to the way real CMOS ICs are implemented and can be a useful model for us without getting into the details of how the transistors actually work.
In particular, note the voltage differential and direction of current flow!
OR gate using Pass Logic and using Regenerative Logic

## Slide 9
AND gate using Pass Logic and using Regenerative Logic
n.o. = normally open
n.c. = normally closed

## Slide 10
NOT gate using Pass Logic and using Regenerative Logic
n.o. = normally open
n.c. = normally closed

## Slide 11
NOR gate using Pass Logic and using Regenerative Logic
n.o. = normally open
n.c. = normally closed

## Slide 12
NAND gate using Pass Logic and using Regenerative Logic
n.o. = normally open
n.c. = normally closed

## Slide 13
Buffer gate using Pass Logic and using Regenerative Logic
n.o. = normally open
n.c. = normally closed

## Slide 14
XOR gate using Pass Logic and using Regenerative Logic
n.o. = normally open
n.c. = normally closed

## Slide 15
XNOR gate using Pass Logic and using Regenerative Logic
n.o. = normally open
n.c. = normally closed

## Slide 16: All Possible Two-Variable Functions

## Slide 17: All Possible Two Variable Functions
Question: How many unique functions of two
variables are there?
Recall earlier question…

## Slide 18: Truth Tables
B5 B4 B3 B2 B1 B0 F
0 0 0 0 0 0 0
0 0 0 0 0 1 1
0 0 0 0 1 0 1
0 0 0 0 1 1 0
.
.
.
1 1 1 1 1 1 1
0
1
2
3
.
.
.
63
26 = 64
Question: How many rows are there in a truth table
for n variables?
As many rows as unique combinations
of inputs
Enumerate by counting in binary
2n

## Slide 19: Two Variable Functions
Question: How many unique combinations of 2n bits?
Enumerate by counting in binary
2
2
n
264
B5 B4 B3 B2 B1 B0 F
0 0 0 0 0 0 0
0 0 0 0 0 1 1
0 0 0 0 1 0 1
0 0 0 0 1 1 0
.
.
.
1 1 1 1 1 1 1
0
1
2
3
.
.
.
63
26 = 64
Notes: Just as we enumerated the number of rows in the truth table by “counting” in binary, we can enumerate all the unique possible functions by “counting” the vector’s possible values in binary.

## Slide 20: All Possible Two Variable Functions
Question: How many unique functions of two
variables are there?
B1 B0 F
0 0 0
0 1 1
1 0 1
1 1 0
22 = 4 rows
4 bits
Number of unique 4 bit words = 24 = 16

## Slide 22: Analyzing Logic Circuits

## Slide 23: Analyzing Logic Circuits
Reference Designators (“Instances”)
X + Z
X
X + Y
(X + Y)×(X + Z)

## Slide 24: Analyzing Logic Circuits
C
A×B
B×C
A×B + B×C

## Slide 25: Another example

## Slide 26: Designing Logic Circuits

## Slide 27: Designing Logic Circuits
F1 = A×B×C + B×C + A×B
SOP form with 3 terms  3 input OR gate

## Slide 28: Designing Logic Circuits
F1 = A×B×C + B×C + A×B
Complement already available

## Slide 29: Some Terminology
F1 = A×B×C + B×C + A×B
Signal line – any “wire” to a gate input or output

## Slide 30: Some Terminology
F1 = A×B×C + B×C + A×B
Net – collection of signal lines which are connected

## Slide 31: Some Terminology
F1 = A×B×C + B×C + A×B
Fan-out – Number of inputs an IC output is driving
Fan-out of 2
Notes: Book confused “fan-out” with “maximum fan-out”

## Slide 32: Some Terminology
F1 = A×B×C + B×C + A×B
Fan-in – Number of inputs to a gate
Fan-in of 3
Book confused “fan-out” with “maximum fan-out”

## Slide 33: Vertical Layout Scheme – SOP Form

## Slide 34: Vertical Layout Scheme – SOP Form

## Slide 35: >2 Input OR Gates Not Available for all IC Technologies
Solution: “Cascading” gates

## Slide 36: Vertical Layout Scheme – POS Form
F2 = (X+Y)×(X+Y)×(X+Z)

## Slide 37: Designing Using DeMorgan Equivalents
Often prefer NAND/NOR to AND/OR when using real ICs
  NAND/NOR typically have more fan-in
  NAND/NOR “functionally complete”
  NAND/NOR usually faster than AND/OR

## Slide 38: NAND and NOR gates

## Slide 39: AND/OR forms of NAND
DeMorgan’s Theorem

## Slide 40: Summary of AND/OR forms
Change OR to AND
“Complement” bubbles

## Slide 41: Equivalent Signal Lines

## Slide 42: NAND/NAND Example

## Slide 43: NOR/NOR Example

## Slide 45: Few more advanced topics

## Slide 46: Duality
Swap 0 & 1, AND & OR
  Result: Theorems still true
Why?
  Each axiom (A1-A5) has a dual (A1¢-A5¢)
Counterexample: X + X × Y = X (T9) X × X + Y = X (dual) X + Y = X (T3¢) ????????????
X + (X × Y) = X (T9) X × (X + Y) = X (dual) (X × X) + (X × Y) = X (T8) X + (X × Y) = X (T3¢)
parentheses, operator precedence!

## Slide 47: N-variable Theorems
Prove using finite induction
Most important: DeMorgan theorems

## Slide 48: DeMorgan Symbol Equivalence

## Slide 49: Likewise for OR
(be sure to check errata!)

## Slide 50: DeMorgan Symbols

## Slide 51: Three Methods of analysis of combinational Circuits

## Slide 52: Combinational analysis

## Slide 53: Signal expressions
Multiply out: F = ((X + Y¢) × Z) + (X¢ × Y × Z¢) = (X × Z) + (Y¢ × Z) + (X¢ × Y × Z¢)

## Slide 54: Signal Kmaps
X’
1
Y’
1
1
1
1
1
1 1 1 1
1 1
1 1
1 1
1
1 1
1
1 1
1 1
You perform Boolean operations on the whole Kmaps.
OR-ing Kmaps

## Slide 55: New circuit, same function

## Slide 56: “Add out” logic function
Circuit:

## Slide 57: Shortcut: Symbol substitution

## Slide 58: Different circuit, same function

## Slide 59: Verification of solutions

## Slide 60: Verification of your solutions helps you in most cases to avoid errors
Circuit
Logic Expression
Truth Table
Karnaugh Map
Optimized Logic Expression
Optimized Circuit with AND , OR and NOT gates
Optimized Circuit with NAND , NOR and NOT gates
SYNTHESIS PROCESS

## Slide 61: Verification of your solution is a reverse process
Circuit
Logic Expression
Truth Table
Karnaugh Map
Optimized Logic Expression
Optimized Circuit with AND , OR and NOT gates
Optimized Circuit with NAND , NOR and NOT gates
BLUE ARROWS ARE SYNTHESIS PROCESS
RED ARROWS ARE VERIFICATION PROCESS

## Slide 62: Practical Example of Verification of a solution

## Slide 63
1 1
1 1
Given is an expression Z  X’Y.
1. Draw a Kmap.
2. Given the Karnaugh Map find circuit from AND, OR and NOT gates.
1 1
1 1
1 1
1 1
You find SOP = X’YZ’ + XZ + Y’Z
You factorize SOP = X’YZ’ + Z(X + Y’) and get the circuit below.
SYNTHESIS

## Slide 64
X’
1
Y’
1
1
1
1
1
1 1 1 1
1 1
1 1
1 1
1
1 1
1
1 1
1 1
You perform Boolean operations on the whole Kmaps.
OR-ing Kmaps
VERIFICATION
1. You start from circuit
2. You write equation for each gate
Verification Method 1
Other verification Method 2 uses Kmaps for each gate. The result is a Kmap.

## Slide 65: Verification of your solution is a reverse process to synthesis
Circuit
Logic Expression
Karnaugh Map
Optimized Logic Expression
Optimized Circuit with AND , OR and NOT gates
Optimized Circuit with NAND , NOR and NOT gates
RED ARROWS ARE VERIFICATION METHODS
Verification Method 1 created the expression for F
Verification Method 2 created the Kmap for F
Truth Table
If required you create Truth Table from KMap
If required you create logic equation of given style from KMap
If required you create logic circuit of given style from KMap

## Slide 66: You will increase your exam, quizz or homework scores if you will verify your solutions

## Slide 67
Perkowski says, based on his own experience:
Clever Engineer verifies his/her solutions before showing them to her/his boss

## Slide 68
Stupid Engineer does NOT verify his/her solutions before showing them to her/his boss and gets into troubles

## Slide 69: Questions and Exam Problems(1)
Draw and explain OR gate in pass transistor logic.
Draw and explain AND gate in pass transistor logic.
Draw and explain NOT gate in pass transistor logic. Draw and explain XOR gate in pass transistor logic.
Draw and explain NAND gate in pass transistor logic.
Draw and explain NOR gate in pass transistor logic.
Draw and explain OR gate in regenerative logic.
Draw and explain AND gate in regenerative logic.
Draw and explain NOT gate in regenerative logic.
Draw and explain XOR gate in regenerative logic.
Draw and explain NAND gate in regenerative logic.
Draw and explain NOR gate in regenerative logic.
Difficult: how to realize all functions of two variables using multiplexers? How many MUX you need? What size?

## Slide 70: Questions and EXAM Problems (2)
13. How to analyze SOP circuits?
14. How to analyze POS circuits?
15. How to verify your solutions to combinational logic circuits?
16. How to analyze arbitrary circuits with NAND,NOR and other gates and many levels?
17. How to realize SOP with NANDs?
18. How to realize SOP with NORs?
19. How to realize POS with NANDs?
20. How to realize POS with NORs?
21. How to realize arbitrary logic circuit (schematics) with NANDs?
22. Show example of sharing subfunctions in a circuit that has only NAND gates.
23. Show example of sharing subfunctions in a circuit that has only NOR gates.
24. How to realize a circuit with AND, OR, NOT and EXOR operations using only NAND gates?
25. How to realize a circuit with AND, OR, NOT and EXOR operators using only XNOR and NAND gates?

## Slide 71: Solution to the very difficult problem
Supposedly solved by 4 students in 2014

## Slide 72
ROLE OF INVERTERS IN MULTI-LEVEL CIRCUITS AND THE TWO-INVERTER PROBLEM”.
Before we proceed to synthesis with NAND and IMPLY gates let us consider the importance of negation in multi-output combinational logic. We solve the famous 2-Inverter problem.
Problem Formulation. Assume that inverter is very expensive and AND and OR gates are for free. Given are two inverters only and an unlimited number of AND and OR gates. Synthesize a three-output function: FA = A’, FB = B’, FC = C’ using only these gates.
The reader is asked not to look to the solution below and try to solve this problem by himself.
This problem is truly difficult and takes much time even from smart students. However, creating systematically Karnaugh Maps for all available functions allows to find a solution as in Figure 11.2.1. Thus we find:
FA = A’ = Z’(B+C) + Z’F’ + F’(BC),
FB = B’ = Z’(A+C) + Z’F’ + F’(AC),
FC = C’ = Z’(A+B) + Z’F’ + F’(AB)
A question however arrives: “how the intermediate functions in Figure 11.2.1 were selected, as we can easily see that there are many more functions that can be created using two inverters and unlimited number of AND and ORs?” One answer is = “use symmetry, because problem is symmetric”. But a better answer is to use the concept of “dissected pairs” which will be introduced below for practical synthesis with the minimum (or reduced) number of inverters.
One more question to the reader: “how to best generalize our results from Figure 11.2.1 above?” Getting some intuitions while solving this problem will help much the reader to understand methods from this and next chapters.

## Slide 73
Figure 11.2.1. Step by step solution to the “two inverter problem”.
FA = A’ = Z’(B+C) + Z’F’ + F’(BC),
FB = B’ = Z’(A+C) + Z’F’ + F’(AC),
FC = C’ = Z’(A+B) + Z’F’ + F’(AB)

## Slide 74
A B
FA = A’ = Z’(B+C) + Z’F’ + F’(BC),
FB = B’ = Z’(A+C) + Z’F’ + F’(AC),
FC = C’ = Z’(A+B) + Z’F’ + F’(AB)
A C
B C
Z
B C
A C
A B
Z’(B+C)
Z’(A+C)
Z’(A+B)
AB C
F
FA
FB
FC

## Slide 75: Sources
Prof. Mark G. Faust
John Wakerly