## Slide 1: Lecture 13
Topics
  Latches
  Flip Flops
  Algorithmic State Machines

## Slide 2: Latches

## Slide 3: Possible States for Light Switch

## Slide 4: S-R Latch
S R Q+
0 0 Q
0 1 0
1 0 1
1 1 0
S-R latch is reset dominant
Different ways to name/nomenclature for current/next state. Text uses Q+ for next.

## Slide 5: Alternative Nomenclature for latches
Present State Next State
Output Symbol Output Symbol
Q Q
Q Q(t+1)
Qt Q(t+1)
Qn Q(n+1)
Q0 Q
Y Y+
y Y

## Slide 6: S-R Latch States
S-R latch is
reset dominant

## Slide 7: Characteristic Equations for SR latch

## Slide 8: Present State/Next State Table (PS/NS) for SR Latch

## Slide 9: Present State/Next State Table (PS/NS) for SR Latch
Another notation, stable states in circles, I think it is a better notation
Students should be able to analyze and draw transitions in a machine

## Slide 10: Timing Diagram for SR Latch

## Slide 11: Detailed Discussion of Timing Diagram for SR Latch

## Slide 12: Races
Just as we used K-maps to not only reduce Boolean equations but to detect hazards, we can use K-maps to analyze anomalous latch behavior as well.
Race is when two or more inputs change simultaneously.
May or may not be a critical race.
Depends upon the behavior of the circuit.

## Slide 13: Critical Races
Can happen when two signals change at the same time

## Slide 14: Critical Race
We start in State represented by minterm m3. (stable state) Q is 0, SR are 11s.
Both S and R are transitioning to 0.
Notice we take different paths through the K-map depending upon whether R or S transitions first.
If S transitions first, we transition to state m0 where Q+ remains Q (no transitions on output).
However, if R transitions first, we attempt to set the latch, resulting in Q+ = 1.
Then, when S transitions we go to state m4.
Not only do we end up in different states, but we have different values on the Q output – all depending upon minor differences in relative timing between transitions on S/R.
This is a critical race.
Start from here

## Slide 15: Critical Race
Critical Race

## Slide 16: Non-Critical Races

## Slide 17: Non-critical race:
Start in state m6 (stable) with SR 10. Both S and R are going to change.
If S changes first, we go to state m4 (a stable state) with no transition on output.
Then when R changes we transition to state m1, also a stable state, and with an output of 0.
If R changes first, we transition to state m3, a stable state with a transition to 0 on output.
When S subsequently changes we transition to m1, another stable state where Q remains 0.
Non-critical race – OK and correct behavior regardless of which signal transitions first.
Non-critical Race

## Slide 18: Metastable State

## Slide 19: Metastable State
An often overlooked condition in which the output can remain in an illegal (even oscillating) state for an indeterminant period of time.
Metastability can be caused by a runt pulse (a positive or negative pulse which never achieves either a value of a 1 or 0).
  This can occur when two inputs to a gate change near simultaneously (see hazards earlier).
Metastability can also occur when two inputs to a latch change near simultaneously.
Condition also arises when synchronizing with external events (e.g. asynchronous inputs to synchronous finite state machines).

## Slide 20: Bistable element
The simplest sequential circuit
Two states
  One state variable, say, Q
HIGH
Let us set this to High and see what will happen
First we discuss correct behavior of a bistable element

## Slide 21: Bistable element
The simplest sequential circuit
Two states
  One state variable, say, Q
HIGH
LOW

## Slide 22: Bistable element
The simplest sequential circuit
Two states
  One state variable, say, Q
HIGH
LOW
LOW

## Slide 23: Bistable element
The simplest sequential circuit
Two states
  One state variable, say, Q
HIGH
LOW
LOW
HIGH

## Slide 24: Bistable element
The simplest sequential circuit
Two states
  One state variable, say, Q
LOW
Let us set this to Low and see what will happen

## Slide 25: Bistable element
The simplest sequential circuit
Two states
  One state variable, say, Q
LOW
HIGH

## Slide 26: Bistable element
The simplest sequential circuit
Two states
  One state variable, say, Q
LOW
HIGH
HIGH

## Slide 27: Bistable element
The simplest sequential circuit
Two states
  One state variable, say, Q
LOW
HIGH
HIGH
LOW

## Slide 28: Analog analysis
Assume pure CMOS thresholds, 5V rail
Theoretical threshold center is 2.5 V

## Slide 29: Analog analysis
Assume pure CMOS thresholds, 5V rail
Theoretical threshold center is 2.5 V
2.5 V
Now we discuss incorrect behavior of a bistable element

## Slide 30: Analog analysis
Assume pure CMOS thresholds, 5V rail
Theoretical threshold center is 2.5 V
2.5 V
2.5 V

## Slide 31: Analog analysis
Assume pure CMOS thresholds, 5V rail
Theoretical threshold center is 2.5 V
2.5 V
2.5 V
2.5 V

## Slide 32: Analog analysis
Assume pure CMOS thresholds, 5V rail
Theoretical threshold center is 2.5 V
2.5 V
2.5 V
2.5 V
2.5 V

## Slide 37: ANIMATED = Analog analysis
Assume pure CMOS thresholds, 5V rail
Theoretical threshold center is 2.5 V
2.5 V
2.5 V
2.5 V
2.0 V
2.0 V
4.8 V
2.5 V
2.51 V
4.8 V
0.0 V
0.0 V
5.0 V

## Slide 38: Metastability
Metastability is inherent in any bistable circuit
Two stable points, one metastable point
stable
stable

## Slide 39: Another look at metastability

## Slide 40: “sube y baja” behavior

## Slide 41: Why all the harping on metastability?
All real systems are subject to it
  Problems are caused by “asynchronous inputs” that do not meet flip-flop setup and hold times.
  Details in Chapter-7 flip-flop descriptions and in Section 8.9 (later in quarter).
Especially severe in high-speed systems
  since clock periods are so short, “metastability resolution time” can be longer than one clock period.
Many digital designers, products, and companies have been burned by this phenomenom.

## Slide 42: Back to the bistable….
How to control it?
  Screwdriver
  Control inputs
S-R latch
Correct behavior

## Slide 43: S-R latch operation without metastability
Correct behavior

## Slide 44: S-R latch operation with metastability
Metastability is possible if S and R are negated simultaneously.
(try it in Foundation)
44
Correct behavior

## Slide 45: State Machines

## Slide 46: State Diagrams – example of state diagram for an SR Latch
S R Q+
0 0 Q
0 1 0
1 0 1
1 1 0
S R Q Q+
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 0
1 0 0 1
1 0 1 1
1 1 0 0
1 1 1 0

## Slide 47: Algorithmic State Machines (ASM)
false
true
The student should be able to transform state diagram to algorithmic state machine and vice versa

## Slide 48: Clock Circuits

## Slide 49: Clock (Oscillator) Circuit
PS/NS Table
K-map
State Diagram
Delay Model

## Slide 50: Clock Waveforms, T, tp and f
Delay
  Buffers
  Additional (maintain odd number) inverters
  RC circuit
  Crystal Oscillator

## Slide 51: Clock signals
Very important with most sequential circuits
  State variables change state at clock edge.
State changes with leading slope
State changes with falling slope

## Slide 52: Gated Sequential Circuits
Addition of control input
  Gated Latch (Level Activated)
  Edge-Triggered Flip Flop
  Pulse Triggered Flip Flop

## Slide 53: Gated SR Latch

## Slide 54: Gated SR Latch Using NANDs

## Slide 55: Gated D Latch
D Q+
0 0
1 1
D Latch is Hazard Free (product terms chain-linked)

## Slide 56: Timing of a Gated D Latch
Good behavior, signal D was long enough, longer than setup time
tw = pulse width
tsu = setup time
th = hold time
tsi = tsu+th = sampling period
Clock changes to 1
This pulse is too short, FF did not change to stable 1
Length of Signal D was longer than tsi and D=1 included interval tsi
Illustration of correct behavior of Gated D Latch

## Slide 57: Gated D Latch Timing
Good behavior, signal D was long enough, longer than setup time
Bad behavior, signal D was NOT long enough, setup time was violated
Bad behavior, signal D was NOT long enough, hold time was violated
Illustration of two cases of incorrect behavior of
Gated D Latch

## Slide 58: Use of gated D latches as Storage Elements
Tri-state
Tri-state

## Slide 59: D Flip-Flop

## Slide 60: Flip Flop Circuits
Pulse Narrowing Circuit
Explain pulse-narrowing circuit. Attach as front end to D flip flop’s C input.

## Slide 61: Edge-Triggered D Flip Flop

## Slide 62: Manual Reset of D Flip Flop
Generates half clock frequency

## Slide 63: 74LS74A

## Slide 64: Other D flip-flop variations
Negative-edge triggered
Clock enable
We read to FF only when Enable signal is =1
Otherwise the old state of the FF is preserved in a feedback loop. This is an important circuit. The MUX on the input is important in other applications.

## Slide 65: Important
These were asynchronous circuits that are used as parts of synchronous circuits.
Now we will be not concerned with designing asynchronous circuits, although they exist in every synchronous circuit.
We will design on the level of SYNCHRONOUS circuits.

## Slide 66
Simple Applications of Flip-Flops:
Shifters and Counters

## Slide 67: Shifters and Counters
D
Q
c
D
Q
c
D
Q
c
Shifter to right, analyze its behavior
D
Q
c
D
Q
c
D
Q
c
Johnson or Moebius counter, analyze its behavior
Q’
All FFs connected to the same clock
Students should be able to convert the logic diagrams like these to state graphs and state tables

## Slide 68: Shifters that is Cyclical and shifts to right
D
Q
c
D
Q
c
D
Q
c
Shifter to right, analyze its behavior
000
111
100
010
001
110
011
101

## Slide 69: Shifters that takes negated output as input and works as an inexpensive counter.
D
Q
c
D
Q
c
D
Q
c
Johnson or Moebius counter, analyze its behavior
Q’
All connected to the same clock
000
100
110
001
011
111

## Slide 70: State Diagrams for Binary Up Counters
Students should be able to convert the state diagrams like these to finite state machine schemata from flip-flops and logic gates.
Typical Problems.
Build the counter from this state diagram using only T flip-flops.
Build modulo-5 counter from D flip-flops

## Slide 71: Generalized Registers
D
Q
c
D
Q
c
D
Q
1 2 3
0
1 2 3
0
1 2 3
0
Control bits select operation executed in the Generalized Register
Green connection selected by control 00 are shift non-cyclically to right
Blue connections selected by control 01 are shift cyclically to the left
You should be able to add connections for any other operations on this Generalized Register

## Slide 72: Shifters and Counters
D
Q
c
D
Q
c
D
Q
c
Linear Counter, analyze its behavior
D
Q
c
D
Q
c
D
Q
c
General Autonomous FSM with shifts and arbitrary logic function, analyze its behavior
Q’
EXOR gate
Arbitrary logic function
Students should be able to convert the logic diagrams like these to state graphs and state tables
ANALYSIS OF MACHINES IS IMPORTANT AND WILL BE ON EXAM

## Slide 73: Flip-Flops for testing

## Slide 74: SCAN Flip-flops are used for testing
Scan
TEST ENABLE
TEST INPUT

## Slide 75: Scan flip-flops -- for testing
TE = 0 ==> normal operation
TE = 1 ==> test operation
  All of the flip-flops are hooked together in a daisy chain from external test input TI.
  Load up (“scan in”) a test pattern, do one normal operation, shift out (“scan out”) result on TO.

## Slide 76: Other types of Flip-Flops

## Slide 77: JK Flip Flops
J K Q+ Comment
0 0 Q No change
0 1 0 Reset
1 0 1 Set
1 1 Q Toggle

## Slide 78: J-K flip-flops
Not used much anymore
Don’t worry about them
Interesting concept to be used in design

## Slide 79: T Flip Flops
J = K=T Q+ Comment
0 0 0 Q No change
0 1
1 0
1 1 1 Q Toggle
T flip-flop created from JK flip-flop
T flip-flop working from leading slope of clock
T flip-flop working from falling slope of clock

## Slide 80: T flip-flops
Important for counters
When EN=1 it toggles, when EN=0 no change of state
When EN=1 it toggles with leading slope of T, when EN=0 no change of state

## Slide 81: Sequential PALs
16R8
Tri=state

## Slide 82: Analysis of a Counter from JK Flip-Flops

## Slide 83: 4-Bit Binary Up Counter
T flip flops ideal for counters (remain same or toggle)!
A Counter built from JK flip-flops
Question to students:
Find what is the sequence of states of this counter by analyzing the circuit using method shown previously
A
B
C
D

## Slide 84: Counter Timing Diagram
000
000
States of individual flip-flops
What is a period of this counter? What is the binary sequence of states?

## Slide 85: State Machines
State Transition Diagrams
Next State Tables
Mealy and Moore Machines
  Mealy: Output logic uses current state and inputs
  Moore: Output logic uses only current state
One Hot vs. Encoded State Machines

## Slide 86: Iterative Circuits versus State Machines

## Slide 87: REMINDER: Cell Table to design iterative circuits
Cell table: analogous to state table
Example: 0101 pattern detector
    Assuming the same assignment for states (A: 00, B: 01, C: 11, D: 10): each cell same as the combinational logic of the sequential circuit derived for the 0101 sequence detector in future slides for state machine.
Present states
Next states
outputs
Two carry signals denote the state of recognition of our sequence 0101
Sequence 0101 recognized for the first time
Sequence 0101 recognized for the second time
Initial carry
Input sequence of arbitrary length

## Slide 88: Synthesis for Iterative Circuit
Example: synthesize an n-cell iterative network
    Each cell has one cell input xi and one cell output zi
    zi = 1: if and only if either one or two of the cell inputs x1, x2, …, xi have value 1
    States A, B, C, D: 0, 1, 2, (3 or more) of the cell inputs to preceding cells have value 1
    Cell table Cell Output-carries and cell-output table
Encode:
A=00
B=01
C=11
D=10
After encoding the table becomes a KMap
This is like three Kmaps in one. First for Yi1, second for Yi2, third for zi

## Slide 89
X1
X2
X3
X4
Z1
Z2
Z3
Z4
0
0
Observations:
This is a systematic method to design iterative circuits
This method is very similar to designing finite state machines that will covered soon.
Good example are comprators, adders, subtractors, comparators.

## Slide 90: Synthesis for Finite State Machine
yi1 yi2\ xi | 0 | 1
00 | 0 | 0
01 | 0 | 1
11 | 1 | 1
10 | 1 | 1
Yi1
yi1 yi2\ xi | 0 | 1
00 | 0 | 1
01 | 1 | 1
11 | 1 | 0
10 | 0 | 0
Yi2
yi1 yi2\ xi | 0 | 1
00 | 0 | 1
01 | 1 | 1
11 | 1 | 0
10 | 0 | 0
zi
D1 Q1
D2 Q2
These must be D ffs

## Slide 91: Comparison of Iterative Circuit and Finite State Machine
D1 Q1
D2 Q2
X1
X2
X3
X4
Z1
Z2
Z3
Z4
0
0
The internal state in Flip-flops in Finite State Machine corresponds to the value of the carry signal in Iterative Circuit.
Data are given sequentially in FSM and in parallel in Iterative Circuit

## Slide 92: Now we create a feedback through flip-flops, not an iterative circuit as before. Please understand similarity and difference. This is very important, you can expect this on Finals.

## Slide 93: Larger Practical Examples of State Machines

## Slide 94: Example 1: T-bird tail-lights

## Slide 95: ANIMATED: T-bird tail-lights example

## Slide 99: State diagram for lights
Inputs:
LEFT, RIGHT, HAZ
Outputs:
Six lamps
(function of state only)
LC, LB, LA, RC, RB, RA
hazard
Alarm state, all lights
Idle state, no lights
Name of state
Name of input

## Slide 100: Encoded or One-Hot?
Encoded
  8 states
  23 = 8
  Need 3 flip flops
  Need to determine state assignment
One-hot
  Dedicate a flip flop per state
  Need 8 flip flops
First we have decide what kind of encoding we need.
The best method is to start synthesis starting from the state graph like in the last slide

## Slide 101: First Method to calculate outputs for Moore Machine

## Slide 102: Implementation (Encoded, Moore Machine)
Next
State
Logic
Output
Logic
Inputs
Outputs
Current State
Realization of output logic

## Slide 103: Output logic: outputs are functions of only states
LC = L3 + LR3
LB = L2 + L3 + LR3
LA = L1 + L2 + L3 + LR3
RA = R1 + R2 + R3 + LR3
RB = R2 + R3 + LR3
RC = R3 + LR3
This table shows Output signals for internal states
We create equations for outputs, based on the table from the left
Observe that we need only OR gates applied to FFs that encode states
This method is not minimal
Inputs:
LEFT, RIGHT, HAZ
Outputs:
Six lamps
(function of state only)
LC, LB, LA, RC, RB, RA
outputs
states
states
This method can be used for both One –Hot encoding and binary encoding.

## Slide 104: Variant to calculate output functions in which the binary encoding of internal states is used

## Slide 105: Output logic: outputs are functions of only states
LC = L3 + LR3
LB = L2 + L3 + LR3
LA = L1 + L2 + L3 + LR3
RA = R1 + R2 + R3 + LR3
RB = R2 + R3 + LR3
RC = R3 + LR3
LC = Q2’×Q1×Q0’ + Q2×Q1’×Q0’
LB = Q2’×Q1×Q0 + Q2’×Q1×Q0’ + Q2×Q1’×Q0’
LA = Q2’×Q1’×Q0 + Q2’×Q1×Q0 + Q2’×Q1×Q0’ + Q2×Q1’×Q0’
RA = Q2×Q1’×Q0 + Q2×Q1×Q0 + Q2×Q1×Q0’ + Q2×Q1’×Q0’
RB = Q2×Q1×Q0 + Q2×Q1×Q0’ + Q2×Q1’×Q0’
RC = Q2×Q1×Q0’ + Q2×Q1’×Q0’
Q2
Q1
Q0
This table shows Output signals for internal states
This table shows Encoding of internal states
We create equations based on the table from the left
This method is not minimal but does not require Kmaps

## Slide 106: Methods to create transition function

## Slide 107: Two Methods to create the Next State Logic
State transition table for encoded states
Next step depends on implementation choice
  Synthesize or Structural with choice of FFs
Encoding of internal states
This table is created from the state graph AND the encoding of internal states

## Slide 108: Method 1 to create transition function. E This method is easy but not minimal

## Slide 109: Transition Equations for Q2* = D2
Q2* = Q2’× Q1’ × Q0’ × (HAZ + LEFT × RIGHT)
+ Q2’ × Q1’ × Q0’ × (RIGHT × HAZ’ × LEFT’)
+ Q2’ × Q1’ × Q0 × (HAZ)
+ Q2’ × Q1 × Q0 × (HAZ)
+ Q2 × Q1’ × Q0 × (HAZ’)
+ Q2 × Q1’ × Q0 × (HAZ)
+ Q2 × Q1 × Q0 × (HAZ’)
+ Q2 × Q1 × Q0 × (HAZ)
Q2* = Q2’× Q1’ × Q0’ × (HAZ + RIGHT)
+ Q2’ × Q0 × HAZ
+ Q2 × Q0
The simplification of equation for Q2* is done using transformations of equation on the left or using Kmaps.

## Slide 110: Transition Equations for Q1* = D1
Q1* = Q2’ × Q1’ × Q0 × (HAZ’)
+ Q2’ × Q1 × Q0 × (HAZ’)
+ Q2 × Q1’ × Q0 × (HAZ’)
+ Q2 × Q1 × Q0 × (HAZ')
Q1* = Q0 × HAZ’

## Slide 111: Transition Equations for Q0* = D0
Q0* = Q2’ × Q1’ × Q0’ × (LEFT × HAZ’ × RIGHT’)
+ Q2’ × Q1’ × Q0’ × (RIGHT × HAZ’ × LEFT’)
+ Q2’ × Q1’ × Q0 × (HAZ’)
+ Q2 × Q1’ × Q0 × (HAZ’)
Q0* = Q2’× Q1’ × Q0’ × HAZ’ × (LEFT Å RIGHT)
+ Q1’ × Q0 × HAZ’
No guarantee these are minimal. They certainly aren’t SOP. What we do next depends upon how we’re going to implement the FSM.
Could just give them whole thing to ABEL or some other tool and let it generate minimal SOP.
Also, transition equation isn’t same as excitation equation (unless we’re using D FFs)

## Slide 112: Optimizing the speed of my machine

## Slide 113: Implementation (Encoded, Moore Machine)
Next
State
Logic
Output
Logic
Inputs
Outputs
Current State
What should the clock’s period be?

## Slide 114: How Fast Can the Clock Be?
Combinational
Logic
Clock
D1
Q
D2
FF tpd
Combinational tpd
FF tsetup
FF 1
FF 2
You want the signal to propagate as fast as possible through this logic
Propagation delay

## Slide 115: Clock Skew
Clock
D1
Q
D2
FF tpd
Combinational tpd
FF tsetup
Even with careful routing, clock will not arrive
at all FFs at the same time. This skew in clock
arrival time affects max clock rate.
Clock Skew
Clock Periodmin = FF tpd + FF tsetup + C tpd + tskew

## Slide 116
Clock Periodmin = FF tpd + FF tsetup + C tpd + tskew
tclk = tffpd + tcomb + tsetup-time-margin + tsetup
Another notation to explain clock period calculations

## Slide 117: Method 2 when costs of flip-flops are not that important to create transition function

## Slide 118: One-Hot Transitions
IDLE* = IDLE × (HAZ + LEFT + RIGHT)’ + L3 + R3 + LR3
L1* = IDLE × LEFT × HAZ’ × RIGHT’
R1* = IDLE × RIGHT × HAZ’ × LEFT’
L2* = L1 × HAZ’
R2* = R1 × HAZ’
L3* = L2 × HAZ’
R3* = R2 × HAZ’
LR3* = IDLE × (HAZ + LEFT × RIGHT) + (L1 + L2 + R1 + R2) × HAZ
No decoding of state required
Flip-flop L1 has value 1 when machine is in state L1.
Otherwise it has value 0.
This is one-hot coding. Easy and fast.

## Slide 119: Behavioral Verilog
If you understand Boolean Equations and the methods presented above, it is very easy to write Verilog code for every Finite State Machine.
Below I give a template how to create a behavioral specification of any state machine in Verilog.
You should be able to reuse this template, only change the Boolean Equations.

## Slide 120: Better Still – Behavioral Verilog
parameter
IDLE = 8'b00000001,
L1 = 8'b00000010,
L2 = 8'b00000100,
L3 = 8'b00001000,
R1 = 8'b00010000,
R2 = 8'b00100000,
R3 = 8'b01000000,
LR3 = 8'b10000000;
reg [7:0] State, NextState;
case (State)
IDLE:
begin
if (Hazard | Left & Right)
NextState = LR3;
else if (Left)
NextState = L1;
else if (Right)
NextState = R1;
else
NextState = IDLE;
end
L1: begin
if (Hazard)
NextState = LR3;
else
NextState = L2;
end
L2: begin
if (Hazard)
NextState = LR3;
else
NextState = L3;
end
L3: begin
NextState = IDLE;
end
R1: begin
if (Hazard)
NextState = LR3;
else
NextState = R2;
end
R2: begin
if (Hazard)
NextState = LR3;
else
NextState = R3;
end
R3: begin
NextState = IDLE;
end
LR3:begin
NextState = IDLE;
end
endcase
Inputs:
LEFT, RIGHT, HAZARD
Outputs:
Six lamps
(function of state only)
LC, LB, LA, RC, RB, RA
Encoding of outputs

## Slide 121: Better Still – Behavioral Verilog
case (State)
IDLE:
begin
if (Hazard | Left & Right)
NextState = LR3;
else if (Left)
NextState = L1;
else if (Right)
NextState = R1;
else
NextState = IDLE;
end
Inputs:
LEFT, RIGHT, HAZARD
Outputs:
Six lamps
(function of state only)
LC, LB, LA, RC, RB, RA
Left &(Hazard | Left & Right)’ =
Left & (Hazard’ & (Left & Right)’) = Left & Hazard’ (Left’ | Right’) =
Left & Hazard’ & Right’
Here we show how the Verilog Code can be transformed using Boolean Algebra to the state graph.

## Slide 122: Example 2: Traffic Light Controller

## Slide 123: Example: Traffic Light Controller
N
S
E
W
Sensors in road detect approaching car on NS and EW roads, generating input signals NScar and EWcar respectively.
Lights are controlled by outputs NSlite and EWlite.
Traffic lights should change only if there is a car approaching from the other direction.
Otherwise the lights should remain unchanged.
NScar
EWcar
Clock
Traffic Light Controller
NSlite
EWlite
r
sensors
lights
Internal state
Internal state
Output state

## Slide 124: Example: Traffic Light Controller
r
State assignment
NSgreen = 0
EWgreen = 1
=1
= 0
State assignment
Output function
CurrentState’
CurrentState

## Slide 125: Example: Traffic Light Controller. General Method
r
00
01,11
10
00
01
10,11
State\ Inputs | 00 | 01 | 11 | 10
NSgreen | NSgreen | EWgreen | EWgreen | NSgreen
EWgreen | EWgreen | EWgreen | NSgreen | NSgreen
Create directly Gray Code and KMap
ENCODE
Nsgreen = 0
Ewgreen = 1
After encoding you obtain an encoded table, which in general you separate to several KMaps, as shown in several examples before.
You minimize these Kmaps using methods that you know from previous lectures.
Draw the schematic with logic and FFs.

## Slide 126: Example 3: NRZ to Manchester Encoder

## Slide 127: Behavioral Verilog 2
If you understand Boolean Equations and the methods presented above, it is very easy to write Verilog code for every Finite State Machine.
Below I give another template how to create a behavioral specification of any state machine in Verilog.
You should be able to reuse this template, only change the Boolean Equations.

## Slide 128
//
// Moore FSM for serial line conversion: NRZ to Manchester encoding
//
module NRZtoManchester(Clock, Clear, BitIn, BitOut);
input Clock, Clear, BitIn;
output BitOut;
reg BitOut;
// define states using same names and state assignments as state diagram and table
// Using one-hot method, we have one bit per state
parameter
S0 = 4'b0001,
S1 = 4'b0010,
S2 = 4'b0100,
S3 = 4'b1000;
reg [3:0] State, NextState;
// Update state or reset on every - clock edge
always @(negedge Clock)
begin
if (Clear)
begin
State <= S0;
$display("Reset: S0");
end
else
begin
State <= NextState;
$display("State: %d",State);
end
end
Verilog
States and state assignment
Description of sequential part with clearing and next state, this is universal.
Changes with negative slope.
BitIn
Clock
Clear
NRZ to
Manchester
Encoder
BitOut

## Slide 129
// Outputs depend only upon state (Moore machine)
always @(State)
begin
case (State)
S0: BitOut = 1'b0;
S1: BitOut = 1'b0;
S2: BitOut = 1'b1;
S3: BitOut = 1'b1;
endcase
end
// Next state generation logic
always @(State or BitIn)
begin
case (State)
S0: if (BitIn)
NextState = S3;
else
NextState = S1;
S1: if (BitIn)
$display("S1 Error!");
else
NextState = S2;
S2: if (BitIn)
NextState = S3;
else
NextState = S1;
S3: if (BitIn)
NextState = S0;
else
$display("S3 Error!");
endcase
end
endmodule
Output logic for every internal state
Transition logic
S0
0
S1
0
S3
1
S2
1
0
0
0
1
1
1
Rising edge of BitClock coincides with rising edge of FSM clock.
BitIn changes at falling edge of BitClock
Use falling edge of FSM clock for synchronization (will be at midpoint of bit time) so no danger of sampling BitClock while it’s changing

## Slide 130: Method 3 in which we minimize the transition functions optimally
SYNTHESIS OF MACHINES IS IMPORTANT AND WILL BE ON EXAM
SYNTHESIS OF NRZ TO MANCHESTER ENCODER USING KMAPS AND MINIMIZATION

## Slide 131
S0
0
S1
0
S3
1
S2
1
0
0
0
1
1
1
PS | Bin = 0 | Bin = 1
S0 | S1 | S3
S1 | S2 | -
S3 | - | S0
S2 | S1 | S3
00
01
11
10
Pay attention to don’t cares created

## Slide 132: Example 4: Airplane Gear

## Slide 133: Airplane Gear Example
PilotLever
GearIsUp
Airplane Landing Gear Control
Valve
PlaneOnGround
GearIsDown
Pump
RedLED
GreenLED
  PilotLever Operated by pilot to control landing gear (1:down 0:up)
  PlaneOnGround Sensor 1 when plane on ground
  GearIsUp Sensor 1 when landing gear fully up
  GearIsDown Sensor 1 when landing gear fully down
  TimeUp 1 when two second timer expired
  Valve Controls position of valve (1:lowering 0:raising)
  Pump Activates hydraulic pump (1: activate)
  ResetTimer 1 to reset count-down timer, 0 to count
  RedLED Indicates landing gear in motion
  GreenLED Indicates landing gear down
Do not retract landing gear if plane on ground
Plane should be airborne two seconds before retracting gear
TimeUp
ResetTimer
inputs
outputs
Respond to changes in lever position (in case plane started with lever in up position)

## Slide 134: State Transition Diagram
Waiting for TakeOff
Waiting for Timer
Gear Up
Raising Gear
Lowering Gear
~PlaneOnGround
PlaneOnGround
TimeUp & ~PilotLever
GearIsUp
~PilotLever
PilotLever
PlaneOnGround
Reset
State | Reset Timer | Pump | Valve | RedLED | GreenLED
WaitingforTakeoff | 1 | 0 | X | 0 | 1
WaitingforTimer | 0 | 0 | X | 0 | 1
RaisingGear | X | 1 | 0 | 1 | 0
GearUp | X | 0 | X | 0 | 0
LoweringGear | X | 1 | 1 | 1 | 0
GearDown | X | 0 | X | 0 | 1
Gear Down
~PilotLever
GearIsDown
PilotLever
Output functions

## Slide 135: Airplane Landing Gear Example
Lever
GearUp
Airplane Landing Gear Control
Valve
OnGround
GearDown
Pump
RedLED
GreenLED
  Lever Operated by pilot to control landing gear (0:down 1:up)
  OnGround Sensor 1 when plane on ground
  GearUp Sensor 1 when landing gear fully up
  GearDown Sensor 1 when landing gear fully down
  Valve Controls position of valve (0:lowering 1:raising)
  Pump Activates hydraulic pump
  RedLED Indicates landing gear in motion
  GreenLED Indicates landing gear down
Do not retract landing gear if plane on ground
Plane should be airborne two seconds before retracting gear

## Slide 136: What students can do with this example ?
You can complete this example using any of the several method shown above.
I suggest first to use Method 2 based on One-Hot Encoding.
Next use Method 3.
Next describe the problem using Verilog.

## Slide 137: Example 5: Design Using JK Flip-flops

## Slide 138: DESIGN EXAMPLE 6: Counter using JK
Design Procedure:
Specification  State Diagram  State Table 
Excitation Table  Karnaugh Map  Circuit Diagram
Example: 2-bit Counter -> 2 FF's
current next
state input state FF inputs
A B x A B Ja Ka Jb Kb
0 0 0 0 0 0 d 0 d
0 0 1 0 1 0 d 1 d
0 1 0 0 1 0 d d 0
0 1 1 1 0 1 d d 1
1 0 0 1 0 d 0 0 d
1 0 1 1 1 d 0 1 d
1 1 0 1 1 d 0 d 0
1 1 1 0 0 d 1 d 1
A
B
x
Ja
1
d d
d d
x
A
B
Ka
d d
d d
1
Kb
A
B
x
1
1
d
d
d
d
Ja = Bx Ka = Bx Jb = x Kb = x
clock
00
01
10
11
x=0
x=1
x=0
x=1
x=0
x=1
x=0
x=1
J Q
C
K Q'
J Q
C
K Q'
x
A
A
B
x
1 d
1 d
d
d
Jb
B
Encoded internal state

## Slide 139: Example 7: Registers, Shifters, Generalized Registers
Bidirectional Shift Register with Parallel Load
D
Q
C
D
Q
C
D
Q
C
D
Q
C
A0
A1
A2
A3
Clock
I0
I1
I2
I3
Shift Register, non-cyclic, shifts to right
D Q
C
D Q
C
D Q
C
D Q
C
Serial
Input
Clock
Serial
Output
D
Q
C
D
Q
C
D
Q
C
D
Q
C
A0
A1
A2
A3
4 x 1
MUX
4 x 1
MUX
4 x 1
MUX
4 x 1
MUX
Clock
S0S1
SeriaI
Input
I0
I1
I2
I3
Serial
Input
Register
This is example of “Generalized Register”
control
Students please analyze this circuit and understand what it does.

## Slide 140: Example 8: Counter modulo 16 with JK flip-flops that act as T flip-flops
J K
Q
J K
Q
J K
Q
J K
Q
Clock
Counter
Enable
A0
A1
A2
A3
Output
Carry

## Slide 141: Example 9: Vending Machine
Taken from Katz & Borriello, “Contemporary Logic Design”

## Slide 142: Example: vending machine
Vending Machine FSM
N
D
Reset
Clock
Open
Coin Sensor
Release Mechanism
Release item after 15 cents are deposited
Single coin slot for dimes, nickels
No change
nickel
dime

## Slide 143: Example: vending machine. Create a tree
Suitable abstract representation
  tabulate typical input sequences:
    3 nickels
    nickel, dime
    dime, nickel
    two dimes
  draw state diagram:
    inputs: N, D, reset
    output: open chute
  assumptions:
    assume N and D asserted for one cycle
    each state has a self loop for N = D = 0 (no coin)
S0
Reset
S2
D
S6
[open]
D
S4
[open]
D
S1
N
S3
N
S5
[open]
N
S8
[open]
D
S7
[open]
N

## Slide 144: Example: vending machine. Minimize machine to minimum number of states
Minimize number of states - reuse states whenever possible
symbolic state table
present inputs next output state D N state open 0¢ 0 0 0¢ 0 0 1 5¢ 0 1 0 10¢ 0 1 1 – – 5¢ 0 0 5¢ 0 0 1 10¢ 0 1 0 15¢ 0 1 1 – – 10¢ 0 0 10¢ 0 0 1 15¢ 0 1 0 15¢ 0 1 1 – – 15¢ – – 15¢ 1
0¢
Reset
5¢
N
N
N + D
10¢
D
15¢
[open]
D

## Slide 145: Example: vending machine: Encoding (or state assignment) of internal states
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 0 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 0 1 0 1 1 0 1 1 – – – 1 1 – – 1 1 1
Uniquely encode states

## Slide 146: Example: Moore implementation
D1 = Q1 + D + Q0 N
D0 = Q0’ N + Q0 N’ + Q1 N + Q1 D
OPEN = Q1 Q0
Mapping to logic
0 0 1 1
0 1 1 1
X X 1 X
1 1 1 1
Q1
D1
Q0
N
D
0 1 1 0
1 0 1 1
X X 1 X
0 1 1 1
Q1
D0
Q0
N
D
0 0 1 0
0 0 1 0
X X 1 X
0 0 1 0
Q1
Open
Q0
N
D
Remember location of don’t cares!

## Slide 147: Example: vending machine – One Hot Encoding
present state inputs next state output Q3 Q2 Q1 Q0 D N D3 D2 D1 D0 open 0 0 0 1 0 0 0 0 0 1 0 0 1 0 0 1 0 0 1 0 0 1 0 0 0 1 1 - - - - - 0 0 1 0 0 0 0 0 1 0 0 0 1 0 1 0 0 0 1 0 1 0 0 0 0 1 1 - - - - - 0 1 0 0 0 0 0 1 0 0 0 0 1 1 0 0 0 0 1 0 1 0 0 0 0 1 1 - - - - - 1 0 0 0 - - 1 0 0 0 1
D0 = Q0 D’ N’
D1 = Q0 N + Q1 D’ N’
D2 = Q0 D + Q1 N + Q2 D’ N’
D3 = Q1 D + Q2 D + Q2 N + Q3
OPEN = Q3
One-hot encoding

## Slide 148: Various procedures for Moore sequential circuits
Use Method 3 to calculate transition functions
State Graph of FSM
Algorithmic State Machine
Natural Language Specification of FSM
Verilog Code
State Table of FSM
Logic Equations
Red is most important
Use Method 2 to calculate transition functions, calculate output functions
Use Method 1 to calculate transition functions, calculate output functions
Use other Methods to calculate transition functions, calculate output functions

## Slide 149: Short Presentation of Mealy Machines

## Slide 150: Comparison of Mealy and Moore state diagrams
Moore machine
  outputs associated with state
0¢
[0]
10¢
[0]
5¢
[0]
15¢
[1]
N’ D’ + Reset
D
D
N
N+D
N
N’ D’
Reset’
N’ D’
N’ D’
Reset
0¢
10¢
5¢
15¢
(N’ D’ + Reset)/0
D/0
D/1
N/0
N+D/1
N/0
N’ D’/0
Reset’/1
N’ D’/0
N’ D’/0
Reset/0
Mealy machine
  outputs associated with transitions

## Slide 151: Example 10: Mealy implementation
0¢
10¢
5¢
15¢
Reset/0
D/0
D/1
N/0
N+D/1
N/0
N’ D’/0
Reset’/1
N’ D’/0
N’ D’/0
Reset/0
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 1 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 1 1 0 1 1 1 1 1 – – – 1 1 – – 1 1 1
D0 = Q0’N + Q0N’ + Q1N + Q1D
D1 = Q1 + D + Q0N
OPEN = Q1Q0 + Q1N + Q1D + Q0D
0 0 1 0
0 0 1 1
X X 1 X
0 1 1 1
Q1
Open
Q0
N
D

## Slide 152: Example 10: Mealy implementation (cont)
D0 = Q0’N + Q0N’ + Q1N + Q1D
D1 = Q1 + D + Q0N
OPEN = Q1Q0 + Q1N + Q1D + Q0D make sure OPEN is 0 when reset – by adding AND gate
When Reset is 1 then Reset’ is zero
Then Open is zero

## Slide 153: Types of FSMs
state feedback
inputs
outputs
reg
combinational logic for next state
logic for outputs
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs
Moore
Mealy
Synchronous Mealy
Mealy not on exams! ENJOY!

## Slide 154: Example 11: Synchronous Mealy

## Slide 155: Retiming
D
D
Q
Q
D
D
Q
Q
D1
D2
D1
D2
D
Q
We are shifting AND gate back through flip-flops and adding one delay after it, to preserve timing of this gate.
One FF Delay + one AND delay
One FF Delay + one AND delay

## Slide 156: Using Retiming to realize Synchronous Mealy

## Slide 157: Mealy to synchronous Mealy
OPEN.d = Q1Q0 + Q1N + Q1D + Q0D
OPEN.d = (Q1 + D + Q0N)(Q0'N + Q0N' + Q1N + Q1D) = Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D
0 0 1 0
0 0 1 1
1 0 1 1
0 1 1 1
Q1
Open.d
Q0
N
D
0 0 1 0
0 0 1 1
X X 1 X
0 1 1 1
Q1
Open.d
Q0
N
D
D0 = Q0’N + Q0N’ + Q1N + Q1D
D1 = Q1 + D + Q0N
OPEN = Q1Q0 + Q1N + Q1D + Q0D make sure OPEN is 0 when reset – by adding AND gate
Our previous Mealy Solution
D0 *D1
Known as don’t cares
From Mealy
I asked earlier to remember location of don’t cares

## Slide 158: Moore to synchronous Mealy
OPEN = Q1Q0 creates a combinational delay after Q1 and Q0 change in Moore implementation
This can be corrected by retiming, i.e., move flip-flops and logic through each other to improve delay
OPEN.d = (Q1 + D + Q0N)(Q0'N + Q0N' + Q1N + Q1D) = Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D
Implementation now looks like a synchronous Mealy machine
  it is common for programmable devices to have FF at end of logic
D1 = Q1 + D + Q0 N
D0 = Q0’ N + Q0 N’ + Q1 N + Q1 D
OPEN = Q1 Q0
This was our Moore Solution

## Slide 159: Questions and EXAM Problems (1)
Explain in your own words how the SR latch from two NOR gates works.
Explain in full detail timing of SR latch.
Create a latch from two NAND gates, similar to one from two NOR gates and explain in detail its timing.
Draw the table of this latch from NAND gates.
What are critical races? Give example of a circuit.
What are non-critical races? Give example of a circuit.
What are metastable states?
You must be able to derive a state machine table from the circuit of a latch.
You must be able to derive a state machine table from a state machine graph.
You must be able to derive a state machine table from a flowchart or Algorithmic State Machine.
Explain how a simple generator works.
Explain behavior of gated SR latch using NOR gates.
Explain behavior of gated SR latch using NAND gates.
Explain behavior of gated D latch using NOR gates.
Explain behavior of gated D latch using NAND gates.

## Slide 160: Questions and Problems
16. Explain in your own words how the Edge Triggered D Flip-Flop works.
17. Build a T flip-flop from D flip-flop and logic gates.
18. Build a JK flip-flop from D flip-flop and logic gates.
19. Build a T flip-flop from JK flip-flop.
20. Build a JK flip-flop from T flip-flop and logic gates.
21. Build a modulo 4 counter from D flip-flops and logic.
22. Build a modulo 4 counter from T flip-flops and logic.
23. Build a modulo 4 counter from JK flip-flops and logic.
24. Design a modulo 5 counter and draw its timing diagram.
25. How to design a modulo 32 counter?
26. How to design a modulo 33 counter?
27. Explain in your own words the difference of Mealy and Moore Machines.
28. What is the synchronous Mealy Machine and how it differs from standard Mealy Machine? 29. What is retiming?
Questions and EXAM Problems (2)

## Slide 161: Questions and Problems
29. Given is a circuit composed from D flip-flops and few logic gates. Create a state graph of this circuit.
30. Given is a circuit composed from D flip-flops and few logic gates. Create a state table of this circuit.
31. TYPICAL PROBLEM FOR EXAM, DEFINITELY WILL BE COVERED:
Given is an English Language formulation of some state machine.
  Create a state graph of this machine.
  Create a state table of this machine. (Moore).
  Create and minimize output logic functions of this machine.
  Create and minimize transition (excitation) functions of this machine.
  Draw the schematic of the machine with flip-flops and logic gates.
  Verify that your schematic really realizes the machine that its specification was given to you.
Most Important EXAM Problems
VERILOG NOT ON EXAM

## Slide 162: Sources
Prof. Mark G. Faust
John Wakerly
Gaetano Borriello
Randy H. Katz